#### UNITED

# NATIONS

Distr.

# GENERAL

# ST/SG/AC.10/C.3/2004/90

2 September 2004

ORIGINAL: ENGLISH

COMMITTEE OF EXPERTS ON THE TRANSPORT OF

# DANGEROUS GOODS AND ON THE GLOBALLY

# HARMONIZED SYSTEM OF CLASSIFICATION

# AND LABELLING OF CHEMICALS

# Sub-Committee of Experts on the

# Transport of Dangerous Goods

# Twenty-sixth session, 29 November-3 December 2004

# Item 3 (b) of the provisional agenda

OUTSTANDING ISSUES OR PROPOSALS OF AMENDMENTS TO THE RECOMMENDATIONS

ON THE TRANSPORT OF DANGEROUS GOODS

Self-reactive substances

New formulation for the list in 2.4.2.3.2.3

Transmitted by the expert from Japan

A new formulation for self-reactive substances as mentioned hereunder meets the criteria of UN 3228, type E. The Data Sheet and the Test Report are attached hereto as annexes 1 and 2 respectively. Approval for maritime transport of the products has already been granted by Japanese Ministry of Land, Infrastructure and Transport.

The products have been transported from Japan to the United States of America and China for some years without any incident or accident.

It is proposed to add the formulation for self-reactive substances in the list in 2.4.2.3.2.3 in order to allow transport in the appropriate conditions.

Proposal

Add the following formulation in the list of currently assigned self-reactive substances in 2.4.2.3.2.3:

Self-reactive Substance:	ACETONE-PYROGALLOL COPOLYMER

1,2-NAPHTHOQUINONEDIAZIDO-5-SULPHONATE

Concentration(%) : 	100

Packing Method : 	OP8

Control Temperature :  	None

Emergency Temperature :  	None

UN Generic entry : 	3228

Remarks :	None

## Annex 1 (ENGLISH ONLY)

DATA SHEET TO BE SUBMITTED TO THE UNITED NATIONS

FOR NEW OR AMENDED CLASSIFICATION OF SUBSTANCES

Submitted by	Japan	Date 	May  25, 2004

Supply all relevant information including sources of basic classification data. Data should relate to the product in the form to be transported. State test methods. Answer all questions - if necessary state "not known" or "not applicable" - If data is not available in the form requested, provide what is available with details. Delete inappropriate words.

Section 1. SUBSTANCE IDENTITY

1.1	Chemical name	Acetone-pyrogallol copolymer 1,2-Naphthoquinonediazido-5-sulphonate

1.2	Chemical formula 	C24H21N3O6S1

1.3	Other names/synonyms	 Acetone-pyrogallol copolymer 2-Diazo-1-naphthol-5-sulphonate

UN number  UN3228

CAS number  68584-99-6

1.5	Proposed classification for the Recommendations

1.5.1    proper shipping name (3.1.2)  Self-reactive solid type E

1.5.2    class/division 4.1	subsidiary risk(s)   None

packing group II

1.5.3    proposed special provisions, if any  274

1.5.4    proposed packing instruction(s)   P520

Section 2. PHYSICAL PROPERTIES

2.1	Melting point or range>290 °C

2.2	Boiling point or range	not applicable

2.3	Relative density at :

2.3.1    15 °C	600kg/m3

2.3.2    20 °C	600kg/m3

2.3.3    50 °C	600kg/m3

2.4	Vapour pressure at :

2.4.1    50 °C	not applicable

2.4.2    65 °C	not applicable

2.5	Viscosity at 20 °C 	not applicable

2.6	Solubility in water at 20 °C	not soluble

2.7	Physical state at 20°C (2.2.1.11)	solid/liquid/gas2

2.8	Appearance at normal transport temperatures, including colour and odour

Yellow powder , odourless

2.9	Other relevant physical properties

Section 3. FLAMMABILITY

3.1	Flammable vapour

3.1.1	Flash point (2.3.31) 	not applicable

3.1.2	Is combustion sustained? (2.3.1.31) yes/no

3.2	Autoignition temperature 	not known

3.3	Flammability range (LEL/UEL)	not known

3.4	Is the substance a flammable solid? (2.4.21) yes/no

3.4.1	If yes, give details

Section 4. CHEMICAL PROPERTIES

4.1	Does the substance require inhibition/stabilization or other treatment such as nitrogen blanket to prevent hazardous reactivity ?	yes/no

If yes, state:

4.1.1	Inhibitor/stabilizer used

4.1.2	Alternative method

4.1.3	Time effective at 55 °C

4.1.4	Conditions rendering it ineffective

4.2	Is the substance an explosive according to paragraph 2.1.1.1? (2.11)  yes/no

4.2.1 If yes, give details

4.3	Is the substance a desensitized explosive? (2.4.2.41)	yes/no

4.3.1 If yes, give details

4.4	Is the substance a self-reactive substance? (2.4.11)	yes/no

If yes, state:

4.4.1	exit box of flow chart    Exit E

What is the self-accelerating decomposition temperature (SADT) for a 50 kg package?65°C

Is the temperature control required? (2.4.2.3.41)	yes/no

4.4.2	proposed control temperature for a 50 kg package	°C

4.4.3	proposed emergency temperature for a 50 kg package	°C

4.5	Is the substance pyrophoric? (2.4.31) 	yes/no

4.5.1 If yes, give details

4.6	Is the substance liable to self-heating? (2.4.31) 	yes/no

4.6.1 If yes, give details

4.7	Is the substance an organic peroxide (2.5.11) 	yes/no

If yes state:

4.7.1 exit box of flow chart

What is the self accelerating decomposition temperature (SADT) for a 50 kg package? 65 °C

Is temperature control required? (2.5.3.4.11) 	yes/no

4.7.2	proposed control temperature for a 50 kg package	°C

4.7.3	proposed emergency temperature for a 50 kg package	°C

4.8	Does the substance in contact with water emit flammable gases? (2.4.41) 	yes/no

4.8.1 If yes, give details

4.9	Does the substance have oxidizing properties (2.5.11)	yes/no

4.9.1 If yes, give details

4.10	Corrosivity (2.81) to:	Not corrosive

4.10.1 mild steel 	mm/year 	 	at 	°C

4.10.2 aluminium	mm/year  	at	°C

4.10.3 other packaging materials (specify)

mm/year   at	°C

mm/year   at	°C

4.11	Other relevant chemical properties

Section 5. HARMFUL BIOLOGICAL EFFECTS

5.1	LD50, oral (2.6.2.1.11)     19400	mg/kg	Animal species  rat

5.2	LD50, dermal (2.6.2.1.21)	mg/kg	Animal species

5.3	LC50, inhalation (2.6.2.1.31)		mg/litre	Exposure time	 hours

or		ml/m3	Animal species

5.4	Saturated vapour concentration at 20 °C (2.6.2.2.4.31)	not applicable

5.5	Skin exposure (2.81) results	Exposure time   	24  hours

Animal species	rabbits

5.6	Other data

5.7	Human experience

Section 6. SUPPLEMENTARY INFORMATION

6.1	Recommended emergency action

6.1.1    Fire (include suitable and unsuitable extinguishing agents)

Use Dry chemical, CO2 as extinguish media

6.1.2    Spillage

Eliminate all ignition sources. Do not touch or walk through spilled material by naked hands. Take up with spilled material using clean non-sparking tools and place into loosely covered plastic containers for later disposal. Prevent entry into floor drains, storm sewer, waterways or confined areas.

6.2	Is it proposed to transport the substance in:

6.2.1   Bulk Containers (6.81)		yes/no

6.2.2   Intermediate Bulk Containers (6.51)?	yes/no

6.2.3   Portable tanks (6.71)?			yes/no

If yes, give details in Sections 7, 8 and/or 9.

Section 7. BULK CONTAINERS (only complete if yes in 6.2.1)

7.1	Proposed type(s)

Section 8. INTERMEDIATE BULK CONTAINERS (IBCs) (only complete if yes in 6.2.2)

8.1	Proposed type(s)

Section 9. MULTIMODAL TANK TRANSPORT (only complete if yes in 6.2.3)

9.1	Description of proposed tank (including IMO tank type if known)

9.2	Minimum test pressure

9.3	Minimum shell thickness

9.4	Details of bottom openings, if any

9.5	Pressure relief arrangements

9.6	Degree of filling

9.7	Unsuitable construction materials

Annex 2 (ENGLISH ONLY)

TEST REPORT

1.	Name of the Self-reactive solid: 	ACETONE-PYROGALLOL COPOLYMER

1,2-NAPHTHOQUINONEDIAZIDO-5-SULPHONATE

2.	General data

2.1	Composition	: 100%

2.2	Molecular formula	: C24H21N2O6S1

2.3	Physical form	: Solid

2.4	Colour	: Yellow

2.5	Density	: 600kg/m3

2.6	Particle diameter	: None

3.	Detonation (test series A)

Box 1 of the flow chart	: Does it propagate a detonation?

3.1	Method	: BAM 50/60 steel tube test (test A.1)

3.2	Sample conditions	: Temperature 26 °C, Humidity 70%

3.3	Observations	: Fragmented part of the tube: 11.6 cm

3.4	Result	: No

3.5	Exit	: 1.3

4. 	Deflagration (test series C)

Box 5 of the flow chart	: Can it propagate a deflagration?

4.1	Method 1	: Time/pressure test (test C.1)

4.2	Sample conditions	: Temperature 18 °C, Humidity 76%

4.3	Observations 	: No pressure rise to 300psi

4.4	Result 	: No

4.5	Method 2 	: Deflagration test (test C.2)

4.6	Sample conditions	: Temperature 16 °C , Humidity 74%

4.7	Observations	: Deflagration rate 0.15 mm/s

4.8	Result  	: No

4.9	Final result 	: No

4.10	Exit 	: 5.3

5.	Heating under confinement (test series E)

Box 9 of the flow chart	: What is the effect of heating it under defined confinement?

5.1	Method 1	: Koenen test (test E.1)

5.2	Sample conditions	: Temperature 20 °C, Humidity 91% , Mass 13.9 g

5.3	Observations 	: Limiting diameter  less than 1.0 mm

5.4	Result	: Low

5.5	Method 2	: Dutch pressure vessel test (test E.2)

5.6	Sample conditions 	: Temperature 18 °C, Humidity 89% , Mass 50 g

5.7	Observations	: Limiting diameter less than 1.0 mm

5.8	Result	: No

5.9	Final result 	: No

5.10	Exit	: 9.4

6.	Thermal stability (outside of the flow chart: test series H)

6.1	Method	: Heat accumulation storage test (test H.4)

6.2	Sample conditions	: Dewar vessel

(Diameter 60mm, Height  180mm , Mass 500 cc)

6.3	Observations	: at 60 °C no exothermal reaction

at 65°C self-promotion decomposition,

SADT 65 °C

6.4	Result	: Control temperature is not required

7. 	General remarks 	: The classification scheme is given in Fig.1

8.	Proposed assignment

8.1	Proper shipping name	: SELF-REACTIVE SOLID TYPE E

8.2	UN number	: 3228

8.3	Division 	: 4.1

8.4	Technical name	: ACETONE-PYROGALLOL COPOLYMER

1,2-NAPHTHOQUINONEDIAZIDO-5-SULPHONATE

8.5	Concentration	: 100%

8.6	Subsidiary risks	: None

8.7	Packing group 	: II

8.8	Packing Method	: OP8

8.9 	Control temperature 	: None

8.10	Emergency temperature	: None

* * * *

Figure 1: FLOW CHART SCHEME FOR SELF-REACTIVE SUBSTANCES

Figure1: FLOW CHART SCHEME FOR SELF-REACTIVE SUBSTANCES (cont'd)

# Footnotes

This and similar references are to chapters and paragraphs in the Model Regulations on the Transport of Dangerous Goods.

See definition of "liquid" in 1.2.1 of the Model Regulations on the Transport of Dangerous Goods.

1 	This and similar references are to chapters and paragraphs in the Model Regulations on the Transport of Dangerous Goods.

1 	This and similar references are to chapters and paragraphs in the Model Regulations on the Transport of Dangerous Goods.

1	This and similar references are to chapters and paragraphs in the Model Regulations on the Transport of Dangerous Goods.

1 	This and similar references are to chapters and paragraphs in the Model Regulations on the Transport of Dangerous Goods.

# Text boxes

STSTE

Secretariat

go to box 11

Exit A

Exit B

Exit C

Exit D

NOT ACCEPTED

FOR TRANSPORT

IN THAT

PACKAGING

1.1 Yes

Box 1

1.2 Partial

1.3 No

Does it propagate

a detonation

?

5.1

Yes, rapidly

Box 5

5.2 Yes, slowly

5.3 No

6.1 Yes

Box 6

6.2 No

7.2 Medium

7.3 Low

7.4 No

Box 7

7.1

Violent

9.2

Medium

Box 9

9.1

Violent

9.3 Low

9.4 No

10.1 Yes

Box 10

10.2 No

Can it

explode as packaged

for transport

?

4.1

Yes, rapidly

Box 4

4.2 Yes, slowly

4.3 No

Box 3

3.2 Yes, slowly

3.3 No

3.1

Yes, rapidly

Box 8

8.1

Violent

2.1 Yes

Box 2

2.2 No

Can it

detonate as packaged

for transport

?

Can it propagate

a deflagration

?

Does it

deflagrate rapidly

in package

?

8.2 Medium

8.3 Low

8.4 No

ACCEPTED FOR

TRANSPORT

IN PACKAGES OF

NOT MORE THAN 25 KG

NET MASS

WITH 'EXPLOSIVE '

SUBSIDIARY RISK LABEL

Can it propagate

a deflagration

?

Can it propagate

a deflagration

?

What is the effect

of heating it under defined

confinement

?

ACCEPTED FOR

TRANSPORT

IN PACKAGES OF NOT

MORE THAN 50 KG

NET MASS

ACCEPTED FOR

TRANSPORT

IN PACKAGES OF NOT

MORE THAN 50 KG

NET MASS

SELF-REACTIVE SUBSTANCE

What is the effect

of heating it under defined

confinement

?

What is the effect

of heating it under defined

confinement

?

from box 9

Exit F

Exit G

Is the

self-reactive substance

to be considered for transport

in IBCs or tanks, or

for exemption

?

11.1 Yes

11.2 No

12.1 Not low

12.2 Low

12.3 None

13.1 Low

13.2 None

Box 11

Box 13

Box 12

Exit E

SHALL BE CONSIDERED

FOR EXEMPTION

ACCEPTED FOR TRANSPORT

IN PACKAGES OF NOT MORE THAN

400 KG/450 LITRES

MAY BE CONSIDERED

FOR TRANSPORT

IN IBCs OR TANKS

What is its

explosive power

?

What is the effect

of heating it under defined

confinement

?