# UN/SCETDG/25/INF.11

COMMITTEE OF EXPERTS ON THE TRANSPORT OF

DANGEROUS GOODS AND ON THE GLOBALLY

HARMONIZED SYSTEM OF CLASSIFICATION

AND LABELLING OF CHEMICALS

Sub-Committee of Experts on the

Transport of Dangerous Goods

Twenty-fifth session

Geneva, 5-14 July 2004

Item 4 (c) of the provisional agenda

PACKAGING

Miscellaneous proposals

### The packaging instruction of DICHLOROISOCYANURIC ACID SALTS

Transmitted by the expert from the People’s Republic of China

Background

The packaging of DICHLOROISOCYANURIC ACID SALTS (UN No. 2465) is IBCS. Its packaging instruction is IBC08 and the special packing provision is B4. Specific packing provision B4 require that Flexible, fibreboard or wooden IBCS shall be sift-proof and water resistant or shall be fitted with a sift-proof and water resistant liner. For flexible IBCS (13H and 13L), There is no stipulations in chapter 6.5 about which types of the IBCS are water resistant. Clause 6.1.4.15.3 water resistant Bag 5L3 and 6.1.4.16.4 water resistant Bag 5H3 in the orange book stipulate in (a), (b), (c) that (a) Separate inner liners of water resistant paper (e.g. waxed kraft paper, tarred paper or plastics–coated kraft paper); or (b) Plastics film bonded to the inner surface of the bag; or (c) One or more inner liners made of plastics material. It can be comprehended from these above that water resistant flexible IBCS contains 13L2, 13L3, 13L4, 13H2, 13H3, 13H4, 13H5 and 13M2. But this is not suitable. First, the packaging instruction P002 for DICHLOROISOCYANURIC ACID SALTS stipulates the “Bag (5H3, 5H4, 5L3, 5M2)”. All these types of packaging are stated clearly as water resistant in Chapter 6.1. Although 5H2, 5L2 have coating or liner, they are not definitely water resistant. Second, in August 2002 at Chinese Qingdao port, the flexible IBCS (woven plastic) 13H2 containing DICHLOROISOCYANURIC ACID SALTS met with sudden heavy rain. The container intake water and exploded several hours later.

Because DICHLOROISOCYANURIC ACID SALTS is a strong oxidant, it reacts strongly when meeting with water and has the danger of catching fire or explosion. If is very important for its packaging to be water resistant. It is not defined dearly about the concept of water resistant flexible IBCS in Chapter 6.5, and the packaging instruction IBC08 does not specify the types of water resistant flexible IBCS. For these reasons, we propose to modify the packaging instruction of IBCS for DICHLOROISOCYANURIC ACID SALTS to specify the types of flexible IBCS for DICHLOROISOCYANURIC ACID SALTS in 4.1.4.2 Special Packing Provision in order to avoid the misunderstanding about water resistant flexible IBCS.

## Proposal 1

Modification of Special Packing Provision stipulations B3 in 4.1.4.2:

Former B3: Flexible IBCS shall be sift–proof and water resistant or shall be fitted with a sift–proof and water resistant liner.

Modified B3: Flexible IBCS shall be sift–proof and water resistant or shall be fitted with a sift–proof and water resistant liner (13H4,13H5,13L4 or 13M2).

## Proposal 2

Add B3 in “Special Provisions of Packaging and IBCS” of UN No.2465 in the DANGEROUS GOODS LIST.