# UN/SCETDG/25/INF.49

COMMITTEE OF EXPERTS ON THE TRANSPORT OF

DANGEROUS GOODS AND ON THE GLOBALLY

HARMONIZED SYSTEM OF CLASSIFICATION

AND LABELLING OF CHEMICALS

Sub-Committee of Experts on the

Transport of Dangerous Goods

Twenty-fifth session

Geneva, 5-14 July 2004

Item 4 (c) of the provisional agenda

##### PACKAGINGS

Miscellaneous proposals

Packaging of pressure receptacles

## Transmitted by the International Air Transport Association (IATA)

# Background

1.	Sections 4.1.6.1.8(e) and 4.1.6.1.9(a) of the UN Model Regulations identify that pressure receptacles and non-refillable pressure receptacles respectively be transported in “an outer packaging”.

2.	The use of the term “outer packaging” in this context is a misnomer as an “outer packaging” is defined in Section 1.2.1 as:

“the outer protection of a composite or combination packaging together with any absorbent materials, cushioning and any other components necessary to contain and protect inner receptacles or inner packagings.”

3.	By using the term “outer packaging” it implies that the pressure receptacle is an inner packaging.  But, the pressure receptacle may be shipped as a completed packaging provided that the requirements of 4.1.6.1.8(a), (b), (c) or (d) are met.

4.	Additionally, the pressure receptacles themselves shall be marked as required by 6.2.2.7 and 6.2.2.8 for UN pressure receptacles and for non-UN pressure receptacles as required by the competent authority in the country of use.  If the marking on the pressure receptacle is no longer visible then the “outer packaging” specified in 4.1.6.1.8(e) and 4.1.6.1.9(a) should be treated as an overpack and the requirements of 5.1.2.1 applied

##### Proposal

It is proposed that 4.1.6.1.7, 4.1.6.1.8(e) and 4.1.6.1.9(a) be amended as follows:

4.1.6.1.7 	Pressure receptacles, including their closures, shall conform to the design, construction, inspection and testing requirements detailed in Chapter 6.2. When outer packagings an overpack is are prescribed, the pressure receptacles shall be firmly secured therein. Unless otherwise specified in the detailed packing instructions, one or more inner packagings pressure receptacles may be enclosed in an outer packagingoverpack.

4.1.6.1.8 	Valves shall be designed and constructed in such a way that they are inherently able to withstand damage without release of the contents or shall be protected from damage which could cause inadvertent release of the contents of the pressure receptacle, by one of the following methods:

(a) 	Valves are placed inside the neck of the pressure receptacle and protected by a threaded plug or cap;

(b) 	Valves are protected by caps. Caps shall possess vent-holes of sufficient cross-sectional area to evacuate the gas if leakage occurs at the valves;

(c) 	Valves are protected by shrouds or guards;

(d) 	Pressure receptacles are transported in frames, (e.g. bundles); or

(e) 	Pressure receptacles are transported in an outer packagingoverpack. The packagingoverpack as prepared for transport shall be capable of meeting the drop test specified in 6.1.5.3 at the packing group I performance level.

For pressure receptacles with valves as described in (b) and (c), the requirements of ISO 11117:1998 shall be met; for valves with inherent protection, the requirements of annex B of ISO 10297:1999 shall be met.

4.1.6.1.9 	Non-refillable pressure receptacles shall:

(a)	be transported in an outer packagingoverpack, such as a box, or crate, or in shrink-wrapped trays or stretch- wrapped trays;

It is also proposed that the definition of “Overpack” in 1.2.1 be amended as follows:

Overpack means an enclosure used by a single consignor to contain one or more packages and to form one unit for protection or convenience of handling and stowage during transport. Examples of overpacks are a number of packages either:

(a) 	Placed or stacked on to a load board such as a pallet and secured by strapping, shrink wrapping, stretch wrapping, or other suitable means; or

(b) 	Placed in a protective outer packaging such as a box or crate for protection;

______________