# UN/SCETDG/25/INF.87

COMMITTEE OF EXPERTS ON THE TRANSPORT OF

DANGEROUS GOODS AND ON THE GLOBALLY

HARMONIZED SYSTEM OF CLASSIFICATION

AND LABELLING OF CHEMICALS

Sub-Committee of Experts on the

Transport of Dangerous Goods

Twenty-fifth session

Geneva, 5-14 July 2004

Item 7 of the provisional agenda

Revision of document ST/SG/AC.10/C.3/2004/54

# MISCELLANEOUS PROPOSALS (Chapters 4.1, 6.1, 6.3, 6.5 and 6.6)

Provisions concerning transport operations by all modes of transport

Revision of Part 7.1.1 Application and general provisions,

Addition of loading and stacking provisions

Transmitted by the expert from the United Kingdom

Introduction

- The expert of the United Kingdom welcomed the efforts of the expert of Australia in document ST/SG/AC.10/C.3/2003/56 to address problems associated with the loading and stacking of IBCs in transport units by proposing text for Part 7 of the Model Regulations, but suggested that the Sub-Committee should take the opportunity to apply a more generic approach to such issues rather than restricting the proposal to IBCs.

In INF.38 submitted at the twenty-fourth session,  the expert from the United Kingdom proposed to include new text in Chapter 7.1 without seriously disrupting the existing layout and numbering. The Sub-Committee made a number of helpful comments and asked the expert from the United Kingdom to submit a formal proposal at the next session.

3.   Since submitting paper 2004/54 a number of helpful suggestions to improve the text have been received. This revised proposal has taken account of many of those suggestions and now makes clear that proposed text only addresses the transport of packaged dangerous goods and unpackaged articles. 'Loading' in the context of transport in portable tanks or bulk containers is properly addressed in other relevant sections of the Model Regulations.  Changes to the original text of 2004/54 are highlighted in this Rev.1.

# Proposal

In the following proposal existing UN text is in normal case and new text is shown in italics.

Replace existing 7.1.1 with the following:

    - Application, general provisions and loading requirements for packaged dangerous goods

      - This Chapter contains provisions applicable to dangerous goods transport operations by all modes of transport.

      - Packaged dangerous goods shall not be offered for transportunless;

- the goods have been properly classified, packaged, marked and labelled and described and certified on a dangerous goods transport document, and

are in a fit condition for transport as required by these Regulations, and no dangerous residue of the dangerous goods adheres to the outside of the package.

Packaged dangerous goods shall not be accepted for transport unless;

- transport units have been approprietly marked, labelled and placarded; and

- transport units are otherwise in a condition for transport as required by these Regulations.

      - 7.1.1.3        Packages containing dangerous goods shall only be loaded in transport units that are strong enough to withstand the shocks and loadings normally encountered during transport, having regard to the conditions to be expected during the anticipated journey. The transport unit shall be constructed in such a way as to prevent the loss of contents during normal conditions of transport, or by changes in temperature, humidity or pressure. Where appropriate the transport unit shall be fitted with devices to facilitate securing and handling of the dangerous goods.

      - The interior and exterior of a transport unit shall be inspected prior to loading to ensure that there is no damage that could affect its integrity or that of the packages to be loaded in it.

      - Transport units shall be loaded so that incompatible dangerous or other goods are segregated in accordance with this Chapter. Specific loading instructions such as orientation arrows, not to be double stacked, keep dry or temperature control requirements shall be met. Liquid dangerous goods should be loaded below dry dangerous goods whenever possible.

      - Packages containing dangerous goods and unpackaged articles shall be secured by suitable means capable of restraining the goods (such as fastening straps, sliding slatboards, adjustable brackets etc) in the transport unit in a manner that will prevent any movement during transport which would change the orientation of the packages or cause them to be damaged. Movement of packages may also be prevented by filling any voids by the use of dunnage or by blocking and bracing. Where restraints such as banding or straps are used, these shall not be over-tightened to cause damage or deformation of the package.

      - Packages shall not be stacked unless designed for that purpose. Where different design types of packages that have been designed for stacking are to be loaded together, they shall not be stacked with each other unless this can be done without causing damge to the packages. Where necessary, stacked packages shall be prevented from damaging the package below by the use of load-bearing devices.

      - During loading and unloading, packages containing dangerous goods shall be protected from being damaged. Particular attention shall be paid to the handling of packages during their preparation for transport, the type of transport unit on which they are to be carried and to the method of loading or unloading, so that accidental damage is not caused through dragging or mishandling the packages. Packages that appear to be leaking or damaged so that the contents may escape shall not be accepted for transport. If a package is found to be damaged so that the contents leak, the damaged package shall not be transported but moved to a safe place in accordance with instructions given by a competent authority, enforcement personnel or a designated responsible person who is familiar with the dangerous goods, the risks involved and the measures that should be taken in an emergency.

NOTE 1:	Additional operational requirements for the transport of packages and IBCs are provided in the special packing provisions for packages and IBCs  (see Chapter 4.1).

NOTE 2:	Additional guidance on the packing of transport units can be found in the IMO/ILO/UNECE Guidelines for Packing Cargo Transport Units (CTUs) contained in the supplement to the International Maritime Dangerous Goods Code. Modal and National Codes of Practice (such as the Agreement governing the exchange and use of Wagons between Railway Undertakings (RIV 200) Appendix II loading guidelines published by the International Union of Railways (UIC)) or the UK DfT Code of Practice on Safety of Loads on Vehicles) may also be available.

_______________