# UN/SCETDG/26/INF.45

COMMITTEE OF EXPERTS ON THE TRANSPORT OF

DANGEROUS GOODS AND ON THE GLOBALLY

HARMONIZED SYSTEM OF CLASSIFICATION

AND LABELLING OF CHEMICALS

Sub-Committee of Experts on the

Transport of Dangerous Goods

Twenty-sixth session

Geneva, 29 November-7 December 2004

Item 3(b) of the agenda

EXPLOSIVES, SELF-REACTIVE SUBSTANCES AND ORGANIC PEROXIDES

Classification criteria for fireworks

Transmitted by the expert from the United Kingdom

## Introduction

At the last meeting of the working group the UK expert said that he would carry out tests on report compositions made from black powder/aluminium powder mixtures following a query from a UK firework importer about Note 2 to the default fireworks table (ST/SG/AC.10/C.3/2004/102).

Results were obtained from 6g samples of 3 types of black powder, a perchlorate/aluminium mixture, a barium nitrate/aluminium mixture and 3 different black powder/aluminium report mixtures. The results showed that black powder/aluminium powder (92:8) produced overpressure values similar to that produced by the barium nitrate/aluminium mixtures

Proposal

The UK expert proposes that Note 2 to the default firework list be amended to include black powder/metal powder fuel mixtures and suggests the following change to the Note:

”Note 2: “Flash compositions” in this table refers to pyrotechnic compositions containing an oxidising substance, or black powder, and a metal powder fuel that are used to produce an aural report effect or used as a bursting charge in firework devices”

Note: The test results of these pyrotechnic compositions can be obtained from the UK expert.

_____________