# UN/SCETDG/26/INF.53

COMMITTEE OF EXPERTS ON THE TRANSPORT OF

DANGEROUS GOODS AND ON THE GLOBALLY

HARMONIZED SYSTEM OF CLASSIFICATION

AND LABELLING OF CHEMICALS

Sub-Committee of Experts on the

Transport of Dangerous Goods

TEXTS ADOPTED BY THE SUB-COMMITTEE AT ITS TWENTY-THIRD, TWENTY-FOURTH AND TWENTY-FIFTH SESSIONS AND RELATED PROPOSALS

Transport of aerosols for disposal

Outcome of the Lunchtime Working Group on 30-11-04

Amended entry for UN 1950 in table 3.2 :

| 1950 | AEROSOLS | 2 |  |  | 63 190 277 XXX | See SP 277 | P003 LP02 | PP17 PP87 L2 |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

Proposed changes:

(a) 	Add a new special provision XXX in chapter 3.3, which should also be listed in column (6) of chapter 3.2 against UN 1950:

"[327] 	waste aerosols consigned in accordance with 5.4.1.4.3.c) may be transported under this entry for the purpose of reprocessing or disposal. They need not be protected against inadvertent discharge provided measures to prevent dangerous build up of pressure and dangerous atmospheres are addressed. Waste aerosols, other than those leaking or severely deformed, shall be packed in accordance with packing instructions P003 and special provision PP87, or packing instruction LP02 and special packing provision L2. Leaking or severely deformed aerosols shall be transported in salvage packagings provided appropriate measures are taken to ensure there is no dangerous build up of pressure.

[Waste aerosols shall not be transported in multimodal freight containers.]"

(b)	Add a new 4.1.1.17.3

"Appropriate measures shall be taken to ensure there is no dangerous build up of pressure."

(c)	LP02 and L2 should be listed in columns (8) and (9) against UN 1950

(d)	P003, PP87, the first sentence should be amended to read:

"For UN 1950 waste aerosols transported in accordance with special provision XXX the packagings shall have a means of retaining any free liquid that might escape during transport e.g. absorbent material.”

(e)	LP02, L2, should be amended to read:

"For UN 1950 aerosols the large packagings shall meet the Packing Group III performance level. Large packagings for waste aerosols transported in accordance with special provision [327] shall have in addition a means of retaining any free liquid that might escape during transport e.g. absorbent material.”

(f)	"7.1.4 	Special provisions applicable to the carriage of gases

7.1.4.1 	Aerosols transported for the purposes of reprocessing or disposal under the provisions of special provision [327] shall only be carried in well-ventilated transport units [other than multimodal freight containers]."

_____________