| UNITED NATIONS | E |
| --- | --- |

|  | Economic and Social Council | Distr. GENERAL TRANS/WP.29/2004/7 10 December 2003 Original: ENGLISH |
| --- | --- | --- |

###### ECONOMIC COMMISSION FOR EUROPE

# INLAND TRANSPORT COMMITTEE

# World Forum for Harmonization of Vehicle Regulations (WP.29)

(One-hundred-and-thirty-second session, 9-12 March 2004,
 agenda item 4.2.14.)

PROPOSAL FOR DRAFT SUPPLEMENT 5 TO REGULATION No. 98

(Headlamps with gas-discharge light sources)

Transmitted by the Working Party on Lighting and Light-Signalling (GRE)

Note:	The text reproduced below was adopted by GRE at its fifty-first session, and is transmitted for consideration to WP.29 and to AC.1.  It is based on document TRANS/WP.29/GRE/2003/37, as amended (TRANS/WP.29/GRE/51, para. 41).

__________

This document is a working document circulated for discussion and comments. The use of this document for other purposes is the entire responsibility of the user. Documents are also available via the INTERNET: http://www.unece.org/trans/main/welcwp29.htm

Paragraph 6.2.5., amend to read:

"6.2.5.	Only one gas-discharge light source is permitted for each passing beam headlamp.  A maximum of two additional light sources are permitted as follows:

6.2.5.1.	One additional light source inside the passing beam headlamp according to Regulation No. 37 may be used to contribute to bend lighting.

6.2.5.2.	One additional light source according to Regulation No. 37, inside the passing beam headlamp, may be used for the purposes of generating infrared radiation.  It shall only be activated at the same time as the gas-discharge light source.  In the event that the gas-discharge light source fails, this additional light source shall be automatically switched off.

The test voltage for the measurement with this additional light source shall be the same as in paragraph 6.2.5.4.

6.2.5.3.	In the event of failure of an additional light source, the headlamp shall continue to fulfil the requirements of the passing beam."

Paragraph 6.2.5.1. (former), renumber as paragraph 6.2.5.4.

Paragraph 6.2.7., amend to read:

"6.2.7.	The requirements in paragraph 6.2.6. above shall also apply to headlamps designed to provide bend lighting and/or that include the additional light source referred to in paragraph 6.2.5.2.

      - If bend lighting is obtained by;"

Paragraphs 6.2.7.1. to 6.2.7.3. (former), renumber as paragraphs 6.2.7.1.1. to 6.2.7.1.3.

_____________