Informal document No.  GRE-52-7

(52nd GRE, 8-9 March 2004,

agenda item 2.2.)

PROPOSAL FOR DRAFT AMENDMENTS TO REGULATION No. 48

(Installation of lighting and light-signalling devices)

Transmitted by the expert from Canada

Text of the document is following the UK informal document No. GRE-52-6 regarding projection of white light towards the rear of the vehicle.

*    *    *

Paragraphs 5.10. to 5.10.2., amend to read:

"5.10.	Visibility of red light to the front of a vehicle and of white light to the rear of a vehicle

Note: No account shall be taken of lighting devices fitted for the interior lighting of a vehicle.

5.10.1.	For the visibility of red light towards the front of a vehicle, with the exception of a red rearmost side-marker lamp, there must be no direct visibility of the apparent surface of a lamp capable of projecting or reflecting red light if viewed by an observer moving within Zone 1 as specified in annex 4.

5.10.2.	For the visibility of white light towards the rear of a vehicle, with the exception of a reversing lamp, cornering lamp and direction indicator lamp, there must be no direct visibility of the apparent surface of a lamp capable of projecting or reflecting white light if viewed by an observer moving within Zone 2 as specified in annex 4."

______________________