|  | Informal document No. GRE-52-17 (52nd GRE, 30 March – 2 April 2004, agenda item 19.1.) |
| --- | --- |

PROPOSAL FOR DRAFT AMENDMENTS TO REGULATION NO. 50

(Position, stop and direction indicator lamps for motorcycles)

(transmitted by the expert from IMMA)

A. PROPOSAL

Paragraph 7.4.1., delete of the footnote 3/:

Paragraph 7.4.1.1., delete of the footnote 3/:

Paragraph 7.4.1.2., delete of the footnote 3/:

Paragraph 7.4.1.3., delete of the footnote 3/:

footnote 3/, delete

Insert a new paragraph 7.11, 7.11.1. and 7.11.2, to read:

"7.11	Maximum values of front direction indicator lamps

"7.11.1	For devices of categories 11 and 11a, the intensity of the the light emitted outside the zone defined by the measuring points +/- 10 degrees H and +/- 10 degrees V (10 degrees-field) shall not exceed the following values:

| Direction indicator of category | Maximum values in cd outside the 10 degrees-field |
| --- | --- |
|  | Single lamp | Single lamp containing more than one light source |
| 11 | 400 | 560 |
| 11a | 400 | 560 |

Between the boundaries of the 10 degrees-field (+/- 10 degrees H and +/- 10 degrees V) and the 5 degrees-field (+/- 5 degrees H and +/- 5 degrees V), the maximum admissible values of the intensities are linearly increased up to the values as defined in paragraph 7.4.1 and 7.4.1.1.;

"7.11.2	For devices of categories 11b and 11c, the intensity of the the light emitted outside the zone defined by the measuring points +/- 15 degrees H and +/- 15 degrees V (15 degrees-field) shall not exceed the following values:

| Direction indicator of category | Maximum values in cd outside the 15 degrees-field |
| --- | --- |
|  | Single lamp | Single lamp containing more than one light source |
| 11b | 250 | 350 |
| 11c | 400 | 560 |

Between the boundaries of the 15 degrees-field (+/- 15 degrees H and +/- 15 degrees V) and the 5 degrees-field (+/- 5 degrees H and +/- 5 degrees V), the maximum values are increased linearly up to the values as defined in paragraph 7.4.1.2 and 7.4.1.3.

B. Justification

In the ECE Regulation No. 50-00 Supplement 4, new categories 11a, 11b and 11c for the front direction indicator lamps have been provided.  This new categories are basically in accordance with the ECE Regulation No. 6 (Direction indicator lamps for 4 wheel vehicles), except for the maximum intensities and their zones.  Actually the maximum intensity of 400 cd outside the zone defined by the +/- 5 degrees H and +/- 10, as shown in the Footnote 3 in ECE Regulation No. 50, is not the same as the ECE Regulation No. 6, which makes some problems.  For example, in Category 11c both the minimum value of 360 cd and the maximum value of 400 cd are applied on H-5L and H-5R.  The range is only 40 cd, and practically it is very difficult to meet such a narrow range of the photometric values.

So, we propose the amendment of the ECE Regulation No. 50, so that the maximum values and their zones are correctly harmonized with ECE Regulation No. 6 and the above problem is resolved.

Category of the front direction indicator

| R50-00 S3 | Regulation No. 50-00 S4 |
| --- | --- |
| Category11 | Category 11: distance between passing beam and direction indicator- 75mm or more |
|  | Category 11a: distance between passing beam and direction indicator- 40mm or more |
|  | Category 11b: distance between passing beam and direction indicator- 20mm or more |
|  | Category 11c: distance between passing beam and direction indicator- less than 20mm |

Photometric requirement of the front direction indicator

| Category | H-V point Min. intensity (cd) | Max. intensity(cd) |
| --- | --- | --- |
|  |  | 1 light source *2 |
| 11 | 90 *1 | 700 *3 |
| 11a | 175 *1 | 700 *3 |
| 11b | 250 *1 | 800 *3 |
| 11c | 400 *1 | 860 *3 |

*1  luminous intensity distribution table for the minimum intensity

*2  In case of a single lamp containing more than one light source, the maximum intensity is given by multiplying by 1.4 the value prescribed for a single lamp.

*3  However, the intensity of the light emitted outside the zone defined by the +/- 5 degrees H and +/- 10 degrees V shall not exceed 400 cd

Maximum and Minimum intensity on the H-H line specified in Regulation No. 50-00 S4

[Category 11]                                 [Category 11c]

Proposal

- Category 11, 11a

(1) delete of the maximum intensity of 400cd to outside of the zone defined by the +/- 5 degrees H and +/- 10 degrees V

(2) provide the new maximum intensity requirement to the outside the zone defined by the +/- 10 degree H and +/- 10 degree V (10 degrees-field).

(3) Between the boundaries of the 10 degrees-field and the 5 degrees-field (+/- 5 degrees H and +/- 5 degrees V), the maximum values are increased linearly up to the 700cd.

- Category 11b, 11c

(1) delete of the maximum intensity of 400cd to outside of the zone defined by the +/- 5 degrees H and +/- 10 degrees V

(2) provide the new maximum intensity requirement to the outside the zone defined by the +/- 15 degree H and +/- 15 degree V (15 degrees-field).

(3) Between the boundaries of the 15 degrees-field and the 5 degrees-field (+/- 5 degrees H and +/- 5 degrees V), the maximum values are increased linearly up to the 800cd(category 11b) or 860cd(category 11c).

| Category | H-V point Min. intensity (cd) | Max. intensity(cd) |
| --- | --- | --- |
|  |  | Area | 1 light source |
| 11 | 90 *1 | inward of H=+/-5 deg, V=+/-5 deg | 700 |
|  |  | outward of H=+/-10 deg, V=+/-10 deg | 400 |
| 11a | 175 *1 | inward of H=+/-5 deg, V=+/-5 deg | 700 |
|  |  | outward of H=+/-10 deg, V=+/-10 deg | 400 |
| 11b | 250 *1 | inward of H=+/-5 deg, V=+/-5 deg | 800 |
|  |  | outward of H=+/-15 deg, V=+/-15 deg | 250 |
| 11c | 400 *1 | inward of H=+/-5 deg, V=+/-5 deg | 860 |
|  |  | outward of H=+/-15 deg, V=+/-15 deg | 400 |

Current ECE Regulation No. 50;

Proposal for ECE Regulation No. 50 amendment;

ECE Regulation No. 6-01;

# Text boxes

11a(=1)

11b(=1a)

11c(=1b)

31.5

157.5

175

87.5

140

225

360

250

Category 11a

(= R6 : Category 1)

Category 11b

(= R6 : Category 1a)

61.25

81

90

140

31.5

157.5

250

400

225

360

175

Category 11a

Category 11b

Category 11c

700

400

800

400

400

87.5

860

H

5°

10°

15°

15°

10°

5°

(cd)

Practically very difficult to meet such a narrow range between the Min. & Max.  photometric values.

(cd)

H

5°

10°

10°

5°

860

400

400

360

Max

Min

40cd

(cd)

H

5°

10°

10°

5°

700

400

90

81

Max

Min

319cd

Category 11c

(= R6 : Category 1b)

700

250

250

800

400

400

400

860

H

5°

10°

15°

15°

10°

5°

(cd)

Category 11

90

81

61.25

Max. Intensity

Min. Intensity

Min. Intensity

Max. Intensity

Min. Intensity

Max. Intensity

1

1a

1b

61.25

157.5

175

87.5

140

225

360

250

Category 1

Category 1a

Category 1b

700

250

250

800

400

400

400

860

H

5°

10°

15°

15°

10°

5°

11

11

11a

11b

11c

400

Category 11