| UNITED NATIONS | E |
| --- | --- |

|  | Economic and Social Council | Distr. GENERAL TRANS/WP.29/GRRF/2004/2 21 November 2003 ENGLISH Original: ENGLISH ENGLISH AND FRENCH ONLY |
| --- | --- | --- |

###### ECONOMIC COMMISSION FOR EUROPE

# INLAND TRANSPORT COMMITTEE

# World Forum for Harmonization of Vehicle Regulations (WP.29)

Working Party on Brakes and Running Gear (GRRF)

(Fifty-fifth session, 3-6 February 2004,

agenda item 6.4.)

## PROPOSAL FOR DRAFT CORRIGENDUM 1 TO SUPPLEMENT 15

## TO THE ORIGINAL VERSION OF REGULATION No. 54

(Pneumatic tyres for commercial vehicles)

# Transmitted by the expert from the European Tyre and Rim Technical Organization (ETRTO)

Note:  The text reproduced below was prepared by the expert from ETRTO.  It is based on the text of a document (informal document No. 15) distributed without a symbol at the fifty-fourth session (TRANS/WP.29/GRRF/54, para. 37).

_______________

_______________

Note: This document is distributed to the Experts on Brakes and Running Gear only.

- PROPOSAL

Paragraph 3.1.15., correct to read:

"3.1.15.	The inscription "FRT" (Free Rolling Tyre) in case of tyres designed for the equipment of trailer axles and axles of motor vehicles other than front steering and drive axles."

*      *     *

B.	JUSTIFICATION

Clarify the text for better understanding of the definition and provide coherency with current practice.

________________