| UNITED NATIONS | E |
| --- | --- |

|  | Economic and Social Council | Distr. GENERAL TRANS/WP.29/GRRF/2004/3 21 November 2003 ENGLISH Original: ENGLISH ENGLISH AND FRENCH ONLY |
| --- | --- | --- |

###### ECONOMIC COMMISSION FOR EUROPE

# INLAND TRANSPORT COMMITTEE

# World Forum for Harmonization of Vehicle Regulations (WP.29)

Working Party on Brakes and Running Gear (GRRF)

(Fifty-fifth session, 3-6 February 2004,

agenda item 6.7.)

## PROPOSAL FOR DRAFT AMENDMENTS TO REGULATION No. 109

(Retreaded pneumatic tyres for commercial vehicles)

# Transmitted by the expert from France

Note:  The text reproduced below was prepared by the expert from France.  It is based on the text of a document (informal document No. 17) distributed without a symbol at the fifty-fourth session (TRANS/WP.29/GRRF/54, para. 42).

_______________

_______________

Note: This document is distributed to the Experts on Brakes and Running Gear only.

- PROPOSAL

Paragraph 7.1.4.2., amend to read:

"7.1.4.2.	It may exceed the value by 4 per cent in the case of radial-ply tyres and 8 per cent in the case of diagonal (bias-ply) tyres.  However, for tyres with nominal section width exceeding 305 mm intended for dual mounting (twinning), the value determined pursuant to paragraph 7.1.1 above shall not be exceeded by more than 2 per cent for radial-ply tyres with nominal aspect ratio higher than 60 or 4 per cent for diagonal (bias-ply) tyres ."

*     *     *

B.	JUSTIFICATION

The proposed amendment intends to harmonize Regulation No. 109, para. 7.1.4.2. with para.6.1.4.2 of Regulation No. 54, as modified by Amendment 2.  In the existing versions the overall width of a tyre 315/60 R 22.5 cannot exceed the value calculated by the formula S=S1+K(A-A1) by 4% in Regulation No. 54 and by 2% in Regulation No. 109.

(For a new tyre 315/60 R 22.5 the maximal acceptable width is 326 mm and for a retreaded tyre the maximal width cannot exceed 319 mm.

______________