| UNITED NATIONS | E |
| --- | --- |

|  | Economic and Social Council | Distr. GENERAL TRANS/WP.29/GRRF/2004/5 21 November 2003 ENGLISH Original: ENGLISH ENGLISH AND FRENCH ONLY |
| --- | --- | --- |

###### ECONOMIC COMMISSION FOR EUROPE

# INLAND TRANSPORT COMMITTEE

# World Forum for Harmonization of Vehicle Regulations (WP.29)

Working Party on Brakes and Running Gear (GRRF)

(Fifty-fifth session, 3-6 February 2004,

agenda item 1.2.)

## PROPOSAL FOR DRAFT CORRIGENDUM 2 TO SUPPLEMENT 8

## TO THE 09 SERIES OF AMENDMENTS TO REGULATION No. 13

(Braking)

# Transmitted by the expert from the United Kingdom

Note:  The text reproduced below has been prepared by the expert from the United Kingdom.  It is a proposal to introduce the marking of maximum wear limit or the inclusion of wear indicators on brake discs and drums, following the decision of GRRF taken at its fifty-fourth session (TRANS/WP.29/GRRF/54, para. 13).

_______________

_______________

Note: This document is distributed to the Experts on Brakes and Running Gear only.

- PROPOSAL

Paragraphs 5.2.1.11.2.2. to 5.2.1.11.2.2.2, amend to read:

"5.2.1.11.2.2.	Assessment of the wear condition of the friction surfaces of brake discs or drums may only be performed by direct measurement of the actual component or examination of wear indicators, which may necessitate some level of disassembly.

5.2.1.11.2.2.1.	At the time of manufacture the manufacturer shall either:

- Permanently mark a disc with the minimum thickness or a drum with the maximum diameter, permissible before replacement is necessary. This should be on a part of the component not subject to deterioration due to corrosion, or

- Permanently mark both friction surfaces of a disc or the friction surface of a drum with a wear indicator.	This may be in the form of an indentation, a groove or other appropriate method.

5.2.1.11.2.2.2.	At the time of type approval, the vehicle manufacturer shall define the following:

- The method by which wear of the friction surfaces of drums and discs may be assessed, including the level of disassembly required and the tools and process required to achieve this.

- Information defining the maximum acceptable wear limit at the point at which replacement becomes necessary.

This information shall be made freely available e.g. vehicle handbook or electronic data record."

*     *     *

B.	JUSTIFICATION

At the fifty-third session of GRRF, revised provisions for periodic technical inspection were adopted and transmitted to WP.29 for agreement. These were reproduced in the meeting report, annex 2 to document TRANS/WP.29/53. The agreed revised wording to the text requires the vehicle manufacturer at the time of type approval to define how the friction surfaces of discs and drums shall be assessed for serviceability and what the maximum wear limits are which make replacement necessary.

This proposal goes one stage further to demand that the manufacturer (either the disc/drum manufacturer or the vehicle manufacturer) shall mark the component with the minimum thickness, in

the case of a disc, or maximum diameter, in the case of a drum.  This will ensure that the correct information is readily available to any person dismantling the vehicle for repair or maintenance.  The component must be permanently marked on a surface that is not subject to deterioration due to the elements.  This can be achieved by marking on the disc "bell" or wheel mounting face.  As an alternative the components may be manufactured to include wear indicators.  These may take the form of indentations or grooves in the friction surfaces of the components.  At the time of type approval the vehicle manufacturer would identify which method had been used.

It was confirmed at the fifty-fourth session of GRRF that many disc and drum manufacturers already mark components that are supplied to the aftermarket with these dimensions and that components supplied for vehicle production could be similarly marked.

This amendment is proposed as a corrigendum to Supplement 8 to the 09 series of amendments so that the requirements will come into force at the same time as the main PTI requirements for which transitional provisions have also been agreed.

________________