| UNITED NATIONS | E |
| --- | --- |

|  | Economic and Social Council | Distr. GENERAL TRANS/WP.29/GRRF/2004/21 7 July 2004 ENGLISH Original: ENGLISH ENGLISH AND FRENCH ONLY |
| --- | --- | --- |

###### ECONOMIC COMMISSION FOR EUROPE

# INLAND TRANSPORT COMMITTEE

# World Forum for Harmonization of Vehicle Regulations (WP.29)

Working Party on Brakes and Running Gear (GRRF)

(Fifty-sixth session, 20-22 September 2004,

agenda item 6.2.)

PROPOSAL FOR DRAFT AMENDMENTS TO REGULATION No. 30

(Pneumatic tyres)

###### Transmitted on behalf of the GRRF informal group on tyre wet grip

Note:	The text reproduced below has been prepared by the experts from the GRRF informal group on tyre wet grip to continue discussion on the introduction of a protocol for the testing of tyres to include wet grip requirements.

This document should be read in conjunction with the proposals contained within TRANS/WP.29/GRRF/2004/9.

_____________

_______________

Note: This document is distributed to the Experts on Brakes and Running Gear only.

A. 	PROPOSAL

Insert a new paragraph 2.38., to read:

"2.38.	"Coupling (Hitch) height" means the height when measured perpendicularly 	from the centre of the articulation point of the trailer towing coupling or hitch to the ground, when the towing vehicle and trailer are coupled together.  The vehicle and trailer must be standing on level pavement surface in its test 	mode complete with the appropriate tyre(s) to be used in the particular test."

### Annex 8,

Paragraph 1.1., amend to read:

"1.1.	Track Characteristics

The track shall have a dense asphalt surface with a gradient in any direction not exceeding 2 per cent.  It shall be of uniform age, composition, and wear and shall be free of loose material or foreign deposits.  The chipping size shall be between 8 – 13 mm and the sand depth measured as specified in ASTM E-965 shall be 0.7 +/- 0.3 mm.

The surface friction value for the wetted track shall be established by one or 	other of the following methods:"

Paragraph 2.1.1.4., amend to read:

"2.1.1.4.	……….maximum angle of 5º.  The longitudinal distance from the centre line of the articulation point of the coupling (hitch) to the transverse centre line of the axle of the trailer shall be at least ten times the coupling (hitch) height."

*      *      *

B.	JUSTIFICATION

These proposals are the results following the last meeting held in Brussels on 26 May 2004 of the GRRF tyre wet grip ad-hoc group which seek to clarify some minor points of detail in the track characteristics and the test trailer.

____________