| UNITED NATIONS | E |
| --- | --- |

|  | Economic and Social Council | Distr. GENERAL TRANS/WP.29/GRRF/2004/22 7 July 2004 ENGLISH Original: ENGLISH ENGLISH AND FRENCH ONLY |
| --- | --- | --- |

###### ECONOMIC COMMISSION FOR EUROPE

# INLAND TRANSPORT COMMITTEE

# World Forum for Harmonization of Vehicle Regulations (WP.29)

Working Party on Brakes and Running Gear (GRRF)

(Fifty-sixth session, 20-22 September 2004,

agenda item 1.2.)

## PROPOSAL FOR DRAFT SUPPLEMENT 3

## TO THE ORIGINAL VERSION OF REGULATION No. 13-H

(Harmonized braking)

# Transmitted by the expert from the United Kingdom

Note:  The text reproduced below has been prepared by the expert from the United Kingdom to clarify Periodical Technical Inspections (P.T.I.) and to introduce the marking of maximum wear limit or the inclusion of wear indicators on brake discs and drums.

_______________

_______________

Note: This document is distributed to the Experts on Brakes and Running Gear only.

- PROPOSAL

Insert new paragraphs 5.1.4. and 5.1.4.1., to read:

"5.1.4.	Provisions for the periodic technical inspection of braking systems

5.1.4.1. 	It shall be possible to assess the wear condition of the components of the service brake that are subject to wear e.g. friction linings and drums/discs (in the case of drums or discs, wear assessment may not necessarily be carried out at the time of periodic technical inspection).  The method by which this may be realized is defined in paragraph 5.2.11.2. of this Regulation."

Paragraph 5.2.11.2., amend to read:

"5.2.11.2.	Checking the wear of the service brake friction components"

Insert new paragraphs 5.2.11.2.1. to 5.2.11.2.2.2., to read:

"5.2.11.2.1.	It shall be possible to easily check this wear on service brake linings from the outside or underside of the vehicle, without the removal of the wheels, by the provision of appropriate inspection holes or by some other means.  This may be achieved by utilizing standard workshop tools or common inspection equipment e.g. mirror, endoscope, etc.  Alternatively, acoustic or optical devices warning the driver at his driving position when lining replacement is necessary are acceptable.  The yellow warning signal specified in paragraph 5.2.21.1.2. below may be used as the optical warning signal.

        - Assessment of the wear condition of the friction surfaces of brake discs or drums may only be performed by direct measurement of the actual component or examination of wear indicators, which may necessitate some level of disassembly.

5.2.11.2.2.1.	At the time of manufacture, the manufacturer shall either:

- Mark the disc with the value of the minimum thickness or the drum with the value of the maximum diameter, permissible before replacement is necessary.  This should be on a part of the component least likely to deterioration due to corrosion, or

- Permanently mark both friction surfaces of the disc or the friction surface of the drum with a wear indicator.  This may be in the form of an indentation, a groove or other appropriate method.

5.2.11.2.2.2.	At the time of type approval, the vehicle manufacturer shall define the following:

- The method by which wear of the friction surfaces of drums and discs may be assessed, including the level of disassembly required and the tools and process required to achieve this.

- Information defining the maximum acceptable wear limit at the point at which replacement becomes necessary.

This information shall be made available free, e.g. vehicle handbook or electronic data record."

Insert new paragraphs 12. to 12.1.2.1., to read:

"12. 			TRANSITIONAL PROVISIONS

12.1.	General

12.1.1.	As from the official date of entry into force of Supplement 3 to the original version of the Regulation, no Contracting Party applying this Regulation shall refuse to grant approval under this Regulation as amended by Supplement 3.

12.1.2.	New type approvals

12.1.2.1.	As from 24 months after the official date of entry into force of Supplement 3, Contracting Parties applying this Regulation shall grant ECE approvals only if the vehicle type to be approved meets the requirements of this Regulation as amended by Supplement 3."

*     *     *

- JUSTIFICATION

At the fifty-third session of GRRF, revised provisions for periodic technical inspection were adopted for Regulation No. 13.  This amendment transposes the appropriate requirements to Regulation No. 13- H.

It was confirmed, at the fifty-fourth session of GRRF, that many disc and drum manufacturers already mark components that are supplied to the aftermarket with these dimensions and that components supplied for vehicle production could be similarly marked.

At the fifty-fifth session of GRRF, the delegate of the United Kingdom was asked to amend document TRANS/WP.29/GRRF/2004/6 to take into consideration grammatical points raised by the Indian delegation and concern expressed by CLEPA regarding the "permanent" marking of discs and drums. This revised document has addressed these points.

In addition, the wording of paragraph 5.2.11.2.1. has been amended to reflect the intention of the PTI ad hoc working group.  The intention was that wheels should not be removed from the vehicle for the purpose of technical inspection and that it is permissible to use standard workshop tools and common inspection equipment to aid the examination.

However, the wording agreed and adopted for Regulation No. 13 as part of Supplement 8 to the 09 series of amendments does not reflect this intention.  It is the understanding of some inspection authorities that they can use devices such as "endoscopes" to aid inspection since this was the intention of the working group.  This is not the case as the regulations clearly state "tools or equipment normally supplied with the vehicle".  Also the wording "the removal of front and/or rear wheels is permitted for this purpose on category M1 and N1 vehicles only" has now been deleted.  It is the correct interpretation of the regulation by some Approval Authorities that now it is permitted to remove the wheels from any category of vehicle if the vehicle is supplied with a jack and wheel brace as there is nothing in the Regulation to say that it is prohibited.  The original wording limited the removal of wheels to category M1 and N1 vehicles, which was not the intention of the ad hoc working group.

Transitional provisions have been included.

______________