| UNITED NATIONS | E |
| --- | --- |

|  | Economic and Social Council | Distr. GENERAL TRANS/WP.29/GRRF/2004/28 9 July 2004 ENGLISH Original: ENGLISH ENGLISH AND FRENCH ONLY |
| --- | --- | --- |

###### ECONOMIC COMMISSION FOR EUROPE

# INLAND TRANSPORT COMMITTEE

# World Forum for Harmonization of Vehicle Regulations (WP.29)

Working Party on Brakes and Running Gear (GRRF)

(Fifty-sixth session, 20-22 September 2004,

agenda item 1.1.)

## PROPOSAL FOR DRAFT AMENDMENTS TO REGULATION No. 13-H

(Harmonized braking)

# Transmitted by the expert from the International Organization of

# Motor Vehicle Manufacturers (OICA)

Note:  The text reproduced below was transmitted by the expert from the OICA in order to amend the scope of Regulation No. 13-H by including N1 category of vehicles at the request of the manufacturer.

_______________

_______________

Note: This document is distributed to the Experts on Brakes and Running Gear only.

A.		PROPOSAL

Paragraph 1.1., amend to read:

"1.1.	This Regulation applies to the braking of vehicles of Category M1, and at the manufacturer's request may be used to approve N1 vehicles as defined in annex 7 to the Consolidated Resolution on the Construction of Vehicles (R.E.3). 1/"

*          *          *

B.	JUSTIFICATION

Along with the proposal in document TRANS/WP29/GRRF/2004/12 to remove M1 vehicles from Regulation No. 13, leaving this category of vehicle to be covered by Regulation No. 13-H, it is proposed to permit that certain vehicles of category N1, at the manufacturer's request, could be approved under Regulation No. 13-H.

In the case of car-derived vans, which have a braking system as in the M1 parent, allowing the approval to take place to Regulation No. 13-H, means that no separate type approval application to Regulation No. 13 has to be made.

The N1 vehicle will have to meet a higher requirement than Regulation No. 13 but would represent a saving in cost and time due to the reduced testing.

___________