Distr.
GÉNÉRALE

ST/SG/AC.10/C.3/2005/53
13 septembre 2005

FRANÇAIS
Original: ANGLAIS

COMITÉ D’EXPERTS DU TRANSPORT DES 
MARCHANDISES DANGEREUSES ET DU SYSTÈME
GÉNÉRAL HARMONISÉ DE CLASSIFICATION ET
D’ÉTIQUETAGE DES PRODUITS CHIMIQUES

Sous-Comité d’experts du transport des marchandises dangereuses

Vingt-huitième session, 28 novembre-7 décembre 2005
Point 6 de l’ordre du jour provisoire

PROPOSITIONS DIVERSES D’AMENDEMENTS AU RÈGLEMENT TYPE
SUR LE TRANSPORT DES MARCHANDISES DANGEREUSES

Communication de l’expert des États-Unis d’Amérique

1.	L’expert des États-Unis d’Amérique a proposé des amendements aux dispositions spéciales applicables au transport en citernes mobiles dans le document UN/SCETDG/27/INF.23. Plusieurs membres du Sous-Comité ont formulé des observations sur ces propositions et il a été convenu qu’une proposition en bonne et due forme serait soumise pour examen à la vingt-huitième session. Le Sous-Comité est invité à examiner un certain nombre d’amendements aux dispositions spéciales applicables au transport en citernes mobiles (dispositions spéciales TP).

Propositions

2.	Il est proposé d’apporter les modifications ci-après aux dispositions spéciales applicables au transport en citernes mobiles:

a)	TP6, supprimer. La disposition TP6 s’applique au peroxyde d’hydrogène sous diverses formes (numéros ONU 2014, 2015, 2984 et 3149) et au chloroprène (numéro ONU 1991). Cette disposition est superflue. Des dispositifs de décompression sont déjà prescrits pour toutes les matières. Des prescriptions à ce sujet sont énoncées à la fois dans les dispositions spéciales TP et au chapitre 6.7 (voir 6.7.2.7.1). La disposition spéciale TP6 répète simplement ce qui est déjà dit au chapitre 6.7;

b)	TP9, supprimer. Cette disposition est ainsi rédigée «Une matière répondant à cette description ne peut être transportée en citernes mobiles qu’avec l’autorisation de l’autorité compétente.». Cette disposition est superflue et elle impose un surcroît de travail à la fois aux expéditeurs et aux autorités compétentes en exigeant l’autorisation de ces dernières. Les rubriques auxquelles est affectée la disposition spéciale TP9 sont des rubriques n.s.a. pour lesquelles des instructions de transport en conteneurs-citernes et des dispositions spéciales sont déjà prescrites dans la Liste des marchandises dangereuses. Toutes les rubriques visées par la disposition spéciale TP9 font déjà l’objet de dispositions restrictives pour le transport en citernes parce que ce sont des rubriques n.s.a. Au cours des 10 dernières années, l’autorité compétente des États-Unis d’Amérique a délivré de nouvelles autorisations TP9 pour le transport de matières visées par cette disposition spéciale, et dans chaque cas les termes de l’autorisation ont été identiques aux conditions admises en vertu des instructions de transport en citernes et des dispositions spéciales prescrites dans la Liste des marchandises dangereuses pour ces matières. Après discussion avec d’autres autorités compétentes, nous sommes parvenus à la conclusion que notre expérience n’est pas un cas isolé. Il est donc recommandé de supprimer la disposition spéciale TP9 à moins que des membres du Sous-Comité ne puissent citer des cas où ils auraient imposé d’autres conditions ou de conditions supplémentaires. Pour la discussion, une liste des matières auxquelles est affectée la disposition TP9 est jointe dans l’annexe 1;

c)	TP12, supprimer. Cette disposition est rédigée comme suit «Cette matière est très corrosive pour l’acier.». La formulation «très corrosive» n’est pas définie et elle ne s’appuie pas sur des critères précis; il s’agit donc sans doute d’un jugement d’expert. La disposition spéciale elle-même n’exprime pas une prescription comme c’est le cas de presque toutes les autres dispositions TP; il s’agit simplement d’une constatation. On ne sait pas non plus si la disposition est affectée à toutes les matières très corrosives. Aux fins de la discussion, une liste des matières auxquelles est affectée la disposition TP12 est présentée dans l’annexe 2 au présent document.

Annex 1 (English only)

Substances assigned TP9 in the UN Model Regulations (based on 13th revised edition)

| UN | Name | Portable tank SP | Class | PG | Sub-risk | SP | TI |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 1993 | FLAMMABLE LIQUID, N.O.S. | TP1 TP9 TP27 | 3 | I |  | 274 | T11 |
| 3295 | HYDROCARBONS, LIQUID, N.O.S. | TP1 TP8 TP9 TP28 | 3 | I |  |  | T11 |
| 1989 | ALDEHYDES, N.O.S. | TP1 TP9 TP27 | 3 | I |  | 274 | T11 |
| 1268 | PETROLEUM DISTILLATES, N.O.S. or PETROLEUM PRODUCTS, N.O.S. | TP1 TP8 TP9 | 3 | I |  |  | T11 |
| 1992 | FLAMMABLE LIQUID, TOXIC, N.O.S. | TP2 TP9 TP13 TP27 | 3 | I | 6.1 | 274 | T14 |
| 3021 | PESTICIDE, LIQUID,FLAMMABLE, TOXIC, N.O.S., flash point less than 23 °C | TP2 TP9 TP13 TP27 | 3 | I | 6.1 | 274 | T14 |
| 3273 | NITRILES, FLAMMABLE, TOXIC, N.O.S. | TP2 TP9 TP13 TP27 | 3 | I | 6.1 | 274 | T14 |
| 2776 | COPPER BASED PESTICIDE, LIQUID, FLAMMABLE, TOXIC, flash point less than 23 °C | TP2 TP9 TP13 TP27 | 3 | I | 6.1 | 274 | T14 |
| 2758 | CARBAMATE PESTICIDE, LIQUID, FLAMMABLE, TOXIC, flash point less than 23 °C | TP2 TP9 TP13 TP27 | 3 | I | 6.1 | 274 | T14 |
| 3346 | PHENOXYACETIC ACID DERIVATIVE PESTICIDE, LIQUID, FLAMMABLE, TOXIC, flash point less than 23 °C | TP2 TP9 TP13 TP27 | 3 | I | 6.1 | 274 | T14 |
| 1986 | ALCOHOLS, FLAMMABLE, TOXIC, N.O.S. | TP2 TP9 TP13 TP27 | 3 | I | 6.1 | 274 | T14 |
| 2760 | ARSENICAL PESTICIDE, LIQUID, FLAMMABLE, TOXIC, flash point less than 23 °C | TP2 TP9 TP13 TP27 | 3 | I | 6.1 | 274 | T14 |
| 3350 | PYRETHROID PESTICIDE, LIQUID, FLAMMABLE, TOXIC, flash point less than 23 °C | TP2 TP9 TP13 TP27 | 3 | I | 6.1 | 274 | T14 |
| 1988 | ALDEHYDES, FLAMMABLE, TOXIC, N.O.S. | TP2 TP9 TP13 TP27 | 3 | I | 6.1 | 274 | T14 |
| 2772 | THIOCARBAMATE PESTICIDE, LIQUID, FLAMMABLE, TOXIC, flash point less than 23 °C | TP2 TP9 TP13 TP27 | 3 | I | 6.1 | 274 | T14 |
| 2778 | MERCURY BASED PESTICIDE, LIQUID, FLAMMABLE, TOXIC, flash point less than 23 °C | TP2 TP9 TP13 TP27 | 3 | I | 6.1 | 274 | T14 |
| 2782 | BIPYRIDILIUM PESTICIDE, LIQUID, FLAMMABLE, TOXIC, flash point less than 23 °C | TP2 TP9 TP13 TP27 | 3 | I | 6.1 | 274 | T14 |
| 2762 | ORGANOCHLORINE PESTICIDE, LIQUID, FLAMMABLE, TOXIC, flash point less than 23 °C | TP2 TP9 TP13 TP27 | 3 | I | 6.1 | 274 | T14 |
| 2784 | ORGANOPHOSPHORUS PESTICIDE, LIQUID, FLAMMABLE, TOXIC, flash point less than 23 °C | TP2 TP9 TP13 TP27 | 3 | I | 6.1 | 274 | T14 |
| 3024 | COUMARIN DERIVATIVE PESTICIDE, LIQUID, FLAMMABLE, TOXIC, flash point less than 23 °C | TP2 TP9 TP13 TP27 | 3 | I | 6.1 | 274 | T14 |
| 2764 | TRIAZINE PESTICIDE, LIQUID, FLAMMABLE, TOXIC, flash point less than 23 °C | TP2 TP9 TP13 TP27 | 3 | I | 6.1 | 274 | T14 |
| 2780 | SUBSTITUTED NITROPHENOL PESTICIDE, LIQUID, FLAMMABLE, TOXIC, flash point less than 23 °C | TP2 TP9 TP13 TP27 | 3 | I | 6.1 | 274 | T14 |
| 2787 | ORGANOTIN PESTICIDE, LIQUID, FLAMMABLE, TOXIC, flash point less than 23 °C | TP2 TP9 TP13 TP27 | 3 | I | 6.1 | 274 | T14 |
| 3286 | FLAMMABLE LIQUID, TOXIC, CORROSIVE, N.O.S. | TP2 TP9 TP13 TP27 | 3 | I | 6.1 8 | 274 | T14 |
| 2924 | FLAMMABLE LIQUID, CORROSIVE, N.O.S. | TP2 TP9 | 3 | I | 8 | 274 | T14 |
| 2733 | AMINES, FLAMMABLE, CORROSIVE, N.O.S. or POLYAMINES, FLAMMABLE, CORROSIVE, N.O.S. | TP1 TP9 TP27 | 3 | I | 8 | 274 | T14 |
| 1268 | PETROLEUM DISTILLATES, N.O.S. or PETROLEUM PRODUCTS, N.O.S. | TP1 TP8 TP9 TP28 | 3 | II |  |  | T7 |
| 1268 | PETROLEUM DISTILLATES, N.O.S. or PETROLEUM PRODUCTS, N.O.S. | TP1 TP9 TP29 | 3 | III |  | 223 | T4 |
| 3200 | PYROPHORIC SOLID, INORGANIC, N.O.S. | TP7 TP9 TP33 | 4.2 | I |  | 274 | T21 |
| 1383 | PYROPHORIC METAL, N.O.S. or PYROPHORIC ALLOY, N.O.S. | TP7 TP9 TP33 | 4.2 | I |  | 274 | T21 |
| 2845 | PYROPHORIC LIQUID, ORGANIC, N.O.S. | TP2 TP7 TP9 | 4.2 | I |  | 274 | T22 |
| 3051 | ALUMINIUM ALKYLS | TP2 TP7 TP9 | 4.2 | I | 4.3 | 320 | T21 |
| 3052 | ALUMINIUM ALKYL HALIDES, LIQUID | TP2 TP7 TP9 | 4.2 | I | 4.3 | 320 | T21 |
| 2988 | CHLOROSILANES, WATER-REACTIVE, FLAMMABLE, CORROSIVE, N.O.S. | TP2 TP7 TP9 TP13 | 4.3 | I | 3 8 |  | T10 |
| 3375 | AMMONIUM NITRATE EMULSION or SUSPENSION or GEL, intermediate for blasting explosives | TP1 TP9 TP17 TP32 | 5.1 | II |  | 309 | T1 T2 |
| 1935 | CYANIDE SOLUTION, N.O.S. | TP2 TP9 TP13 TP27 | 6.1 | I |  |  | T14 |
| 3440 | SELENIUM COMPOUND, LIQUID, N.O.S. | TP2 TP9 TP27 | 6.1 | I |  |  | T14 |
| 3020 | ORGANOTIN PESTICIDE, LIQUID, TOXIC | TP2 TP9 TP13 TP27 | 6.1 | I |  | 61 274 | T14 |
| 3026 | COUMARIN DERIVATIVE PESTICIDE, LIQUID, TOXIC | TP2 TP9 TP13 TP27 | 6.1 | I |  | 61 274 | T14 |
| 2788 | ORGANOTIN COMPOUND, LIQUID, N.O.S. | TP2 TP9 TP13 TP27 | 6.1 | I |  | 43 274 | T14 |
| 2902 | PESTICIDE, LIQUID, TOXIC, N.O.S. | TP2 TP9 TP13 TP27 | 6.1 | I |  | 61 274 | T14 |
| 3018 | ORGANOPHOSPHORUS PESTICIDE, LIQUID, TOXIC | TP2 TP9 TP13 TP27 | 6.1 | I |  | 61 274 | T14 |
| 3352 | PYRETHROID PESTICIDE, LIQUID, TOXIC | TP2 TP9 TP13 TP27 | 6.1 | I |  | 61 274 | T14 |
| 2998 | TRIAZINE PESTICIDE, LIQUID, TOXIC | TP2 TP9 TP13 TP27 | 6.1 | I |  | 61 274 | T14 |
| 3348 | PHENOXYACETIC ACID DERIVATIVE PESTICIDE, LIQUID, TOXIC | TP2 TP9 TP13 TP27 | 6.1 | I |  | 61 274 | T14 |
| 3016 | BIPYRIDILIUM PESTICIDE, LIQUID, TOXIC | TP2 TP9 TP13 TP27 | 6.1 | I |  | 61 274 | T14 |
| 3014 | SUBSTITUTED NITROPHENOL PESTICIDE, LIQUID, TOXIC | TP2 TP9 TP13 TP27 | 6.1 | I |  | 61 274 | T14 |
| 3012 | MERCURY BASED PESTICIDE, LIQUID, TOXIC | TP2 TP9 TP13 TP27 | 6.1 | I |  | 61 274 | T14 |
| 3010 | COPPER BASED PESTICIDE, LIQUID, TOXIC | TP2 TP9 TP13 TP27 | 6.1 | I |  | 61 274 | T14 |
| 1556 | ARSENIC COMPOUND, LIQUID, N.O.S., inorganic, including: Arsenates, n.o.s., Arsenites, n.o.s.; and Arsenic sulphides, n.o.s. | TP2 TP9 TP13 TP27 | 6.1 | I |  | 43 | T14 |
| 2996 | ORGANOCHLORINE PESTICIDE, LIQUID, TOXIC | TP2 TP9 TP13 TP27 | 6.1 | I |  | 61 274 | T14 |
| 3006 | THIOCARBAMATE PESTICIDE, LIQUID, TOXIC | TP2 TP9 TP13 | 6.1 | I |  | 61 274 | T14 |
| 3276 | NITRILES, TOXIC, LIQUID, N.O.S. | TP2 TP9 TP13 TP27 | 6.1 | I |  | 274 315 | T14 |
| 3278 | ORGANOPHOSPHORUS COMPOUND, TOXIC, LIQUID, N.O.S. | TP2 TP9 TP13 TP27 | 6.1 | I |  | 43 274 315 | T14 |
| 3281 | METAL CARBONYLS, LIQUID, N.O.S. | TP2 TP9 TP13 TP27 | 6.1 | I |  | 274 315 | T14 |
| 3280 | ORGANOARSENIC COMPOUND, LIQUID, N.O.S. | TP2 TP9 TP13 TP27 | 6.1 | I |  | 274 315 | T14 |
| 3282 | ORGANOMETALLIC COMPOUND, TOXIC, LIQUID, N.O.S. | TP2 TP9 TP13 TP27 | 6.1 | I |  | 274 | T14 |
| 3287 | TOXIC LIQUID, INORGANIC, N.O.S. | TP2 TP9 TP13 TP27 | 6.1 | I |  | 274 315 | T14 |
| 2810 | TOXIC LIQUID, ORGANIC, N.O.S. | TP2 TP9 TP13 TP27 | 6.1 | I |  | 274 315 | T14 |
| 2992 | CARBAMATE PESTICIDE, LIQUID, TOXIC | TP2 TP9 TP13 TP27 | 6.1 | I |  | 61 274 | T14 |
| 2994 | ARSENICAL PESTICIDE, LIQUID, TOXIC | TP2 TP9 TP13 TP27 | 6.1 | I |  | 61 274 | T14 |
| 3382 | TOXIC BY INHALATION LIQUID, N.O.S. with an inhalation toxicity lower than or equal to 1000 ml/m3 and saturated vapour concentration greater than or equal to 10 LC50 | TP2 TP9 TP13 | 6.1 | I |  | 274 | T20 |
| 3381 | TOXIC BY INHALATION LIQUID, N.O.S. with an inhalation toxicity lower than or equal to 200 ml/m3 and saturated vapour concentration greater than or equal to 500 LC50 | TP2 TP9 TP13 | 6.1 | I |  | 274 | T22 |
| 2588 | PESTICIDE, SOLID, TOXIC, N.O.S. | TP9 TP33 | 6.1 | I |  | 61 274 | T6 |
| 2026 | PHENYLMERCURIC COMPOUND, N.O.S. | TP9 TP33 | 6.1 | I |  | 43 | T6 |
| 3467 | ORGANOMETALLIC COMPOUND, TOXIC, SOLID, N.O.S. | TP9 TP33 | 6.1 | I |  | 274 | T6 |
| 2811 | TOXIC SOLID, ORGANIC, N.O.S. | TP9 TP33 | 6.1 | I |  | 274 | T6 |
| 3284 | TELLURIUM COMPOUND, N.O.S. | TP9 TP33 | 6.1 | I |  |  | T6 |
| 3466 | METAL CARBONYLS, SOLID, N.O.S. | TP9 TP33 | 6.1 | I |  | 274 | T6 |
| 3465 | ORGANOARSENIC COMPOUND, SOLID, N.O.S. | TP9 TP33 | 6.1 | I |  | 274 | T6 |
| 3464 | ORGANOPHOSPHORUS COMPOUND, TOXIC, SOLID, N.O.S. | TP9 TP33 | 6.1 | I |  | 43 274 | T6 |
| 3462 | TOXINS, EXTRACTED FROM LIVING SOURCES, SOLID, N.O.S. | TP9 TP33 | 6.1 | I |  | 210 274 | T6 |
| 3448 | TEAR GAS SUBSTANCE, SOLID, N.O.S. | TP9 TP33 | 6.1 | I |  | 274 | T6 |
| 3439 | NITRILES, TOXIC, SOLID, N.O.S. | TP9 TP33 | 6.1 | I |  | 274 | T6 |
| 3349 | PYRETHROID PESTICIDE, SOLID, TOXIC | TP9 TP33 | 6.1 | I |  | 61 274 | T6 |
| 3345 | PHENOXYACETIC ACID DERIVATIVE PESTICIDE, SOLID, TOXIC | TP9 TP33 | 6.1 | I |  | 61 274 | T6 |
| 1544 | ALKALOIDS, SOLID, N.O.S. or ALKALOID SALTS, SOLID, N.O.S. | TP9 TP33 | 6.1 | I |  | 43 274 | T6 |
| 3288 | TOXIC SOLID, INORGANIC, N.O.S. | TP9 TP33 | 6.1 | I |  | 274 | T6 |
| 3285 | VANADIUM COMPOUND, N.O.S. | TP9 TP33 | 6.1 | I |  |  | T6 |
| 3283 | SELENIUM COMPOUND, SOLID, N.O.S. | TP9 TP33 | 6.1 | I |  |  | T6 |
| 1655 | NICOTINE COMPOUND, SOLID, N.O.S. or NICOTINE PREPARATION, SOLID, N.O.S. | TP9 TP33 | 6.1 | I |  | 43 | T6 |
| 2025 | MERCURY COMPOUND, SOLID, N.O.S. | TP9 TP33 | 6.1 | I |  | 43 66 | T6 |
| 3143 | DYE, SOLID, TOXIC, N.O.S. or DYE INTERMEDIATE, SOLID, TOXIC, N.O.S. | TP9 TP33 | 6.1 | I |  | 274 | T6 |
| 3146 | ORGANOTIN COMPOUND, SOLID, N.O.S. | TP9 TP33 | 6.1 | I |  | 43 274 | T6 |
| 1588 | CYANIDES, INORGANIC, SOLID, N.O.S. | TP9 TP33 | 6.1 | I |  | 47 274 | T6 |
| 1557 | ARSENIC COMPOUND, SOLID, N.O.S., inorganic, including: Arsenates, n.o.s.; Arsenites, n.o.s.; and Arsenic sulphides, n.o.s. | TP9 TP33 | 6.1 | I |  | 43 | T6 |
| 1601 | DISINFECTANT, SOLID, TOXIC, N.O.S. | TP9 TP33 | 6.1 | I |  | 274 | T6 |
| 3019 | ORGANOTIN PESTICIDE, LIQUID, TOXIC, FLAMMABLE, flash point not less than 23 °C | TP2 TP9 TP13 TP27 | 6.1 | I | 3 | 61 274 | T14 |
| 3017 | ORGANOPHOSPHORUS PESTICIDE, LIQUID, TOXIC, FLAMMABLE, flash point not less than 23 °C | TP2 TP9 TP13 TP27 | 6.1 | I | 3 | 61 274 | T14 |
| 2903 | PESTICIDE, LIQUID, TOXIC, FLAMMABLE, N.O.S., flash point not less than 23 °C | TP2 TP9 TP13 TP27 | 6.1 | I | 3 | 61 274 | T14 |
| 3351 | PYRETHROID PESTICIDE, LIQUID, TOXIC, FLAMMABLE, flash point not less than 23 °C | TP2 TP9 TP13 TP27 | 6.1 | I | 3 | 61 274 | T14 |
| 2997 | TRIAZINE PESTICIDE, LIQUID, TOXIC, FLAMMABLE, flash point not less than 23 °C | TP2 TP9 TP13 TP27 | 6.1 | I | 3 | 61 274 | T14 |
| 3015 | BIPYRIDILIUM PESTICIDE, LIQUID, TOXIC, FLAMMABLE, flash point not less than 23 °C | TP2 TP9 TP13 TP27 | 6.1 | I | 3 | 61 274 | T14 |
| 2929 | TOXIC LIQUID, FLAMMABLE, ORGANIC, N.O.S. | TP2 TP9 TP13 TP27 | 6.1 | I | 3 | 274 315 | T14 |
| 2993 | ARSENICAL PESTICIDE, LIQUID, TOXIC, FLAMMABLE, flash point not less than 23 °C | TP2 TP9 TP13 TP27 | 6.1 | I | 3 | 61 274 | T14 |
| 3013 | SUBSTITUTED NITROPHENOL PESTICIDE, LIQUID, TOXIC, FLAMMABLE, flash point not less than 23 °C | TP2 TP9 TP13 TP27 | 6.1 | I | 3 | 61 274 | T14 |
| 3009 | COPPER BASED PESTICIDE, LIQUID, TOXIC, FLAMMABLE, flash point not less than 23 °C | TP2 TP9 TP13 TP27 | 6.1 | I | 3 | 61 274 | T14 |
| 3025 | COUMARIN DERIVATIVE PESTICIDE, LIQUID, TOXIC, FLAMMABLE, flash point not less than 23 °C | TP2 TP9 TP13 TP27 | 6.1 | I | 3 | 61 274 | T14 |
| 2991 | CARBAMATE PESTICIDE, LIQUID, TOXIC, FLAMMABLE, flash point not less than 23 °C | TP2 TP9 TP13 TP27 | 6.1 | I | 3 | 61 274 | T14 |
| 3011 | MERCURY BASED PESTICIDE, LIQUID, TOXIC, FLAMMABLE, flash point not less than 23 °C | TP2 TP9 TP13 TP27 | 6.1 | I | 3 | 61 274 | T14 |
| 2995 | ORGANOCHLORINE PESTICIDE, LIQUID, TOXIC, FLAMMABLE, flash point not less than 23 °C | TP2 TP9 TP13 TP27 | 6.1 | I | 3 | 61 274 | T14 |
| 3279 | ORGANOPHOSPHORUS COMPOUND, TOXIC, FLAMMABLE, N.O.S. | TP2 TP9 TP13 TP27 | 6.1 | I | 3 | 43 274 315 | T14 |
| 3347 | PHENOXYACETIC ACID DERIVATIVE PESTICIDE, LIQUID, TOXIC, FLAMMABLE, flash point not less than 23 °C | TP2 TP9 TP13 TP27 | 6.1 | I | 3 | 61 274 | T14 |
| 3005 | THIOCARBAMATE PESTICIDE, LIQUID, TOXIC, FLAMMABLE, flash point not less than 23 °C | TP2 TP9 TP13 | 6.1 | I | 3 | 61 274 | T14 |
| 3275 | NITRILES, TOXIC, FLAMMABLE, N.O.S. | TP2 TP9 TP13 TP27 | 6.1 | I | 3 | 274 315 | T14 |
| 3384 | TOXIC BY INHALATION LIQUID, FLAMMABLE, N.O.S. with an inhalation toxicity lower than or equal to 1000 ml/m3 and saturated vapour concentration greater than or equal to 10 LC50 | TP2 TP9 TP13 | 6.1 | I | 3 | 274 | T20 |
| 3383 | TOXIC BY INHALATION LIQUID, FLAMMABLE, N.O.S. with an inhalation toxicity lower than or equal to 200 ml/m3 and saturated vapour concentration greater than or equal to 500 LC50 | TP2 TP9 TP13 | 6.1 | I | 3 | 274 | T22 |
| 2930 | TOXIC SOLID, FLAMMABLE, ORGANIC, N.O.S. | TP9 TP33 | 6.1 | I | 4.1 | 274 | T6 |
| 3124 | TOXIC SOLID, SELF-HEATING, N.O.S. | TP9 TP33 | 6.1 | I | 4.2 | 274 | T6 |
| 3386 | TOXIC BY INHALATION LIQUID, WATER-REACTIVE, N.O.S. with an inhalation toxicity lower than or equal to 1000 ml/m3 and saturated vapour concentration greater than or equal to 10 LC50 | TP2 TP9 TP13 | 6.1 | I | 4.3 | 274 | T20 |
| 3385 | TOXIC BY INHALATION LIQUID, WATER-REACTIVE, N.O.S. with an inhalation toxicity lower than or equal to 200 ml/m3 and saturated vapour concentration greater than or equal to 500 LC50 | TP2 TP9 TP13 | 6.1 | I | 4.3 | 274 | T22 |
| 3125 | TOXIC SOLID, WATER-REACTIVE, N.O.S. | TP9 TP33 | 6.1 | I | 4.3 | 274 | T6 |
| 3388 | TOXIC BY INHALATION LIQUID, OXIDIZING, N.O.S. with an inhalation toxicity lower than or equal to 1000 ml/m3 and saturated vapour concentration greater than or equal to 10 LC50 | TP2 TP9 TP13 | 6.1 | I | 5.1 | 274 | T20 |
| 3387 | TOXIC BY INHALATION LIQUID, OXIDIZING, N.O.S. with an inhalation toxicity lower than or equal to 200 ml/m3 and saturated vapour concentration greater than or equal to 500 LC50 | TP2 TP9 TP13 | 6.1 | I | 5.1 | 274 | T22 |
| 3086 | TOXIC SOLID, OXIDIZING, N.O.S. | TP9 TP33 | 6.1 | I | 5.1 | 274 | T6 |
| 3289 | TOXIC LIQUID, CORROSIVE, INORGANIC, N.O.S. | TP2 TP9 TP13 TP27 | 6.1 | I | 8 | 274 315 | T14 |
| 2927 | TOXIC LIQUID, CORROSIVE, ORGANIC, N.O.S. | TP2 TP9 TP13 TP27 | 6.1 | I | 8 | 274 315 | T14 |
| 3390 | TOXIC BY INHALATION LIQUID, CORROSIVE, N.O.S. with an inhalation toxicity lower than or equal to 1000 ml/m3 and saturated vapour concentration greater than or equal to 10 LC50 | TP2 TP9 TP13 | 6.1 | I | 8 | 274 | T20 |
| 3389 | TOXIC BY INHALATION LIQUID, CORROSIVE, N.O.S. with an inhalation toxicity lower than or equal to 200 ml/m3 and saturated vapour concentration greater than or equal to 500 LC50 | TP2 TP9 TP13 | 6.1 | I | 8 | 274 | T22 |
| 2928 | TOXIC SOLID, CORROSIVE, ORGANIC, N.O.S. | TP9 TP33 | 6.1 | I | 8 | 274 | T6 |
| 3290 | TOXIC SOLID, CORROSIVE, INORGANIC, N.O.S. | TP9 TP33 | 6.1 | I | 8 | 274 | T6 |
| 2735 | AMINES, LIQUID, CORROSIVE, N.O.S. or POLYAMINES, LIQUID, CORROSIVE, N.O.S. | TP2 TP9 TP27 | 8 | I |  | 274 | T14 |
| 3267 | CORROSIVE LIQUID, BASIC, ORGANIC, N.O.S. | TP2 TP9 TP27 | 8 | I |  | 274 | T14 |
| 1760 | CORROSIVE LIQUID, N.O.S. | TP2 TP9 TP27 | 8 | I |  | 274 | T14 |
| 3265 | CORROSIVE LIQUID, ACIDIC, ORGANIC, N.O.S. | TP2 TP9 TP27 | 8 | I |  | 274 | T14 |
| 3264 | CORROSIVE LIQUID, ACIDIC, INORGANIC, N.O.S. | TP2 TP9 TP27 | 8 | I |  | 274 | T14 |
| 3145 | ALKYLPHENOLS, LIQUID, N.O.S. (including C2-C12 homologues) | TP2 TP9 | 8 | I |  |  | T14 |
| 2801 | DYE, LIQUID, CORROSIVE, N.O.S. or DYE INTERMEDIATE, LIQUID, CORROSIVE, N.O.S. | TP2 TP9 TP27 | 8 | I |  | 274 | T14 |
| 3266 | CORROSIVE LIQUID, BASIC, INORGANIC, N.O.S. | TP2 TP9 TP27 | 8 | I |  | 274 | T14 |
| 3147 | DYE, SOLID, CORROSIVE, N.O.S. or DYE INTERMEDIATE, SOLID, CORROSIVE, N.O.S. | TP9 TP33 | 8 | I |  | 274 | T6 |
| 3263 | CORROSIVE SOLID, BASIC, ORGANIC, N.O.S. | TP9 TP33 | 8 | I |  | 274 | T6 |
| 1759 | CORROSIVE SOLID, N.O.S. | TP9 TP33 | 8 | I |  | 274 | T6 |
| 3262 | CORROSIVE SOLID, BASIC, INORGANIC, N.O.S. | TP9 TP33 | 8 | I |  | 274 | T6 |
| 3261 | CORROSIVE SOLID, ACIDIC, ORGANIC, N.O.S. | TP9 TP33 | 8 | I |  | 274 | T6 |
| 3259 | AMINES, SOLID, CORROSIVE, N.O.S. or POLYAMINES, SOLID, CORROSIVE, N.O.S. | TP9 TP33 | 8 | I |  | 274 | T6 |
| 2430 | ALKYLPHENOLS, SOLID, N.O.S. (including C2-C12 homologues) | TP9 TP33 | 8 | I |  |  | T6 |
| 3260 | CORROSIVE SOLID, ACIDIC, INORGANIC, N.O.S. | TP9 TP33 | 8 | I |  | 274 | T6 |
| 2734 | AMINES, LIQUID, CORROSIVE, FLAMMABLE, N.O.S. or POLYAMINES, LIQUID, CORROSIVE, FLAMMABLE, N.O.S. | TP2 TP9 TP27 | 8 | I | 3 | 274 | T14 |
| 2920 | CORROSIVE LIQUID, FLAMMABLE, N.O.S. | TP2 TP9 TP27 | 8 | I | 3 | 274 | T14 |
| 2921 | CORROSIVE SOLID, FLAMMABLE, N.O.S. | TP9 TP33 | 8 | I | 4.1 | 274 | T6 |
| 3095 | CORROSIVE SOLID, SELF-HEATING, N.O.S. | TP9 TP33 | 8 | I | 4.2 | 274 | T6 |
| 3096 | CORROSIVE SOLID, WATER-REACTIVE, N.O.S. | TP9 TP33 | 8 | I | 4.3 | 274 | T6 |
| 3084 | CORROSIVE SOLID, OXIDIZING, N.O.S. | TP9 TP33 | 8 | I | 5.1 | 274 | T6 |
| 2922 | CORROSIVE LIQUID, TOXIC, N.O.S. | TP2 TP9 TP13 TP27 | 8 | I | 6.1 | 274 | T14 |
| 2923 | CORROSIVE SOLID, TOXIC, N.O.S. | TP9 TP33 | 8 | I | 6.1 | 274 | T6 |

##### Annex 2 (English only)

Substances assigned TP12 in the UN Model Regulations (based on 13th revised edition)

| UN# | Name | Class | PG | S.R. | Portable Tank instruction | Portable Tank Special Provisions |
| --- | --- | --- | --- | --- | --- | --- |
| 1716 | ACETYL BROMIDE | 8 | II |  | T8 | TP2 TP12 |
| 1717 | ACETYL CHLORIDE | 3 | II | 8 | T8 | TP2 TP12 |
| 1736 | BENZOYL CHLORIDE | 8 | II |  | T8 | TP2 TP12 TP13 |
| 1737 | BENZYL BROMIDE | 6.1 | II | 8 | T8 | TP2 TP12 TP13 |
| 1738 | BENZYL CHLORIDE | 6.1 | II | 8 | T8 | TP2 TP12 TP13 |
| 1739 | BENZYL CHLOROFORMATE | 8 | I |  | T10 | TP2 TP12 TP13 |
| 1742 | BORON TRIFLUORIDE ACETIC ACID COMPLEX, LIQUID | 8 | II |  | T8 | TP2 TP12 |
| 1743 | BORON TRIFLUORIDE PROPIONIC ACID COMPLEX, LIQUID | 8 | II |  | T8 | TP2 TP12 |
| 1744 | BROMINE or BROMINE SOLUTION | 8 | I | 6.1 | T22 | TP2 TP10 TP12 TP13 |
| 1745 | BROMINE PENTAFLUORIDE | 5.1 | I | 6.1 8 | T22 | TP2 TP12 TP13 |
| 1746 | BROMINE TRIFLUORIDE | 5.1 | I | 6.1 8 | T22 | TP2 TP12 TP13 |
| 1754 | CHLORO-SULPHONIC ACID (with or without sulphur trioxide) | 8 | I |  | T20 | TP2 TP12 |
| 1755 | CHROMIC ACID SOLUTION | 8 | III |  | T4 | TP1 TP12 |
| 1755 | CHROMIC ACID SOLUTION | 8 | II |  | T8 | TP2 TP12 |
| 1758 | CHROMIUM OXYCHLORIDE | 8 | I |  | T10 | TP2 TP12 |
| 1764 | DICHLOROACETIC ACID | 8 | II |  | T8 | TP2 TP12 |
| 1768 | DIFLUOROPHOSPHORIC ACID, ANHYDROUS | 8 | II |  | T8 | TP2 TP12 |
| 1776 | FLUOROPHOSPHORIC ACID, ANHYDROUS | 8 | II |  | T8 | TP2 TP12 |
| 1777 | FLUOROSULPHONIC ACID | 8 | I |  | T10 | TP2 TP12 |
| 1778 | FLUOROSILICIC ACID | 8 | II |  | T8 | TP2 TP12 |
| 1782 | HEXAFLUOROPHOSPHORIC ACID | 8 | II |  | T8 | TP2 TP12 |
| 1786 | HYDROFLUORIC ACID AND SULPHURIC ACID MIXTURE | 8 | I | 6.1 | T10 | TP2 TP12 TP13 |
| 1789 | HYDROCHLORIC ACID | 8 | II |  | T8 | TP2 TP12 |
| 1789 | HYDROCHLORIC ACID | 8 | III |  | T4 | TP1 TP12 |
| 1790 | HYDROFLUORIC ACID, with more than 60% hydrogen fluoride | 8 | I | 6.1 | T10 | TP2 TP12 TP13 |
| 1790 | HYDROFLUORIC ACID, with not more than 60% hydrogen fluoride | 8 | II | 6.1 | T8 | TP2 TP12 |
| 1796 | NITRATING ACID MIXTURE with not more than 50% nitric acid | 8 | II |  | T8 | TP2 TP12 TP13 |
| 1796 | NITRATING ACID MIXTURE with more than 50% nitric acid | 8 | I | 5.1 | T10 | TP2 TP12 TP13 |
| 1798 | NITROHYDROCHLORIC ACID | 8 | I |  | T10 | TP2 TP12 TP13 |
| 1817 | PYROSULPHURYL CHLORIDE | 8 | II |  | T8 | TP2 TP12 |
| 1826 | NITRATING ACID MIXTURE, SPENT, with more than 50% nitric acid | 8 | I | 5.1 | T10 | TP2 TP12 TP13 |
| 1826 | NITRATING ACID MIXTURE, SPENT, with not more than 50% nitric acid | 8 | II |  | T8 | TP2 TP12 |
| 1828 | SULPHUR CHLORIDES | 8 | I |  | T20 | TP2 TP12 |
| 1829 | SULPHUR TRIOXIDE, STABILIZED | 8 | I |  | T20 | TP4 TP12 TP13 TP25 TP26 |
| 1830 | SULPHURIC ACID with more than 51% acid | 8 | II |  | T8 | TP2 TP12 |
| 1831 | SULPHURIC ACID, FUMING | 8 | I | 6.1 | T20 | TP2 TP12 TP13 |
| 1832 | SULPHURIC ACID, SPENT | 8 | II |  | T8 | TP2 TP12 |
| 1834 | SULPHURYL CHLORIDE | 8 | I |  | T20 | TP2 TP12 |
| 1836 | THIONYL CHLORIDE | 8 | I |  | T10 | TP2 TP12 TP13 |
| 1873 | PERCHLORIC ACID with more than 50% but not more than 72% acid, by mass | 5.1 | I | 8 | T10 | TP1 TP12 |
| 1906 | SLUDGE ACID | 8 | II |  | T8 | TP2 TP12 TP28 |
| 2031 | NITRIC ACID, other than red fuming, with more than 70% nitric acid | 8 | I | 5.1 | T10 | TP2 TP12 TP13 |
| 2031 | NITRIC ACID, other than red fuming, with not more than 70% nitric acid | 8 | II |  | T8 | TP2 TP12 |
| 2032 | NITRIC ACID, RED FUMING | 8 | I | 5.1 6.1 | T20 | TP2 TP12 TP13 |
| 2240 | CHROMOSULPHURIC ACID | 8 | I |  | T10 | TP2 TP12 TP13 |
| 2308 | NITROSYLSULPHURIC ACID, LIQUID | 8 | II |  | T8 | TP2 TP12 |
| 2353 | BUTYRYL CHLORIDE | 3 | II | 8 | T8 | TP2 TP12 TP13 |
| 2513 | BROMOACETYL BROMIDE | 8 | II |  | T8 | TP2 TP12 |
| 2571 | ALKYLSULPHURIC ACIDS | 8 | II |  | T8 | TP2 TP12 TP13 TP28 |
| 2584 | ALKYSULPHONIC ACIDS, LIQUID or ARYLSULPHONIC ACIDS, LIQUID with more than 5% free sulphuric acid | 8 | II |  | T8 | TP2 TP12 TP13 |
| 2692 | BORON TRIBROMIDE | 8 | I |  | T20 | TP2 TP12 TP13 |
| 2699 | TRIFLUOROACETIC ACID | 8 | I |  | T10 | TP2 TP12 |
| 2796 | SULPHURIC ACID with not more than 51% acid or BATTERY FLUID, ACID | 8 | II |  | T8 | TP2 TP12 |
| 2817 | AMMONIUM HYDROGEN-DIFLUORIDE SOLUTION | 8 | II | 6.1 | T8 | TP2 TP12 TP13 |
| 2817 | AMMONIUM HYDROGEN-DIFLUORIDE SOLUTION | 8 | III | 6.1 | T4 | TP1 TP12 TP13 |
| 2879 | SELENIUM OXYCHLORIDE | 8 | I | 6.1 | T10 | TP2 TP12 TP13 |
| 3246 | METHANESULPHONYL CHLORIDE | 6.1 | I | 8 | T14 | TP2 TP12 TP13 |

-----

# Text boxes

NATIONS UNIES

Secrétariat

ST