# UN/SCETDG/27/INF.8

COMMITTEE OF EXPERTS ON THE TRANSPORT OF

DANGEROUS GOODS AND ON THE GLOBALLY

HARMONIZED SYSTEM OF CLASSIFICATION

AND LABELLING OF CHEMICALS

Sub-Committee of Experts on the

Transport of Dangerous Goods

Twenty-seventh session

Geneva, 4-8 July 2005

Item 7 of the provisional agenda

MISCELLANEOUS PROPOSALS OF AMENDMENT TO THE MODEL REGULATIONS

ON THE TRANSPORT OF DANGEROUS GOODS

### Maximum degree of filling for filling by mass

Transmitted by the expert from Austria

#### Introduction

Packagings and tanks are often filled by weight using a balance. This should be reflected in the formulas of part 4 referring to the maximum degree of filling for liquids, by adding also the more user-friendly formula for the maximum mass in kg/m3 capacity.

For this formula, only the density at 50 °C is required. For the volume the density at 50 °C, the density at 15 °C and the temperature of the substance is required. Adding this formula may also contribute to a better understanding.

If the committee agrees that this would improve the regulations, we will come forward with a formal proposal at the next meeting.

#### Proposal

| Existing text | Proposed amended text |
| --- | --- |
| 4.1.1.4 When filling packagings, including IBCs and large packagings, with liquids, sufficient ullage (outage) shall be left to ensure that neither leakage nor permanent distortion of the packaging occurs as a result of an expansion of the liquid caused by temperatures likely to occur during transport. Unless specific requirements are prescribed, liquids shall not completely fill a packaging at a temperature of 55 °C. However, sufficient ullage shall be left in an IBC to ensure that at the mean bulk temperature of 50 °C it is not filled to more than 98% of its water capacity. 4.2.1.9.2 The maximum degree of filling (in %) for general use is determined by the formula: 4.2.1.9.3 The maximum degree of filling (in %) for liquids of Class 6.1 and Class 8, in packing groups I and II, and liquids with an absolute vapour pressure of more than 175 kPa (1.75 bar) at 65 °C, is determined by the formula: 4.2.5.3 TP1 The degree of filling prescribed in 4.2.1.9.2 shall not be exceeded. TP2 The degree of filling prescribed in 4.2.1.9.3 shall not be exceeded. | 4.1.1.4 When filling packagings, including IBCs and large packagings, with liquids, sufficient ullage (outage) shall be left to ensure that neither leakage nor permanent distortion of the packaging occurs as a result of an expansion of the liquid caused by temperatures likely to occur during transport. Unless specific requirements are prescribed, liquids shall not completely fill a packaging at a temperature of 55 °C. However, sufficient ullage shall be left in an IBC to ensure that at the mean bulk temperature of 50 °C it is not filled to more than 98% of its water capacity. Maximum degree of filling (in kg/m3 capacity) = 98 x d50 (density in kg/m3) 4.2.1.9.2 The maximum degree of filling for general use is determined by the formula: or Maximum degree of filling (in kg/m3 capacity) = 97 x d50 (density in kg/m3) 4.2.1.9.3 The maximum degree of filling for liquids of Class 6.1 and Class 8, in packing groups I and II, and liquids with an absolute vapour pressure of more than 175 kPa (1.75 bar) at 65 °C, is determined by the formula: or Maximum degree of filling (in kg/m3 capacity) = 95 x d50 (density in kg/m3) 4.2.5.3 TP1 The degree of filling prescribed in 4.2.1.9.2 shall not be exceeded. TP2 The degree of filling prescribed in 4.2.1.9.3 shall not be exceeded. |