# UN/SCETDG/27/INF.35

COMMITTEE OF EXPERTS ON THE TRANSPORT OF

DANGEROUS GOODS AND ON THE GLOBALLY

HARMONIZED SYSTEM OF CLASSIFICATION

AND LABELLING OF CHEMICALS

Sub-Committee of Experts on the

Transport of Dangerous Goods

Twenty-seventh session

Geneva, 4-8 July 2005

Item 6 of the provisional agenda

LISTING, CLASSIFICATION AND PACKING

Portable tank instructions and special provisions for UN 3129

Transmitted by the expert from the United States of America

1.	Introduction

Currently there are no portable tank instructions assigned to water-reactive liquid, n.o.s., water-reactive liquid, corrosive, n.o.s. or to the PG I entries for water-reactive solid, n.o.s and water reactive solid, corrosive, n.o.s.  It is proposed that tank assignments consistent with the “Guidelines for assigning portable tank requirements to substances in Classes 3 to 9” (see ST/SG/AC.10/25/Add.2) be assigned.  These assignments are also consistent with similarly classed entries in the Dangerous Goods List (see Annex 1 for a listing of current tank assignments for 4.3 substances).

2.	Proposal

Add new portable tank instructions and portable tank special provisions to the following entries in the Dangerous Goods List as follows:

| UN No. | Name and description | UN packing group | Portable tanks and bulk containers |
| --- | --- | --- | --- |
|  |  |  | Instructions | Special Provisions |
| 3129 | Water-reactive liquid, corrosive, n.o.s. | I | T10 | TP2 TP9 |
|  |  | II | T7 | TP2 TP28 |
|  |  | III | T7 | TP1 TP28 |
| 3148 | Water-reactive liquid, n.o.s. | I | T9 | TP2 TP9 |
|  |  | II | T7 | TP2 TP28 |
|  |  | III | T7 | TP1 TP28 |
| 3131 | Water-reactive solid, corrosive, n.o.s. | I | T9 | TP33 |
| 2813 | Water-reactive solid, n.o.s. | I | T9 | TP33 |

*****

Annex 1

| Current Tank Assignments for 4.3 Liquid and Solid Substances |
| --- |
| UN# | UN Name and Description | Class | PG | S.R. | SP | Tank Instruction | Tank Special Provision |
| 3401 | ALKALI METAL AMALGAM, SOLID | 4.3 | I |  | 182 | T9 | TP7 TP33 |
| 1390 | ALKALI METAL AMIDES | 4.3 | II |  | 182 | T3 | TP33 |
| 1393 | ALKALINE EARTH METAL ALLOY, N.O.S. | 4.3 | II |  |  | T3 | TP33 |
| 3402 | ALKALINE EARTH METAL AMALGAM, SOLID | 4.3 | I |  | 183 | T9 | TP7 TP33 |
| 1394 | ALUMINIUM CARBIDE | 4.3 | II |  |  | T3 | TP33 |
| 1395 | ALUMINIUM FERROSILICON POWDER | 4.3 | II | 6.1 |  | T3 | TP33 |
| 1396 | ALUMINIUM POWDER, UNCOATED | 4.3 | II |  |  | T3 | TP33 |
| 1396 | ALUMINIUM POWDER, UNCOATED | 4.3 | III |  | 223 | T1 | TP33 |
| 1398 | ALUMINIUM SILICON POWDER, UNCOATED | 4.3 | III |  | 37 223 | T1 | TP33 |
| 3170 | ALUMINIUM SMELTING BY-PRODUCTS or ALUMINIUM REMELTING BY-PRODUCTS | 4.3 | II |  | 244 | T3 BK1 BK2 | TP33 |
| 3170 | ALUMINIUM SMELTING BY-PRODUCTS or ALUMINIUM REMELTING BY-PRODUCTS | 4.3 | III |  | 223 244 | T1 BK1 BK2 | TP33 |
| 1400 | BARIUM | 4.3 | II |  |  | T3 | TP33 |
| 2965 | BORON TRIFLUORIDE DIMETHYL ETHERATE | 4.3 | I | 3 8 |  | T10 | TP2 TP7 |
| 1401 | CALCIUM | 4.3 | II |  |  | T3 | TP33 |
| 1402 | CALCIUM CARBIDE | 4.3 | I |  |  | T9 | TP7 TP33 |
| 1402 | CALCIUM CARBIDE | 4.3 | II |  |  | T3 | TP33 |
| 1403 | CALCIUM CYANAMIDE with more than 0.1% calcium carbide | 4.3 | III |  | 38 | T1 | TP33 |
| 2844 | CALCIUM MANGANESE SILICON | 4.3 | III |  |  | T1 | TP33 |
| 1405 | CALCIUM SILICIDE | 4.3 | II |  |  | T3 | TP33 |
| 1405 | CALCIUM SILICIDE | 4.3 | III |  | 223 | T1 | TP33 |
| 3078 | CERIUM, turnings or gritty powder | 4.3 | II |  |  | T3 | TP33 |
| 2988 | CHLOROSILANES, WATER-REACTIVE, FLAMMABLE, CORROSIVE, N.O.S. | 4.3 | I | 3 8 |  | T10 | TP2 TP7 TP9 TP13 |
| 1183 | ETHYLDICHLOROSILANE | 4.3 | I | 3 8 |  | T10 | TP2 TP7 TP13 |
| 1408 | FERROSILICON with 30% or more but less than 90% silicon | 4.3 | III | 6.1 | 39 223 | T1 BK2 | TP33 |
| 2830 | LITHIUM FERROSILICON | 4.3 | II |  |  | T3 | TP33 |
| 2805 | LITHIUM HYDRIDE, FUSED SOLID | 4.3 | II |  |  | T3 | TP33 |
| 1417 | LITHIUM SILICON | 4.3 | II |  |  | T3 | TP33 |
| 2950 | MAGNESIUM GRANULES, COATED, particle size not less than 149 microns | 4.3 | III |  |  | T1 BK2 | TP33 |
| 1418 | MAGNESIUM POWDER or MAGNESIUM ALLOYS POWDER | 4.3 | II | 4.2 |  | T3 | TP33 |
| 1418 | MAGNESIUM POWDER or MAGNESIUM ALLOYS POWDER | 4.3 | III | 4.2 | 223 | T1 | TP33 |
| 2624 | MAGNESIUM SILICIDE | 4.3 | II |  |  | T3 | TP33 |
| 2968 | MANEB, STABILIZED or MANEB PREPARATION, STABILIZED against self-heating | 4.3 | III |  | 223 | T1 | TP33 |
| 1409 | METAL HYDRIDES, WATER-REACTIVE, N.O.S. | 4.3 | II |  | 274 | T3 | TP33 |
| 3208 | METALLIC SUBSTANCE, WATER-REACTIVE, N.O.S. | 4.3 | II |  | 274 | T3 | TP33 |
| 3208 | METALLIC SUBSTANCE, WATER-REACTIVE, N.O.S. | 4.3 | III |  | 223 274 | T1 | TP33 |
| 3209 | METALLIC SUBSTANCE, WATER-REACTIVE, SELF-HEATING, N.O.S. | 4.3 | II | 4.2 | 274 | T3 | TP33 |
| 3209 | METALLIC SUBSTANCE, WATER-REACTIVE, SELF-HEATING, N.O.S. | 4.3 | III | 4.2 | 223 274 | T1 | TP33 |
| 1242 | METHYLDI-CHLOROSILANE | 4.3 | I | 3 8 |  | T10 | TP2 TP7 TP13 |
| 3398 | ORGANOMETALLIC SUBSTANCE, LIQUID, WATER-REACTIVE | 4.3 | I |  | 274 | T13 | TP2 TP7 |
| 3398 | ORGANOMETALLIC SUBSTANCE, LIQUID, WATER-REACTIVE | 4.3 | II |  | 274 | T7 | TP2 TP7 |
| 3398 | ORGANOMETALLIC SUBSTANCE, LIQUID, WATER-REACTIVE | 4.3 | III |  | 223 274 | T7 | TP2 TP7 |
| 3399 | ORGANOMETALLIC SUBSTANCE, LIQUID, WATER-REACTIVE, FLAMMABLE | 4.3 | I | 3 | 274 | T13 | TP2 TP7 |
| 3399 | ORGANOMETALLIC SUBSTANCE, LIQUID, WATER-REACTIVE, FLAMMABLE | 4.3 | II | 3 | 274 | T7 | TP2 TP7 |
| 3399 | ORGANOMETALLIC SUBSTANCE, LIQUID, WATER-REACTIVE, FLAMMABLE | 4.3 | III | 3 | 223 274 | T7 | TP2 TP7 |
| 3395 | ORGANOMETALLIC SUBSTANCE, SOLID, WATER-REACTIVE | 4.3 | I |  | 274 | T9 | TP7 TP33 |
| 3395 | ORGANOMETALLIC SUBSTANCE, SOLID, WATER-REACTIVE | 4.3 | II |  | 274 | T3 | TP33 |
| 3395 | ORGANOMETALLIC SUBSTANCE, SOLID, WATER-REACTIVE | 4.3 | III |  | 223 274 | T1 | TP33 |
| 3396 | ORGANOMETALLIC SUBSTANCE, SOLID, WATER-REACTIVE, FLAMMABLE | 4.3 | I | 4.1 | 274 | T9 | TP7 TP33 |
| 3396 | ORGANOMETALLIC SUBSTANCE, SOLID, WATER-REACTIVE, FLAMMABLE | 4.3 | II | 4.1 | 274 | T3 | TP33 |
| 3396 | ORGANOMETALLIC SUBSTANCE, SOLID, WATER-REACTIVE, FLAMMABLE | 4.3 | III | 4.1 | 223 274 | T1 | TP33 |
| 3397 | ORGANOMETALLIC SUBSTANCE, SOLID, WATER-REACTIVE, SELF-HEATING | 4.3 | I | 4.2 | 274 | T9 | TP7 TP33 |
| 3397 | ORGANOMETALLIC SUBSTANCE, SOLID, WATER-REACTIVE, SELF-HEATING | 4.3 | II | 4.2 | 274 | T3 | TP33 |
| 3397 | ORGANOMETALLIC SUBSTANCE, SOLID, WATER-REACTIVE, SELF-HEATING | 4.3 | III | 4.2 | 223 274 | T1 | TP33 |
| 1340 | PHOSPHORUS PENTASULPHIDE, free from yellow and white phosphorus | 4.3 | II | 4.1 |  | T3 | TP33 |
| 2257 | POTASSIUM | 4.3 | I |  |  | T9 | TP7 TP33 |
| 3403 | POTASSIUM METAL ALLOYS, SOLID | 4.3 | I |  |  | T9 | TP7 TP33 |
| 1422 | POTASSIUM SODIUM ALLOYS, LIQUID | 4.3 | I |  |  | T9 | TP3 TP7 TP31 |
| 3404 | POTASSIUM SODIUM ALLOYS, SOLID | 4.3 | I |  |  | T9 | TP7 TP33 |
| 1428 | SODIUM | 4.3 | I |  |  | T9 | TP7 TP33 |
| 2835 | SODIUM ALUMINIUM HYDRIDE | 4.3 | II |  |  | T3 | TP33 |
| 1295 | TRICHLOROSILANE | 4.3 | I | 3 8 |  | T14 | TP2 TP7 TP13 |
| 3131 | WATER-REACTIVE SOLID, CORROSIVE, N.O.S. | 4.3 | II | 8 | 274 | T3 | TP33 |
| 3131 | WATER-REACTIVE SOLID, CORROSIVE, N.O.S. | 4.3 | III | 8 | 223 274 | T1 | TP33 |
| 3132 | WATER-REACTIVE SOLID, FLAMMABLE, N.O.S. | 4.3 | II | 4.1 | 274 | T3 | TP33 |
| 3132 | WATER-REACTIVE SOLID, FLAMMABLE, N.O.S. | 4.3 | III | 4.1 | 223 274 | T1 | TP33 |
| 2813 | WATER-REACTIVE SOLID, N.O.S. | 4.3 | II |  | 274 | T3 | TP33 |
| 2813 | WATER-REACTIVE SOLID, N.O.S. | 4.3 | III |  | 223 274 | T1 | TP33 |
| 3135 | WATER-REACTIVE SOLID, SELF-HEATING, N.O.S. | 4.3 | II | 4.2 | 274 | T3 | TP33 |
| 3135 | WATER-REACTIVE SOLID, SELF-HEATING, N.O.S. | 4.3 | III | 4.2 | 223 274 | T1 | TP33 |
| 3134 | WATER-REACTIVE SOLID, TOXIC, N.O.S. | 4.3 | II | 6.1 | 274 | T3 | TP33 |
| 3134 | WATER-REACTIVE SOLID, TOXIC, N.O.S. | 4.3 | III | 6.1 | 223 274 | T1 | TP33 |
| 1435 | ZINC ASHES | 4.3 | III |  | 223 | T1 | TP33 |
| 1436 | ZINC POWDER or ZINC DUST | 4.3 | II | 4.2 |  | T3 | TP33 |
| 1436 | ZINC POWDER or ZINC DUST | 4.3 | III | 4.2 | 223 | T1 | TP33 |

____________