PROPOSAL FOR DRAFT AMENDMENTS TO REGULATION No. 16

(Safety-belts)

Note:  The text reproduced below was prepared by the expert from Japan.  The modifications to the text are marked in bold characters.

## A. PROPOSAL

Annex 16, amend to read:

# Annex 16

MINIMUM REQUIREMENTS FOR SAFETY BELTS AND RETRACTORS

| Vehicle Category | Forward facing seating positions | Rear facing Seating positions |
| --- | --- | --- |
|  | Outboard seating positions | Centre seating positions |  |
|  | Front | Other than front | Front | Other than front |  |
| ….. | …. | …. | ….. | ….. | …. |
| N2 N3 | B,Br3,Br4m,Br4Nm or A, Ar4m,Ar4Nm* | …. | …. | …. | …. |

## B. JUSTIFICATION

Japan is currently considering adopting ECE Regulation No. 16 into its national regulations.  However, the Japanese Safety Regulation and ECE Regulation No. 16 differ from each other in that the Safety Regulation requires, from a standpoint of ensuring the driver’s safety in the event of a collision, mandatory installation of an Emergency Locking Retractor (ELR) at the driver’s seat of category N2 and N3 vehicles, whereas the ECE Regulation does not require such mandatory installation of ELRs.  For this reason, Japan proposes to amend ECE Regulation No. 16 as above.  In addition, since this proposal involves tightening installation requirements for safety belts, the proposed amendment must be issued as a new series of amendments.

- - - - -