#### UNITED

# NATIONS

Distr.

# GENERAL

# ST/SG/AC.10/C.3/2006/35

10 April 2006

Original: ENGLISH

COMMITTEE OF EXPERTS ON THE TRANSPORT OF

# DANGEROUS GOODS AND ON THE GLOBALLY

## HARMONIZED SYSTEM OF CLASSIFICATION

# AND LABELLING OF CHEMICALS

# Sub-Committee of Experts on the

# Transport of Dangerous Goods

# Twenty-ninth session

# Geneva, 3-12 (a.m.) July 2006

# Item 7 of the provisional agenda

miscellaneous Proposals of AmeNdments to the model regulations on The Transport of Dangerous Goods

Transport of various substances of Classes 3-9 in portable tanks

Transmitted by the expert from the United Kingdom

Introduction

- The Sub-Committee will recall that the system of aligning portable tanks to substances based on the rationalised approach has been developed during previous biennia. These first appeared in the 11th revised edition of the Model Regulations. Since then there have been additions to the list of substances that can be carried in portable tanks and there have also been a number of working and information papers that have sought to explain the criteria behind this for the purposes of developing the guiding principles.

- The expert from the United Kingdom is aware that there are still a number of substances indicated in the Dangerous Goods List of the Model Regulations that do not attract a portable tank code; the expert from the United Kingdom attaches a list of those substances in the attached Annex. None of those substances appear to come into the category of those considered unsuitable for portable tanks and are referred to in the general guidelines for portable tanks, see part 1 of ST/SG/AC.10/C.3/2005/51, produced by the expert from the United States of America.

- The expert from the United Kingdom would welcome discussion on the suitability of these portable tank codes for the substances listed and if the Sub-Committee agrees proposes listing these codes under columns 10 and 11 of the Dangerous Goods List.

______________

Annex  (ENGLISH ONLY)

| UN NUMBER | PROPER SHIPPING NAME | CLASS | SUB HAZARD | PG | PROPOSEDPORTABLE TANK CODE | PROPOSED TP CODE | RID/ADR TANK (CODE) |
| --- | --- | --- | --- | --- | --- | --- | --- |
| UN 1308 | ZIRCONIUM SUSPENDED IN A FLAMMABLE LIQUID | 3 |  | I | T11 | TP1 TP27 | YES (L4BN)(L1.5BN) |
| UN 1308 | ZIRCONIUM SUSPENDED IN A FLAMMABLE LIQUID | 3 |  | II | T7 | TP1 TP8 TP28 | YES (L1.5BN)(LGBF) |
| UN 1308 | ZIRCONIUM SUSPENDED IN A FLAMMABLE LIQUID | 3 |  | III | T4 | TP1 TP29 | YES (LGBF) |
| UN 3248 | MEDICINE, LIQUID, FLAMMABLE, TOXIC, N.O.S. | 3 | 6.1 | II | T11 | TP2 TP27 | YES (L4BH) |
| UN 3248 | MEDICINE, LIQUID, FLAMMABLE, TOXIC, N.O.S. | 3 | 6.1 | III | T7 | TP1 TP28 | YES (L4BH) |
| UN 1380 | PENTABORANE | 4.2 | 6.1 | I | T21 | TP2 TP7 | YES (L21DH) |
| UN 1471 | LITHIUM HYPOCHLORITE, DRY OR LITHIUM HYPOCHLORITE MIXTURE | 5.1 |  | II | T3 | TP33 | YES (SGAN) |
| UN 1748 | CALCIUM HYPOCHLORITE,DRY or CALCIUM HYPOCHLORITE MIXTURE, DRY | 5.1 |  | II | T3 | TP33 | YES (SGAN) |
| UN 1748 | CALCIUM HYPOCHLORITE,DRY or CALCIUM HYPOCHLORITE MIXTURE, DRY | 5.1 |  | III | T1 | TP33 | YES (SGAV) |
| UN 2208 | CALCIUM HYPOCHLORITE MIXTURE, DRY with more than 10% but not more then 39% available chlorine | 5.1 |  | III | T1 | TP33 | YES (SGAN) |
| UN 2880 | CALCIUM HYPOCHLORITE, HYDRATED or CALCIUM HYPOCHLORITE, HYDRATED MIXTURE with not less than 5.5% and not more than 16% water | 5.1 |  | II | T3 | TP33 | YES (SGAN) |
| UN 2880 | CALCIUM HYPOCHLORITE, HYDRATED or CALCIUM HYPOCHLORITE, HYDRATED MIXTURE with not less than 5.5% and not more than 16% water | 5.1 |  | III | T1 | TP33 | YES (SGAV) |
| UN 1259 | NICKEL CARBONYL | 6.1 | 3 | I | T14 | TP2 TP7 TP13 TP27 | YES (L15CH) |
| UN 1583 | CHLOROPICRIN MIXTURE, N.O.S. | 6.1 |  | I | T14 | TP2 | YES (L10CH) |
| UN 1583 | CHLOROPICRIN MIXTURE, N.O.S. | 6.1 |  | II | T11 | TP2 TP27 | YES (L4BH) |
| UN 1583 | CHLOROPICRIN MIXTURE, N.O.S. | 6.1 |  | III | T7 | TP1 TP28 | YES (L4BH) |
| UN 1602 | DYE, LIQUID, TOXIC, N.O.S. or DYE INTERMEDIATE, LIQUID, TOXIC N.O.S. | 6.1 |  | I | T14 | TP2 | YES (L10CH) |
| UN 1602 | DYE, LIQUID, TOXIC, N.O.S. or DYE INTERMEDIATE, LIQUID, TOXIC N.O.S. | 6.1 |  | II | T11 | TP2 TP27 | YES (L4BH) |
| UN 1602 | DYE, LIQUID, TOXIC, N.O.S. or DYE INTERMEDIATE, LIQUID, TOXIC N.O.S. | 6.1 |  | III | T7 | TP1 TP28 | YES (L4BH) |
| UN 1647 | METHYL BROMIDE AND ETHYLENE DIBROMIDE MIXTURE, LIQUID | 6.1 |  | I | T14 | TP2 TP13 | YES (L10CH) |
| UN 1656 | NICOTINE HYDROCHLORIDE, LIQUID or SOLUTION | 6.1 |  | II | T7 | TP2 | YES (L4BH) |
| UN 1656 | NICOTINE HYDROCHLORIDE, LIQUID or SOLUTION | 6.1 |  | III | T4 | TP1 | YES (L4BH) |
| UN 1699 | DIPHENYLCHLOROARSINE, LIQUID | 6.1 |  | I | T14 | TP2 TP13 | YES (L10CH) |
| UN 1851 | MEDICINE, LIQUID, TOXIC, N.O.S. | 6.1 |  | II | T11 | TP2 TP27 | YES (L4BH) |
| UN 1851 | MEDICINE, LIQUID, TOXIC, N.O.S. | 6.1 |  | III | T7 | TP1 TP28 | YES (L4BH) |
| UN 2024 | MERCURY COMPOUND, LIQUID, N.O.S. | 6.1 |  | I | T14 | TP2 | YES (L10CH) |
| UN 2024 | MERCURY COMPOUND, LIQUID, N.O.S. | 6.1 |  | II | T11 | TP2 TP27 | YES (L4BH) |
| UN 2024 | MERCURY COMPOUND LIQUID, N.O.S. | 6.1 |  | III | T7 | TP1 TP28 | YES (L4BH) |
| UN 2609 | TRIALLYL BORATE | 6.1 |  | III | T4 | TP1 | YES (L4BH) |
| UN 3122 | TOXIC LIQUID, OXIDIZING, N.O.S. | 6.1 | 5.1 | I | T14 | TP2 | YES (L10CH) |
| UN 3122 | TOXIC LIQUID, OXIDIZING, N.O.S. | 6.1 | 5.1 | II | T11 | TP2 TP27 | YES (L4BH) |
| UN 3123 | TOXIC LIQUID, WATER REACTIVE, N.O.S. | 6.1 | 4.3 | I | T14 | TP2 | YES (L10CH) |
| UN 3123 | TOXIC LIQUID, WATER REACTIVE, N.O.S. | 6.1 | 4.3 | II | T11 | TP2 TP27 | YES (L4BH) |
| UN 3140 | ALKALOIDS, LIQUID, N.O.S or ALKALOID SALTS, LIQUID, N.O.S. | 6.1 |  | I | T14 | TP2 | YES (L10CH) |
| UN 3140 | ALKALOIDS, LIQUID, N.O.S or ALKALOID SALTS, LIQUID, N.O.S. | 6.1 |  | II | T11 | TP2 TP27 | YES (L4BH) |
| UN 3140 | ALKALOIDS, LIQUID, N.O.S or ALKALOID SALTS, LIQUID, N.O.S. | 6.1 |  | III | T7 | TP1 TP28 | YES (L4BH) |
| UN 3141 | ANTIMONY COMPOUND, INORGANIC, LIQUID, N.O.S. | 6.1 |  | III | T7 | TP1 TP28 | YES (L4BH) |
| UN 3142 | DISINFECTANT, LIQUID, TOXIC, N.O.S. | 6.1 |  | I | T14 | TP2 | YES (L10CH) |
| UN 3142 | DISINFECTANT, LIQUID, TOXIC, N.O.S. | 6.1 |  | II | T11 | TP2 TP27 | YES (L4BH) |
| UN 3142 | DISINFECTANT, LIQUID, TOXIC, N.O.S. | 6.1 |  | III | T7 | TP1 TP28 | YES (L4BH) |
| UN 3144 | NICOTINE COMPOUND, LIQUID, N.O.S. or NICOTINE PREPARATION, LIQUID, N.O.S. | 6.1 |  | I | T14 | TP2 | YES (L10CH) |
| UN 3144 | NICOTINE COMPOUND, LIQUID, N.O.S. or NICOTINE PREPARATION, LIQUID, N.O.S. | 6.1 |  | II | T11 | TP2 TP27 | YES (L4BH) |
| UN 3144 | NICOTINE COMPOUND, LIQUID, N.O.S. or NICOTINE PREPARATION, LIQUID, N.O.S. | 6.1 |  | III | T7 | TP1 TP28 | YES (L4BH) |
| UN 3172 | TOXINS, EXTRACTED FROM LIVING SOURCES, LIQUID, N.O.S. | 6.1 |  | I | T14 | TP2 | YES (L10CH) |
| UN 3172 | TOXINS, EXTRACTED FROM LIVING SOURCES, LIQUID, N.O.S. | 6.1 |  | II | T11 | TP2 TP27 | YES (L4BH) |
| UN 3172 | TOXINS, EXTRACTED FROM LIVING SOURCES, LIQUID, N.O.S. | 6.1 |  | III | T7 | TP1 TP28 | YES (L4BH) |
| UN 1903 | DISINFECTANT, LIQUID, CORROSIVE, N.O.S. | 8 |  | I | T14 | TP2 TP27 | YES (L10BH) |
| UN 1903 | DISINFECTANT, LIQUID, CORROSIVE, N.O.S. | 8 |  | II | T11 | TP2 TP27 | YES (L4BN) |
| UN 1903 | DISINFECTANT, LIQUID, CORROSIVE, N.O.S. | 8 |  | III | T7 | TP1 TP28 | YES (L4BN) |
| UN 2809 | MERCURY | 8 |  | III | T4 | TP1 | YES (L4BN) |
| UN 2904 | CHLOROPHENOLATES,LIQUID, or PHENOLATES LIQUID | 8 |  | III | T4 | TP1 | YES (L4BN) |
| UN 3093 | CORROSIVE LIQUID, OXIDIZING, N.O.S. | 8 | 5.1 | I | T14 | TP2 TP27 | YES (L10BH) |
| UN 3093 | CORROSIVE LIQUID, OXIDIZING, N.O.S. | 8 | 5.1 | II | T11 | TP2 TP27 | YES (L4BN) |
| UN 3094 | CORROSIVE LIQUID, WATER, REACTIVE, N.O.S. | 8 | 4.3 | I | T14 | TP2 TP27 | YES (L10BH) |
| UN 3094 | CORROSIVE LIQUID, WATER, REACTIVE, N.O.S. | 8 | 4.3 | II | T11 | TP2 TP27 | YES (L4BN) |
| UN 3151 | POLYHALOGENATED BIPHENYLS, LIQUID or POLYHALOGENATED TERPHENYLS, LIQUID | 9 |  | II | T4 | TP1 | YES (L4BH) |

# Text boxes

STSTE

Secretariat