#### UNITED

# NATIONS

Distr.

# GENERAL

# ST/SG/AC.10/C.3/2006/47

13 April 2006

Original: ENGLISH

## COMMITTEE OF EXPERTS ON THE TRANSPORT OF

# DANGEROUS GOODS AND ON THE GLOBALLY

# HARMONIZED SYSTEM OF CLASSIFICATION

# AND LABELLING OF CHEMICALS

# Sub-Committee of Experts on the

# Transport of Dangerous Goods

# Twenty-ninth session

# Geneva, 3-12 (a.m.) July 2006

# Item 6 of the provisional agenda

LISTING, CLASSIFICATION AND PACKING

Provisions for the transport of solid substances in bulk containers
- Revised rationalised approach -

Transmitted by the International Council of Chemical Associations (ICCA)

Background

1.	Provisions for the use of bulk containers for the transport of solid substances in bulk were included in a new Chapter 4.3 of the thirteenth revised edition of the UN Model Regulations. At the same time two new bulk container codes (BK1 for transport in sheeted bulk containers and BK2 for transport in closed bulk containers) were added in column 10 of the Dangerous Goods List for some 25 UN entries.

2.	These provisions were the result of a series of discussions, which started with document ST/SG/AC.10/C.3/1999/92 (Germany), followed by documents ST/SG/AC.10/C.3/2001/37 (United Kingdom and Germany) and ST/SG/AC.10/C.3/2002/29 (United Kingdom and Germany) (and informal document UN/SCETDG/21/INF.66) before they were finally adopted at the 21st session in July 2002.

3.	During these discussions, ICCA promised to present in future a proposal for a rationalised approach for the assignment of bulk container codes. Since then ICCA has made two proposals (ST/SG/AC.10/C.3/2004/42 and UN/SCETDG/27/INF.24) which were not received favourably.

Introduction

4.	As a result of the discussion ICCA took into consideration the solid substances that are currently being allowed to be transported in bulk in the different modes and regulations.

5.	As a basis, all solid substances were considered that are currently allowed to be transported in bulk by road/rail in Europe according to ADR (Road) and RID (Rail). These are identified by the presence of a special provision for the carriage in bulk (VVx in ADR and similarly with WWx in RID) in column (17) of the Dangerous Goods List in ADR and RID. The meaning of these special provisions can be found in the Annex 2 at the end of this document (reproduction of Chapter 7.3 of ADR 2005 – RID has an identical chapter).

6.	In order to provide a general overview this list of substances (see Annex 1) has been completed by indicating an eventual reference to:

- § 173.240 in column (8c) of the Hazardous Material Table in CFR 49 of United States of America, authorising the use of “closed bulk bins” (see item c of § 173.240);

- BK2 in column (13) of the Dangerous Goods List of the IMO IMDG Code. Note that sheeted bulk containers (BK1) are not allowed for sea transport;

- Listing of the substance in the IMO Code of Practice for Solid Bulk Cargoes (BC Code). Group B refers to cargoes with chemical hazards.

7.	In addition to all entries with a BK code in the Dangerous Goods List of the 14th revised Edition of the UN Model Regulations, ADR/RID have assigned a VV/WW special provision to many more solid substances and this is the case also, albeit to a lesser extent, for CFR 49.

8.	The IMDG Code has assigned BK2 to a number of solids, which have no BK code in the UN Model Regulations. In most, but not all cases, this corresponds to solids, which have been listed in the BC Code.

Proposal

9.	The table below provides a summary of the findings and proposed amendments:

| Class | Subrisk | PG | CFR 49 (§ 173.240) | ADR/RID (VV/WW) | Number of UN entries | UN numbers already with BK-provision: Assign- ments to be kept: see (a) | Proposal for adding |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  |  | BK1 | BK2 |
| 4.1 |  | II | x | VV3 | 1 | 3175 (BK1-BK2) |  |  |
|  |  | III | x (except UN 1338) | VV1 - VV2 | 28 | 1334 -1350-2213 (all BK1-BK2) | (b) | (b) |
| 4.2 |  | III | - | VV4 | 19 | 1376 (BK2) |  |  |
|  | 4.3 | III | - | VV4 | 1 |  |  |  |
| 4.3 |  | I | - | - | 1 |  |  |  |
|  |  | II | - | VV3 - VV5 - VV7 | 4 | 3170 (BK1-BK2) |  |  |
|  | 6.1 | II | - | - | 1 |  |  |  |
|  |  | III | - | VV1 - VV5 - VV7 | 10 | 2950 (BK2) - 3170 (BK1-BK2) |  |  |
|  | 4.2 | III | - | VV5 | 3 |  |  |  |
|  | 6.1 | III | x | VV1 | 1 | 1408 (BK2) |  |  |
| 5.1 |  | II | - -/x | VV8 | 25 | 1495 - 3378 (all BK1-BK2) | (b) | (b) |
|  | 6.1 | II | - | - | 2 |  |  |  |
|  |  | III | x | VV8 | 31 | 1438 - 1454 - 1474 - 1486 - 1498 - 1499 - 1942 - 2067 - 3377 - 3378 (all BK1-BK2) | (b) | (b) |
| 6.1 |  | II | x | VV10 | 1 | 3243 (BK1-BK2) |  |  |
|  |  | III | x (except UN 3249-3462) | VV9a - VV9b | 87 |  |  | (b) |
| 6.2 |  | - | - | - | 2 | 2900 (BK1-BK2) - 3291 (BK2) |  |  |
| 8 |  | II | x | VV9a - VV10 | 4 | 3244 (BK1-BK2) |  |  |
|  |  | III | x | VV9b | 34 |  |  | (b) |
|  |  | - | - | VV14 | 4 |  |  |  |
|  | 6.1 | III | x | VV9b | 1 |  |  | (b) |
| 9 |  | II | -/x | VV3 - VV15 | 3 | 2969 (BK1-BK2) |  |  |
|  |  | III | -/x | VV3 | 8 |  | (b) | (b) |

(a)	Current assignments of BK1 or BK2 to solid substances should be maintained

(b)	Assignment of BK1 and/or BK2 (marked b) is proposed to substances, listed in the Annex, with the following classification

- Class 4.1 – PG III: assign BK1 and BK2

- Class 5.1 – PG II – no subrisk: assign BK1 and BK2

- Class 5.1 – PG III: assign BK1 and BK2

- Class 6.1 – PG III: assign BK2

- Class 8 – PG III: assign BK2

- *Class 9 – PG III: assign BK1 and BK2 (limited to UN 1841-1931)

(c)	of BK1 and/or BK2 could be added to individual substances, not covered by a) or b), based on e.g. current assignments by IMO such as UN 1363, UN 1386, etc.

No indication for assignment is given in the table above for the moment.

10.	The proposed assignments per UN number can be found in the last column of the list in the Annex: they reflect both the maintenance of current assignments (see (a) above) as well as the proposed new assignments according to the rationalised approach (see (b)). No indication in the last column means that it is proposed not to assign a BK code for the moment to this substance, unless this could be justified (see (c)).

11.	ICCA is not requesting UNSCETDG to make a decision on the proposal at this meeting but invites comments from delegates, in order to allow ICCA to make a revised proposal at the December meeting, taking into account the comments made.

Justification

12.	There is no need to amend the current assignment of BK codes to substances, which are currently already allowed to be transported in bulk as they are permitted by the various regulations, as there is a demonstrated industry need for them and because of practical reasons e.g. UN 3175, UN 3243 and UN 3244 to deal with wastes following spillages.

13.	For those substances for which now the assignment of BK1 and/or BK2 is proposed, it is believed that the extension to similar substances of the same class can be made because their carriage in bulk containers is generally already allowed in land modes whereby

      - The provisions for the use of bulk containers (Chapter 4.3 of UN Model Regulations) are adequately covered by the special provisions VVx/WWx of ADR/RID (Chapter 7.3 of ADR/RID) and to a large extent also CFR 49;

      - The requirements for the design, construction, inspection and testing of bulk containers (Chapter 6.8 of the UN Model Regulations), nearly integrally taken over by ADR/RID (Chapter 6.11) and IMDG (Chapter 6.9) remain applicable.

14.	Therefore ICCA is of the opinion that the list of solid substances, transported in bulk containers, could be extended in a rationalised way, without jeopardising safety.

* * * * *

Annex 1 (ENGLISH ONLY)

| Provisions for bulk transport of solids in UN - ADR - CFR 49 - IMO |
| --- |
| UN Model Regulations | ADR | CFR 49 | IMO IMDG Code | IMO BC Code | Propo-sal |
| UN No. | Name and description | Class or division | Subsi diary risk | Packing group | Portable tanks and bulk containers |  |  |  |  |  |
|  |  |  |  |  | Instruc-tions | Special provisions | Bulk Special prov (7.3.3) | Bulk (173. 240) | BK2 | Group |  |
| (1) | (2) | (3) | (4) | (5) | (10) | (11) |  |  |  |  |  |
| 3175 | SOLIDS CONTAINING FLAMMABLE LIQUID, N.O.S. | 4.1 |  | II | T3 BK1 BK2 | TP33 | VV3 | X | BK2 |  | BK1 BK2 |
| 1309 | ALUMINIUM POWDER, COATED | 4.1 |  | III | T1 | TP33 | VV1 | X |  |  | BK1 BK2 |
| 1312 | BORNEOL | 4.1 |  | III | T1 | TP33 | VV1 | X |  |  | BK1 BK2 |
| 1313 | CALCIUM RESINATE | 4.1 |  | III | T1 | TP33 | VV1 | X |  |  | BK1 BK2 |
| 1314 | CALCIUM RESINATE, FUSED | 4.1 |  | III | T1 | TP33 | VV1 | X |  |  | BK1 BK2 |
| 1318 | COBALT RESINATE, PRECIPITATED | 4.1 |  | III | T1 | TP33 | VV1 | X |  |  | BK1 BK2 |
| 1325 | FLAMMABLE SOLID, ORGANIC, N.O.S. | 4.1 |  | III | T1 | TP33 | VV1 | X |  |  | BK1 BK2 |
| 1328 | HEXAMETHYLENE-TETRAMINE | 4.1 |  | III | T1 | TP33 | VV1 | X |  |  | BK1 BK2 |
| 1330 | MANGANESE RESINATE | 4.1 |  | III | T1 | TP33 | VV1 | X |  |  | BK1 BK2 |
| 1332 | METALDEHYDE | 4.1 |  | III | T1 | TP33 | VV1 | X |  |  | BK1 BK2 |
| 1334 | NAPHTHALENE, CRUDE or NAPHTHALENE, REFINED | 4.1 |  | III | T1 BK1 BK2 | TP33 | VV2 | X | BK2 |  | BK1 BK2 |
| 1338 | PHOSPHORUS, AMORPHOUS | 4.1 |  | III | T1 | TP33 | VV1 | - |  |  | BK1 BK2 |
| 1346 | SILICON POWDER, AMORPHOUS | 4.1 |  | III | T1 | TP33 | VV1 | X |  |  | BK1 BK2 |
| 1350 | SULPHUR | 4.1 |  | III | T1 BK1 BK2 | TP33 | VV1 | X | BK2 | B | BK1 BK2 |
| 1869 | MAGNESIUM or MAGNESIUM ALLOYS with more than 50% magnesium in pellets, turnings or ribbons | 4.1 |  | III | T1 | TP33 | VV1 | X |  |  | BK1 BK2 |
| 2001 | COBALT NAPHTHENATES, POWDER | 4.1 |  | III | T1 | TP33 | VV1 | X |  |  | BK1 BK2 |
| 2213 | PARAFORM-ALDEHYDE | 4.1 |  | III | T1 BK1 BK2 | TP33 | VV1 | X | BK2 |  | BK1 BK2 |
| 2538 | NITRONAPHTHALENE | 4.1 |  | III | T1 | TP33 | VV1 | X |  |  | BK1 BK2 |
| 2687 | DICYCLOHEXYL-AMMONIUM NITRITE | 4.1 |  | III | T1 | TP33 | VV1 | X |  |  | BK1 BK2 |
| 2714 | ZINC RESINATE | 4.1 |  | III | T1 | TP33 | VV1 | X |  |  | BK1 BK2 |
| 2715 | ALUMINIUM RESINATE | 4.1 |  | III | T1 | TP33 | VV1 | X |  |  | BK1 BK2 |
| 2717 | CAMPHOR, synthetic | 4.1 |  | III | T1 | TP33 | VV1 | X |  |  | BK1 BK2 |
| 2858 | ZIRCONIUM, DRY, coiled wire, finished metal sheets, strip (thinner than 254 microns but not thinner than 18 microns) | 4.1 |  | III |  |  | VV1 | X |  |  | BK1 BK2 |
| 2878 | TITANIUM SPONGE GRANULES or TITANIUM SPONGE POWDERS | 4.1 |  | III | T1 | TP33 | VV1 | X |  |  | BK1 BK2 |
| 2989 | LEAD PHOSPHITE, DIBASIC | 4.1 |  | III | T1 | TP33 | VV1 | X |  |  | BK1 BK2 |
| 3089 | METAL POWDER, FLAMMABLE, N.O.S. | 4.1 |  | III | T1 | TP33 | VV1 | X |  |  | BK1 BK2 |
| 3178 | FLAMMABLE SOLID, INORGANIC, N.O.S. | 4.1 |  | III | T1 | TP33 | VV1 | X |  |  | BK1 BK2 |
| 3181 | METAL SALTS OF ORGANIC COMPOUNDS, FLAMMABLE, N.O.S. | 4.1 |  | III | T1 | TP33 | VV1 | X |  |  | BK1 BK2 |
| 3182 | METAL HYDRIDES, FLAMMABLE, N.O.S. | 4.1 |  | III | T1 | TP33 | VV1 | X |  |  | BK1 BK2 |
| 1361 | CARBON, animal or vegetable origin | 4.2 |  | III | T1 | TP33 | VV4 | - |  |  |  |
| 1362 | CARBON, ACTIVATED | 4.2 |  | III | T1 | TP33 | VV4 | - |  |  |  |
| 1363 | COPRA | 4.2 |  | III |  |  | VV4 | - | BK2 | B |  |
| 1364 | COTTON WASTE, OILY | 4.2 |  | III |  |  | VV4 | - |  |  |  |
| 1365 | COTTON, WET | 4.2 |  | III |  |  | VV4 | - |  |  |  |
| 1373 | FIBRES or FABRICS, ANIMAL or VEGE-TABLE or SYNTHETIC, N.O.S. with oil | 4.2 |  | III | T1 | TP33 | VV4 | - |  |  |  |
| 1376 | IRON OXIDE, SPENT or IRON SPONGE, SPENT obtained from coal gas purification | 4.2 |  | III | T1 BK2 | TP33 | VV4 | X | BK2 | B | BK2 |
| 1379 | PAPER, UNSATURATED OIL TREATED, incompletely dried (including carbon paper) | 4.2 |  | III |  |  | VV4 | - |  |  |  |
| 1386 | SEED CAKE with more than 1.5% oil and not more than 11% moisture | 4.2 |  | III |  |  | VV4 | - | BK2 | B |  |
| 1932 | ZIRCONIUM SCRAP | 4.2 |  | III | T1 | TP33 | VV4 | X |  |  |  |
| 2008 | ZIRCONIUM POWDER, DRY | 4.2 |  | III | T1 | TP33 | VV4 | - |  |  |  |
| 2009 | ZIRCONIUM, DRY, finished sheets, strip or coiled wire | 4.2 |  | III |  |  | VV4 | X |  |  |  |
| 2210 | MANEB or MANEB PREPARATION with not less than 60% maneb | 4.2 | 4.3 | III | T1 | TP33 | VV4 | - |  |  |  |
| 2217 | SEED CAKE with not more than 1.5% oil and not more than 11% moisture | 4.2 |  | III |  |  | VV4 | - | BK2 | B |  |
| 2545 | HAFNIUM POWDER, DRY | 4.2 |  | III | T1 | TP33 | VV4 | - |  |  |  |
| 2546 | TITANIUM POWDER, DRY | 4.2 |  | III | T1 | TP33 | VV4 | - |  |  |  |
| 2793 | FERROUS METAL BORINGS, SHAVINGS, TURNINGS or CUTTINGS in a form liable to self-heating | 4.2 |  | III |  |  | VV4 | - | BK2 | B |  |
| 2881 | METAL CATALYST, DRY | 4.2 |  | III | T1 | TP33 | VV4 | - |  |  |  |
| 3189 | METAL POWDER, SELF-HEATING, N.O.S. | 4.2 |  | III | T1 | TP33 | VV4 | - |  |  |  |
| 3190 | SELF-HEATING SOLID, INORGANIC, N.O.S. | 4.2 |  | III | T1 | TP33 | VV4 | - |  |  |  |
| 1402 | CALCIUM CARBIDE | 4.3 |  | I | T9 | TP7 TP33 | - | - | BK2 |  |  |
| 1394 | ALUMINIUM CARBIDE | 4.3 |  | II | T3 | TP33 | VV5 | - |  |  |  |
| 1395 | ALUMINIUM FERROSILICON POWDER | 4.3 | 6.1 | II | T3 | TP33 | - | - | BK2 | B |  |
| 1402 | CALCIUM CARBIDE | 4.3 |  | II | T3 | TP33 | VV5 | - | BK2 |  |  |
| 1405 | CALCIUM SILICIDE | 4.3 |  | II | T3 | TP33 | VV7 | - |  |  |  |
| 3170 | ALUMINIUM SMELTING BY-PRODUCTS or ALUMINIUM REMELTING BY-PRODUCTS | 4.3 |  | II | T3 BK1 BK2 | TP33 | VV3 | - | BK2 | B | BK1 BK2 |
| 1396 | ALUMINIUM POWDER, UNCOATED | 4.3 |  | III | T1 | TP33 | VV5 | - |  |  |  |
| 1398 | ALUMINIUM SILICON POWDER, UNCOATED | 4.3 |  | III | T1 | TP33 | VV5 | - | BK2 | B |  |
| 1405 | CALCIUM SILICIDE | 4.3 |  | III | T1 | TP33 | VV5 VV7 | - |  |  |  |
| 1408 | FERROSILICON with 30% or more but less than 90% silicon | 4.3 | 6.1 | III | T1 BK2 | TP33 | VV1 | X | BK2 | B | BK2 |
| 1418 | MAGNESIUM POWDER or MAGNESIUM ALLOYS POWDER | 4.3 | 4.2 | III | T1 | TP33 | VV5 | - |  |  |  |
| 1435 | ZINC ASHES | 4.3 |  | III | T1 | TP33 | VV5 | - | BK2 | B |  |
| 1436 | ZINC POWDER or ZINC DUST | 4.3 | 4.2 | III | T1 | TP33 | VV5 | - |  |  |  |
| 2813 | WATER-REACTIVE SOLID, N.O.S. | 4.3 |  | III | T1 | TP33 | VV5 | - |  |  |  |
| 2844 | CALCIUM MANGANESE SILICON | 4.3 |  | III | T1 | TP33 | VV5 VV7 | - |  |  |  |
| 2950 | MAGNESIUM GRANULES, COATED, particle size not less than 149 microns | 4.3 |  | III | T1 BK2 | TP33 | VV5 | X | BK2 |  | BK2 |
| 2968 | MANEB, STABILIZED or MANEB PREPARATION, STABILIZED against self-heating | 4.3 |  | III | T1 | TP33 | VV5 | - |  |  |  |
| 3170 | ALUMINIUM SMELTING BY-PRODUCTS or ALUMINIUM REMELTING BY-PRODUCTS | 4.3 |  | III | T1 BK1 BK2 | TP33 | VV1 VV5 | - | BK2 | B | BK1 BK2 |
| 3208 | METALLIC SUBSTANCE, WATER-REACTIVE, N.O.S. | 4.3 |  | III | T1 | TP33 | VV5 | - |  |  |  |
| 3209 | METALLIC SUBSTANCE, WATER-REACTIVE, SELF-HEATING, N.O.S. | 4.3 | 4.2 | III | T1 | TP33 | VV5 | - |  |  |  |
| 1442 | AMMONIUM PERCHLORATE | 5.1 |  | II | T3 | TP33 | VV8 | - |  |  | BK1 BK2 |
| 1446 | BARIUM NITRATE | 5.1 | 6.1 | II | T3 | TP33 | - | - | BK2 | B |  |
| 1450 | BROMATES, INORGANIC, N.O.S. | 5.1 |  | II | T3 | TP33 | VV8 | - |  |  | BK1 BK2 |
| 1452 | CALCIUM CHLORATE | 5.1 |  | II | T3 | TP33 | VV8 | - |  |  | BK1 BK2 |
| 1455 | CALCIUM PERCHLORATE | 5.1 |  | II | T3 | TP33 | VV8 | - |  |  | BK1 BK2 |
| 1458 | CHLORATE AND BORATE MIXTURE | 5.1 |  | II | T3 | TP33 | VV8 | X |  |  | BK1 BK2 |
| 1459 | CHLORATE AND MAGNESIUM CHLORIDE MIXTURE, SOLID | 5.1 |  | II | T3 | TP33 | VV8 | X |  |  | BK1 BK2 |
| 1461 | CHLORATES, INORGANIC, N.O.S. | 5.1 |  | II | T3 | TP33 | VV8 | - |  |  | BK1 BK2 |
| 1469 | LEAD NITRATE | 5.1 | 6.1 | II | T3 | TP33 | - | - | BK2 | B |  |
| 1473 | MAGNESIUM BROMATE | 5.1 |  | II | T3 | TP33 | VV8 | - |  |  | BK1 BK2 |
| 1475 | MAGNESIUM PERCHLORATE | 5.1 |  | II | T3 | TP33 | VV8 | - |  |  | BK1 BK2 |
| 1481 | PERCHLORATES, INORGANIC, N.O.S. | 5.1 |  | II | T3 | TP33 | VV8 | - |  |  | BK1 BK2 |
| 1484 | POTASSIUM BROMATE | 5.1 |  | II | T3 | TP33 | VV8 | - |  |  | BK1 BK2 |
| 1485 | POTASSIUM CHLORATE | 5.1 |  | II | T3 | TP33 | VV8 | - | BK2 |  | BK1 BK2 |
| 1487 | POTASSIUM NITRATE AND SODIUM NITRITE MIXTURE | 5.1 |  | II | T3 | TP33 | VV8 | X |  |  | BK1 BK2 |
| 1488 | POTASSIUM NITRITE | 5.1 |  | II | T3 | TP33 | VV8 | - |  |  | BK1 BK2 |
| 1489 | POTASSIUM PERCHLORATE | 5.1 |  | II | T3 | TP33 | VV8 | - |  |  | BK1 BK2 |
| 1493 | SILVER NITRATE | 5.1 |  | II | T3 | TP33 | VV8 | - |  |  | BK1 BK2 |
| 1494 | SODIUM BROMATE | 5.1 |  | II | T3 | TP33 | VV8 | - |  |  | BK1 BK2 |
| 1495 | SODIUM CHLORATE | 5.1 |  | II | T3 BK1 BK2 | TP33 | VV8 | X | BK2 |  | BK1 BK2 |
| 1502 | SODIUM PERCHLORATE | 5.1 |  | II | T3 | TP33 | VV8 | - |  |  | BK1 BK2 |
| 1506 | STRONTIUM CHLORATE | 5.1 |  | II | T3 | TP33 | VV8 | - |  |  | BK1 BK2 |
| 1508 | STRONTIUM PERCHLORATE | 5.1 |  | II | T3 | TP33 | VV8 | - |  |  | BK1 BK2 |
| 1513 | ZINC CHLORATE | 5.1 |  | II | T3 | TP33 | VV8 | - |  |  | BK1 BK2 |
| 2721 | COPPER CHLORATE | 5.1 |  | II | T3 | TP33 | VV8 | - |  |  | BK1 BK2 |
| 2723 | MAGNESIUM CHLORATE | 5.1 |  | II | T3 | TP33 | VV8 | - |  |  | BK1 BK2 |
| 3378 | SODIUM CARBONATE PEROXYHYDRATE | 5.1 |  | II | T3 BK1 BK2 | TP33 | VV8 | X | BK2 |  | BK1 BK2 |
| 1438 | ALUMINIUM NITRATE | 5.1 |  | III | T1 BK1 BK2 | TP33 | VV8 | X | BK2 | B | BK1 BK2 |
| 1444 | AMMONIUM PERSULPHATE | 5.1 |  | III | T1 | TP33 | VV8 | X |  |  | BK1 BK2 |
| 1451 | CAESIUM NITRATE | 5.1 |  | III | T1 | TP33 | VV8 | X |  |  | BK1 BK2 |
| 1454 | CALCIUM NITRATE | 5.1 |  | III | T1 BK1 BK2 | TP33 | VV8 | X | BK2 | B | BK1 BK2 |
| 1458 | CHLORATE AND BORATE MIXTURE | 5.1 |  | III | T1 | TP33 | VV8 | X |  |  | BK1 BK2 |
| 1459 | CHLORATE AND MAGNESIUM CHLORIDE MIXTURE, SOLID | 5.1 |  | III | T1 | TP33 | VV8 | X |  |  | BK1 BK2 |
| 1465 | DIDYMIUM NITRATE | 5.1 |  | III | T1 | TP33 | VV8 | X |  |  | BK1 BK2 |
| 1466 | FERRIC NITRATE | 5.1 |  | III | T1 | TP33 | VV8 | X |  |  | BK1 BK2 |
| 1467 | GUANIDINE NITRATE | 5.1 |  | III | T1 | TP33 | VV8 | X |  |  | BK1 BK2 |
| 1474 | MAGNESIUM NITRATE | 5.1 |  | III | T1 BK1 BK2 | TP33 | VV8 | X | BK2 | B | BK1 BK2 |
| 1477 | NITRATES, INORGANIC, N.O.S. | 5.1 |  | III | T1 | TP33 | VV8 | X |  |  | BK1 BK2 |
| 1481 | PERCHLORATES, INORGANIC, N.O.S. | 5.1 |  | III | T1 | TP33 | VV8 | X |  |  | BK1 BK2 |
| 1486 | POTASSIUM NITRATE | 5.1 |  | III | T1 BK1 BK2 | TP33 | VV8 | X | BK2 | B | BK1 BK2 |
| 1492 | POTASSIUM PERSULPHATE | 5.1 |  | III | T1 | TP33 | VV8 | X |  |  | BK1 BK2 |
| 1498 | SODIUM NITRATE | 5.1 |  | III | T1 BK1 BK2 | TP33 | VV8 | X | BK2 | B | BK1 BK2 |
| 1499 | SODIUM NITRATE AND POTASSIUM NITRATE MIXTURE | 5.1 |  | III | T1 BK1 BK2 | TP33 | VV8 | X | BK2 | B | BK1 BK2 |
| 1505 | SODIUM PERSULPHATE | 5.1 |  | III | T1 | TP33 | VV8 | X |  |  | BK1 BK2 |
| 1507 | STRONTIUM NITRATE | 5.1 |  | III | T1 | TP33 | VV8 | X |  |  | BK1 BK2 |
| 1942 | AMMONIUM NITRATE with not more than 0.2% total combustible material, including any organic substance calculated as carbon, to the exclusion of any other added substance | 5.1 |  | III | T1 BK1 BK2 | TP33 | VV8 | X | BK2 | B | BK1 BK2 |
| 2067 | AMMONIUM NITRATE BASED FERTILIZER | 5.1 |  | III | T1 BK1 BK2 | TP33 | VV8 | X | BK2 | B | BK1 BK2 |
| 2469 | ZINC BROMATE | 5.1 |  | III | T1 | TP33 | VV8 | X |  |  | BK1 BK2 |
| 2720 | CHROMIUM NITRATE | 5.1 |  | III | T1 | TP33 | VV8 | X |  |  | BK1 BK2 |
| 2722 | LITHIUM NITRATE | 5.1 |  | III | T1 | TP33 | VV8 | X |  |  | BK1 BK2 |
| 2724 | MANGANESE NITRATE | 5.1 |  | III | T1 | TP33 | VV8 | X |  |  | BK1 BK2 |
| 2725 | NICKEL NITRATE | 5.1 |  | III | T1 | TP33 | VV8 | X |  |  | BK1 BK2 |
| 2726 | NICKEL NITRITE | 5.1 |  | III | T1 | TP33 | VV8 | X |  |  | BK1 BK2 |
| 2728 | ZIRCONIUM NITRATE | 5.1 |  | III | T1 | TP33 | VV8 | X |  |  | BK1 BK2 |
| 2880 | CALCIUM HYPOCHLORITE, HYDRATED, or CALCIUM HYPOCHLORITE, HYDRATED MIXTURE, with not less than 5.5% but not more than 16% water | 5.1 |  | III |  |  | VV8 | X |  |  | BK1 BK2 |
| 3215 | PERSULPHATES, INORGANIC, N.O.S. | 5.1 |  | III | T1 | TP33 | VV8 | X |  |  | BK1 BK2 |
| 3377 | SODIUM PERBORATE MONOHYDRATE | 5.1 |  | III | T1 BK1 BK2 | TP33 | VV8 | X | BK2 |  | BK1 BK2 |
| 3378 | SODIUM CARBONATE PEROXYHYDRATE | 5.1 |  | III | T1 BK1 BK2 | TP33 | VV8 | X | BK2 |  | BK1 BK2 |
| 3243 | SOLIDS CONTAINING TOXIC LIQUID, N.O.S. | 6.1 |  | II | T3 BK1 BK2 | TP33 | VV10 | X | BK2 |  | BK1 BK2 |
| 1544 | ALKALOIDS, SOLID, N.O.S. or ALKALOID SALTS, SOLID, N.O.S. | 6.1 |  | III | T1 | TP33 | VV9b | X |  |  | BK2 |
| 1548 | ANILINE HYDROCHLORIDE | 6.1 |  | III | T1 | TP33 | VV9b | X |  |  | BK2 |
| 1549 | ANTIMONY COMPOUND, INORGANIC, SOLID, N.O.S. | 6.1 |  | III | T1 | TP33 | VV9b | X |  |  | BK2 |
| 1550 | ANTIMONY LACTATE | 6.1 |  | III | T1 | TP33 | VV9b | X |  |  | BK2 |
| 1551 | ANTIMONY POTASSIUM TARTRATE | 6.1 |  | III | T1 | TP33 | VV9b | X |  |  | BK2 |
| 1557 | ARSENIC COMPOUND, SOLID, N.O.S., inorganic, including: Arsenates, n.o.s.; Arsenites, n.o.s.; and Arsenic sulphides, n.o.s. | 6.1 |  | III | T1 | TP33 | VV9b | X |  |  | BK2 |
| 1564 | BARIUM COMPOUND, N.O.S. | 6.1 |  | III | T1 | TP33 | VV9a | X |  |  | BK2 |
| 1566 | BERYLLIUM COMPOUND, N.O.S. | 6.1 |  | III | T1 | TP33 | VV9b | X |  |  | BK2 |
| 1579 | 4-CHLORO-o-TOLUIDINE HYDROCHLORIDE, SOLID | 6.1 |  | III | T1 | TP33 | VV9b | X |  |  | BK2 |
| 1588 | CYANIDES, INORGANIC, SOLID, N.O.S. | 6.1 |  | III | T1 | TP33 | VV9b | X |  |  | BK2 |
| 1601 | DISINFECTANT, SOLID, TOXIC, N.O.S. | 6.1 |  | III | T1 | TP33 | VV9b | X |  |  | BK2 |
| 1616 | LEAD ACETATE | 6.1 |  | III | T1 | TP33 | VV9b | X |  |  | BK2 |
| 1655 | NICOTINE COMPOUND, SOLID, N.O.S. or NICOTINE PREPARATION, SOLID, N.O.S. | 6.1 |  | III | T1 | TP33 | VV9b | X |  |  | BK2 |
| 1663 | NITROPHENOLS (o-, m-, p-) | 6.1 |  | III | T1 | TP33 | VV9b | X |  |  | BK2 |
| 1673 | PHENYLENE-DIAMINES (o-, m-, p-) | 6.1 |  | III | T1 | TP33 | VV9b | X |  |  | BK2 |
| 1690 | SODIUM FLUORIDE, SOLID | 6.1 |  | III | T1 | TP33 | VV9b | X |  |  | BK2 |
| 1709 | 2,4-TOLUYLENE-DIAMINE, SOLID | 6.1 |  | III | T1 | TP33 | VV9b | X |  |  | BK2 |
| 1812 | POTASSIUM FLUORIDE, SOLID | 6.1 |  | III | T1 | TP33 | VV9b | X |  |  | BK2 |
| 1884 | BARIUM OXIDE | 6.1 |  | III | T1 | TP33 | VV9a | X |  |  | BK2 |
| 2020 | CHLOROPHENOLS, SOLID | 6.1 |  | III | T1 | TP33 | VV9b | X |  |  | BK2 |
| 2025 | MERCURY COMPOUND, SOLID, N.O.S. | 6.1 |  | III | T1 | TP33 | VV9b | X |  |  | BK2 |
| 2026 | PHENYLMERCURIC COMPOUND, N.O.S. | 6.1 |  | III | T1 | TP33 | VV9b | X |  |  | BK2 |
| 2074 | ACRYLAMIDE, SOLID | 6.1 |  | III | T1 | TP33 | VV9b | X |  |  | BK2 |
| 2077 | alpha-NAPHTHYLAMINE | 6.1 |  | III | T1 | TP33 | VV9b | X |  |  | BK2 |
| 2233 | CHLOROANISIDINES | 6.1 |  | III | T1 | TP33 | VV9b | X |  |  | BK2 |
| 2237 | CHLORONITRO-ANILINES | 6.1 |  | III | T1 | TP33 | VV9b | X |  |  | BK2 |
| 2239 | CHLOROTOLUIDINES, SOLID | 6.1 |  | III | T1 | TP33 | VV9b | X |  |  | BK2 |
| 2291 | LEAD COMPOUND, SOLUBLE, N.O.S. | 6.1 |  | III | T1 | TP33 | VV9b | X |  |  | BK2 |
| 2446 | NITROCRESOLS, SOLID | 6.1 |  | III | T1 | TP33 | VV9b | X |  |  | BK2 |
| 2473 | SODIUM ARSANILATE | 6.1 |  | III | T1 | TP33 | VV9b | X |  |  | BK2 |
| 2505 | AMMONIUM FLUORIDE | 6.1 |  | III | T1 | TP33 | VV9b | X |  |  | BK2 |
| 2512 | AMINOPHENOLS (o-, m-, p-) | 6.1 |  | III | T1 | TP33 | VV9b | X |  |  | BK2 |
| 2516 | CARBON TETRABROMIDE | 6.1 |  | III | T1 | TP33 | VV9b | X |  |  | BK2 |
| 2570 | CADMIUM COMPOUND | 6.1 |  | III | T1 | TP33 | VV9b | X |  |  | BK2 |
| 2588 | PESTICIDE, SOLID, TOXIC, N.O.S. | 6.1 |  | III | T1 | TP33 | VV9b | X |  |  | BK2 |
| 2651 | 4,4'-DIAMINO-DIPHENYL-METHANE | 6.1 |  | III | T1 | TP33 | VV9b | X |  |  | BK2 |
| 2655 | POTASSIUM FLUOROSILICATE | 6.1 |  | III | T1 | TP33 | VV9b | X |  |  | BK2 |
| 2659 | SODIUM CHLOROACETATE | 6.1 |  | III | T1 | TP33 | VV9b | X |  |  | BK2 |
| 2660 | NITROTOLUIDINES (MONO) | 6.1 |  | III | T1 | TP33 | VV9b | X |  |  | BK2 |
| 2662 | HYDROQUINONE, SOLID | 6.1 |  | III | T1 | TP33 | VV9b | X |  |  | BK2 |
| 2674 | SODIUM FLUOROSILICATE | 6.1 |  | III | T1 | TP33 | VV9b | X |  |  | BK2 |
| 2713 | ACRIDINE | 6.1 |  | III | T1 | TP33 | VV9b | X |  |  | BK2 |
| 2716 | 1,4-BUTYNEDIOL | 6.1 |  | III | T1 | TP33 | VV9b | X |  |  | BK2 |
| 2729 | HEXACHLOROBENZENE | 6.1 |  | III | T1 | TP33 | VV9b | X |  |  | BK2 |
| 2757 | CARBAMATE PESTICIDE, SOLID, TOXIC | 6.1 |  | III | T1 | TP33 | VV9b | X |  |  | BK2 |
| 2759 | ARSENICAL PESTICIDE, SOLID, TOXIC | 6.1 |  | III | T1 | TP33 | VV9b | X |  |  | BK2 |
| 2761 | ORGANOCHLORINE PESTICIDE, SOLID, TOXIC | 6.1 |  | III | T1 | TP33 | VV9b | X |  |  | BK2 |
| 2763 | TRIAZINE PESTICIDE, SOLID, TOXIC | 6.1 |  | III | T1 | TP33 | VV9b | X |  |  | BK2 |
| 2771 | THIOCARBAMATE PESTICIDE, SOLID, TOXIC | 6.1 |  | III | T1 | TP33 | VV9b | X |  |  | BK2 |
| 2775 | COPPER BASED PESTICIDE, SOLID, TOXIC | 6.1 |  | III | T1 | TP33 | VV9b | X |  |  | BK2 |
| 2777 | MERCURY BASED PESTICIDE, SOLID, TOXIC | 6.1 |  | III | T1 | TP33 | VV9b | X |  |  | BK2 |
| 2779 | SUBSTITUTED NITROPHENOL PESTICIDE, SOLID, TOXIC | 6.1 |  | III | T1 | TP33 | VV9b | X |  |  | BK2 |
| 2781 | BIPYRIDILIUM PESTICIDE, SOLID, TOXIC | 6.1 |  | III | T1 | TP33 | VV9b | X |  |  | BK2 |
| 2783 | ORGANOPHOS-PHORUS PESTICIDE, SOLID, TOXIC | 6.1 |  | III | T1 | TP33 | VV9b | X |  |  | BK2 |
| 2786 | ORGANOTIN PESTICIDE, SOLID, TOXIC | 6.1 |  | III | T1 | TP33 | VV9b | X |  |  | BK2 |
| 2811 | TOXIC SOLID, ORGANIC, N.O.S. | 6.1 |  | III | T1 | TP33 | VV9b | X |  |  | BK2 |
| 2853 | MAGNESIUM FLUOROSILICATE | 6.1 |  | III | T1 | TP33 | VV9b | X |  |  | BK2 |
| 2854 | AMMONIUM FLUOROSILICATE | 6.1 |  | III | T1 | TP33 | VV9b | X |  |  | BK2 |
| 2855 | ZINC FLUOROSILICATE | 6.1 |  | III | T1 | TP33 | VV9b | X |  |  | BK2 |
| 2856 | FLUOROSILICATES, N.O.S. | 6.1 |  | III | T1 | TP33 | VV9b | X |  |  | BK2 |
| 2862 | VANADIUM PENTOXIDE, non-fused form | 6.1 |  | III | T1 | TP33 | VV9b | X |  |  | BK2 |
| 2871 | ANTIMONY POWDER | 6.1 |  | III | T1 | TP33 | VV9b | X |  |  | BK2 |
| 2875 | HEXACHLOROPHENE | 6.1 |  | III | T1 | TP33 | VV9b | X |  |  | BK2 |
| 2876 | RESORCINOL | 6.1 |  | III | T1 | TP33 | VV9b | X |  |  | BK2 |
| 3027 | COUMARIN DERIVATIVE PESTICIDE, SOLID, TOXIC | 6.1 |  | III | T1 | TP33 | VV9b | X |  |  | BK2 |
| 3143 | DYE, SOLID, TOXIC, N.O.S. or DYE INTERMEDIATE, SOLID, TOXIC, N.O.S. | 6.1 |  | III | T1 | TP33 | VV9b | X |  |  | BK2 |
| 3146 | ORGANOTIN COMPOUND, SOLID, N.O.S. | 6.1 |  | III | T1 | TP33 | VV9b | X |  |  | BK2 |
| 3249 | MEDICINE, SOLID, TOXIC, N.O.S. | 6.1 |  | III | T1 | TP33 | VV9b | - |  |  | BK2 |
| 3283 | SELENIUM COMPOUND, SOLID, N.O.S. | 6.1 |  | III | T1 | TP33 | VV9b | X |  |  | BK2 |
| 3284 | TELLURIUM COMPOUND, N.O.S. | 6.1 |  | III | T1 | TP33 | VV9b | X |  |  | BK2 |
| 3285 | VANADIUM COMPOUND, N.O.S. | 6.1 |  | III | T1 | TP33 | VV9b | X |  |  | BK2 |
| 3288 | TOXIC SOLID, INORGANIC, N.O.S. | 6.1 |  | III | T1 | TP33 | VV9b | X |  |  | BK2 |
| 3345 | PHENOXYACETIC ACID DERIVATIVE PESTICIDE, SOLID, TOXIC | 6.1 |  | III | T1 | TP33 | VV9b | X |  |  | BK2 |
| 3349 | PYRETHROID PESTICIDE, SOLID, TOXIC | 6.1 |  | III | T1 | TP33 | VV9b | X |  |  | BK2 |
| 3427 | CHLOROBENZYL CHLORIDES, SOLID | 6.1 |  | III | T1 | TP33 | VV9b | X |  |  | BK2 |
| 3438 | alpha-METHYLBENZYL ALCOHOL, SOLID | 6.1 |  | III | T1 | TP33 | VV9b | X |  |  | BK2 |
| 3439 | NITRILES, TOXIC, SOLID, N.O.S. | 6.1 |  | III | T1 | TP33 | VV9b | X |  |  | BK2 |
| 3457 | CHLORONITRO-TOLUENES, SOLID | 6.1 |  | III | T1 | TP33 | VV9b | X |  |  | BK2 |
| 3458 | NITROANISOLES, SOLID | 6.1 |  | III | T1 | TP33 | VV9b | X |  |  | BK2 |
| 3459 | NITROBROMO-BENZENES, SOLID | 6.1 |  | III | T1 | TP33 | VV9b | X |  |  | BK2 |
| 3460 | N-ETHYLBENZYL-TOLUIDINES, SOLID | 6.1 |  | III | T1 | TP33 | VV9b | X |  |  | BK2 |
| 3462 | TOXINS, EXTRACTED FROM LIVING SOURCES, SOLID, N.O.S. | 6.1 |  | III | T1 | TP33 | VV9b | - |  |  | BK2 |
| 3464 | ORGANOPHOS-PHORUS COMPOUND, TOXIC, SOLID, N.O.S. | 6.1 |  | III | T1 | TP33 | VV9b | X |  |  | BK2 |
| 3465 | ORGANOARSENIC COMPOUND, SOLID, N.O.S. | 6.1 |  | III | T1 | TP33 | VV9b | X |  |  | BK2 |
| 3466 | METAL CARBONYLS, SOLID, N.O.S. | 6.1 |  | III | T1 | TP33 | VV9b | X |  |  | BK2 |
| 3467 | ORGANOMETALLIC COMPOUND, TOXIC, SOLID, N.O.S. | 6.1 |  | III | T1 | TP33 | VV9b | X |  |  | BK2 |
| 3291 | CLINICAL WASTE, UNSPECIFIED, N.O.S. or (BIO) MEDICAL WASTE, N.O.S. or REGULATED MEDICAL WASTE, N.O.S. | 6.2 |  | II | BK2 (in ADR in 2007) |  | VV11 | - |  |  | BK2 |
| 2900 | INFECTIOUS SUBSTANCE, AFFECTING ANIMALS only | 6.2 |  |  | BK1 BK2 |  | - | - | BK2 |  | BK1 BK2 |
| 1794 | LEAD SULPHATE with more than 3% free acid | 8 |  | II | T3 | TP33 | VV9a | X |  |  |  |
| 2506 | AMMONIUM HYDROGEN SULPHATE | 8 |  | II | T3 | TP33 | VV9a | X |  |  |  |
| 2509 | POTASSIUM HYDROGEN SULPHATE | 8 |  | II | T3 | TP33 | VV9a | X |  |  |  |
| 3244 | SOLIDS CONTAINING CORROSIVE LIQUID, N.O.S. | 8 |  | II | T3 BK1 BK2 | TP33 | VV10 | X | BK2 |  | BK1 BK2 |
| 1740 | HYDROGENDI-FLUORIDES, N.O.S. | 8 |  | III | T1 | TP33 | VV9b | X |  |  | BK2 |
| 1759 | CORROSIVE SOLID, N.O.S. | 8 |  | III | T1 | TP33 | VV9b | X |  |  | BK2 |
| 1773 | FERRIC CHLORIDE, ANHYDROUS | 8 |  | III | T1 | TP33 | VV9b | X |  |  | BK2 |
| 1907 | SODA LIME with more than 4% sodium hydroxide | 8 |  | III | T1 | TP33 | VV9b | X |  |  | BK2 |
| 2214 | PHTHALIC ANHYDRIDE with more than 0.05% of maleic anhydride | 8 |  | III | T1 | TP33 | VV9b | X |  |  | BK2 |
| 2215 | MALEIC ANHYDRIDE | 8 |  | III | T4 | TP1 | VV9b | X |  |  | BK2 |
| 2280 | HEXAMETHYLENE-DIAMINE, SOLID | 8 |  | III | T1 | TP33 | VV9b | X |  |  | BK2 |
| 2331 | ZINC CHLORIDE, ANHYDROUS | 8 |  | III | T1 | TP33 | VV9b | X |  |  | BK2 |
| 2430 | ALKYLPHENOLS, SOLID, N.O.S. (including C2-C12 homologues) | 8 |  | III | T1 | TP33 | VV9b | X |  |  | BK2 |
| 2440 | STANNIC CHLORIDE PENTAHYDRATE | 8 |  | III | T1 | TP33 | VV9b | X |  |  | BK2 |
| 2475 | VANADIUM TRICHLORIDE | 8 |  | III | T1 | TP33 | VV9b | X |  |  | BK2 |
| 2503 | ZIRCONIUM TETRACHLORIDE | 8 |  | III | T1 | TP33 | VV9b | X |  |  | BK2 |
| 2507 | CHLOROPLATINIC ACID, SOLID | 8 |  | III | T1 | TP33 | VV9b | X |  |  | BK2 |
| 2508 | MOLYBDENUM PENTACHLORIDE | 8 |  | III | T1 | TP33 | VV9b | X |  |  | BK2 |
| 2578 | PHOSPHORUS TRIOXIDE | 8 |  | III | T1 | TP33 | VV9b | X |  |  | BK2 |
| 2579 | PIPERAZINE | 8 |  | III | T1 | TP33 | VV9b | X |  |  | BK2 |
| 2585 | ALKYLSULPHONIC ACIDS, SOLID or ARYLSULPHONIC ACIDS, SOLID with not more than 5% free sulphuric acid | 8 |  | III | T1 | TP33 | VV9b | X |  |  | BK2 |
| 2698 | TETRAHYDRO-PHTHALIC ANHYDRIDES with more than 0.05% of maleic anhydride | 8 |  | III | T1 | TP33 | VV9b | X |  |  | BK2 |
| 2802 | COPPER CHLORIDE | 8 |  | III | T1 | TP33 | VV9b | X |  |  | BK2 |
| 2803 | GALLIUM | 8 |  | III |  |  | VV9b | X |  |  | BK2 |
| 2823 | CROTONIC ACID | 8 |  | III | T1 | TP33 | VV9b | X |  |  | BK2 |
| 2834 | PHOSPHOROUS ACID | 8 |  | III | T1 | TP33 | VV9b | X |  |  | BK2 |
| 2865 | HYDROXYLAMINE SULPHATE | 8 |  | III | T1 | TP33 | VV9b | X |  |  | BK2 |
| 2869 | TITANIUM TRICHLORIDE MIXTURE | 8 |  | III | T1 | TP33 | VV9b | X |  |  | BK2 |
| 2905 | CHLOROPHENO-LATES, SOLID or PHENOLATES, SOLID | 8 |  | III | T1 | TP33 | VV9b | X |  |  | BK2 |
| 2923 | CORROSIVE SOLID, TOXIC, N.O.S. | 8 | 6.1 | III | T1 | TP33 | VV9b | X |  |  | BK2 |
| 2967 | SULPHAMIC ACID | 8 |  | III | T1 | TP33 | VV9b | X |  |  | BK2 |
| 3147 | DYE, SOLID, CORROSIVE, N.O.S. or DYE INTERMEDIATE, SOLID, CORROSIVE, N.O.S. | 8 |  | III | T1 | TP33 | VV9b | X |  |  | BK2 |
| 3253 | DISODIUM TRIOXOSILICATE | 8 |  | III | T1 | TP33 | VV9b | X |  |  | BK2 |
| 3259 | AMINES, SOLID, CORROSIVE, N.O.S. or POLYAMINES, SOLID, CORROSIVE, N.O.S. | 8 |  | III | T1 | TP33 | VV9b | X |  |  | BK2 |
| 3260 | CORROSIVE SOLID, ACIDIC, INORGANIC, N.O.S. | 8 |  | III | T1 | TP33 | VV9b | X |  |  | BK2 |
| 3261 | CORROSIVE SOLID, ACIDIC, ORGANIC, N.O.S. | 8 |  | III | T1 | TP33 | VV9b | X |  |  | BK2 |
| 3262 | CORROSIVE SOLID, BASIC, INORGANIC, N.O.S. | 8 |  | III | T1 | TP33 | VV9b | X |  |  | BK2 |
| 3263 | CORROSIVE SOLID, BASIC, ORGANIC, N.O.S. | 8 |  | III | T1 | TP33 | VV9b | X |  |  | BK2 |
| 3453 | PHOSPHORIC ACID, SOLID | 8 |  | III | T1 | TP33 | VV9b | X |  |  | BK2 |
| 2794 | BATTERIES, WET, FILLED WITH ACID, electric storage | 8 |  |  |  |  | VV14 | - |  |  |  |
| 2795 | BATTERIES, WET, FILLED WITH ALKALI, electric storage | 8 |  |  |  |  | VV14 | - |  |  |  |
| 2800 | BATTERIES, WET, NON-SPILLABLE, electric storage | 8 |  |  |  |  | VV14 | - |  |  |  |
| 3028 | BATTERIES, DRY, CONTAINING POTASSIUM HYDROXIDE SOLID, electric storage | 8 |  |  |  |  | VV14 | - |  |  |  |
| 2969 | CASTOR BEANS or CASTOR MEAL or CASTOR POMACE or CASTOR FLAKE | 9 |  | II | T3 BK1 BK2 | TP33 | VV3 | X | BK2 | B | BK1 BK2 |
| 3152 | POLYHALOGENATED BIPHENYLS, SOLID or POLYHALOGENATED TERPHENYLS, SOLID | 9 |  | II | T3 | TP33 | VV15 | - |  |  |  |
| 3432 | POLYCHLORINATED BIPHENYLS, SOLID | 9 |  | II | T3 | TP33 | VV15 | X |  |  |  |
| 1841 | ACETALDEHYDE AMMONIA | 9 |  | III | T1 | TP33 | VV3 | X |  |  | BK1 BK2 |
| 1931 | ZINC DITHIONITE (ZINC HYDROSULPHITE) | 9 |  | III | T1 | TP33 | VV3 | X |  |  | BK1 BK2 |
| 2071 | AMMONIUM NITRATE BASED FERTILIZER | 9 |  | III |  |  | Not subject to ADR | X | BK2 | B |  |
| 2211 | POLYMERIC BEADS, EXPANDABLE, evolving flammable vapour | 9 |  | III | T1 | TP33 | VV3 | - | BK2 |  |  |
| 2216 | FISH MEAL (FISH SCRAP), STABILISED | 9 |  | III |  |  | Not subject to ADR | - | BK2 | B |  |
| 3077 | ENVIRONMENTALLY HAZARDOUS SUBSTANCE, SOLID, N.O.S. | 9 |  | III | T1 | TP33 | VV3 | X |  |  |  |
| 3258 | ELEVATED TEMPERATURE SOLID, N.O.S., at or above 240 °C | 9 |  | III |  |  | VV13 | - |  |  |  |
| 3314 | PLASTICS MOULDING COMPOUND in dough, sheet or extruded rope form evolving flammable vapour | 9 |  | III |  |  | VV3 | - |  |  |  |

Annex 2

## (ADR 2005) CHAPTER 7.3

## PROVISIONS CONCERNING CARRIAGE IN BULK

7.3.1	General provisions

7.3.1.1	Goods may not be carried in bulk in vehicles or containers unless:

(a)	either a special provision, identified by the code BK, explicitly authorizing this mode of carriage is indicated in column (10) of Table A of Chapter 3.2 and the relevant conditions of 7.3.2 are satisfied in addition to those of this section; or

(b)	a special provision, identified by the code VV, explicitly authorizing this mode of carriage is indicated in column (17) of Table A of Chapter 3.2 and the conditions of this special provision, as laid down in 7.3.3 are satisfied in addition to those of this section.

Nevertheless, empty packagings, uncleaned, may be carried in bulk if this mode of carriage is not explicitly prohibited by other provisions of ADR.

NOTE: 	For carriage in tanks, see Chapters 4.2 and 4.3.

7.3.1.2	Substances which may become liquid at temperatures likely to be encountered during carriage, are not permitted for carriage in bulk.

7.3.1.3	Containers or bodies of vehicles shall be siftproof and shall be so closed that none of the contents can escape under normal conditions of carriage including the effect of vibration, or by changes of temperature, humidity or pressure.

7.3.1.4	Bulk solids shall be loaded and evenly distributed in a manner that minimises movement that could result in damage to the container or vehicle or leakage of the dangerous goods.

7.3.1.5	Where venting devices are fitted they shall be kept clear and operable.

7.3.1.6	Bulk solids shall not react dangerously with the material of the container, vehicle, gaskets, equipment including lids and tarpaulins and with protective coatings which are in contact with the contents or significantly weaken them. Containers or vehicles shall be so constructed or adapted that the goods cannot penetrate between wooden floor coverings or come into contact with those parts of the container or vehicle that may be affected by the materials or residues thereof.

7.3.1.7	Before being filled and offered for carriage, each container or vehicle shall be inspected and cleaned to ensure that it does not contain any residue on the interior or exterior of the container or vehicle that could:

-	cause a dangerous reaction with the substance intended for carriage;

-	detrimentally affect the structural integrity of the container or vehicle; or

-	affect the dangerous goods retention capabilities of the container or vehicle.

7.3.1.8	During carriage, no dangerous residues shall adhere to the outer surfaces of containers or of the bodies of vehicles.

7.3.1.9	If several closure systems are fitted in series, the system which is located nearest to the substance to be carried shall be closed first before filling.

7.3.1.10	Empty containers or vehicles which have carried a dangerous solid substance in bulk shall be treated in the same manner as is required by ADR for a filled container or vehicle, unless adequate measures have been taken to nullify any hazard.

7.3.1.11	If containers or vehicles are used for the carriage in bulk of goods liable to cause a dust explosion, or evolve flammable vapours (e. g. for certain wastes) measures shall be taken to exclude sources of ignition and prevent dangerous electrostatic discharge during carriage, filling or discharge of the substance.

7.3.1.12	Substances, for example wastes, which may react dangerously with one another and substances of different classes and goods not subject to ADR, which are liable to react dangerously with one another shall not be mixed together in the same container or vehicle. Dangerous reactions are:

(a)		combustion and/or evolution of considerable heat;

(b)		emission of flammable and/or toxic gases;

(c)		formation of corrosive liquids; or

(d)		formation of unstable substances.

7.3.1.13	Before a container or vehicle is filled it shall be visually examined to ensure it is structurally serviceable, its interior walls, ceiling and floors are free from protrusions or damage and that any inner liners or substance retaining equipment are free from rips, tears or any damage that would compromise its cargo retention capabilities. Structurally serviceable means the container or vehicle does not have major defects in its structural components, such as top and bottom side rails, top and bottom end rails, door sill and header, floor cross members, corner posts, and corner fittings in a container. Major defects include:

(a)	bends, cracks or breaks in the structural or supporting members that affect the integrity of the container or of the body of the vehicle;

(b)	more than one splice or an improper splice (such as a lapped splice) in top or bottom end rails or door headers;

(c)	more than two splices in any one top or bottom side rail;

(d)	any splice in a door sill or corner post;

(e)	door hinges and hardware that are seized, twisted, broken, missing, or otherwise inoperative;

(f)	gaskets and seals that do not seal;

(g)	any distortion of the overall configuration of a container great enough to prevent proper alignment of handling equipment, mounting and securing on a chassis or vehicle;

(h)	any damage to lifting attachments or handling equipment interface features; or

(i)	any damage to service or operational equipment.

7.3.3	Special provisions for the carriage in bulk when the provisions of 7.3.1.1 (b) are applied

When they are shown under an entry in Column (17) of Table A of Chapter 3.2, the following special provisions apply:

VV1	Carriage in bulk in closed or sheeted vehicles, in closed containers or in large sheeted containers is permitted.

VV2	Carriage in bulk is permitted in closed vehicles with a metal body, closed metal containers and in sheeted vehicles and sheeted large containers covered with a non-combustible sheet and having a metal body or having floor and walls protected from the load.

VV3	Carriage in bulk is permitted in sheeted vehicles and sheeted large containers with adequate ventilation.

VV4	Carriage in bulk is permitted in closed or sheeted vehicles with a metal body, and in closed metal containers or in sheeted large metal containers. For UN Nos. 2008, 2009, 2210, 2545, 2546, 2881, 3189 and 3190, only carriage in bulk of solid waste is permitted.

VV5	Carriage in bulk is permitted in specially equipped vehicles and containers.

The openings used for loading and unloading shall be capable of being closed hermetically.

VV6	(Reserved)

VV7	Carriage in bulk in closed or sheeted vehicles, in closed containers or in large sheeted containers is permitted only if the substance is in pieces.

VV8	Carriage in bulk is permitted, as a full load, in closed vehicles, closed containers or sheeted vehicles or large containers covered with an impermeable, non-combustible sheet.

Vehicles and containers shall be so constructed either that the substances contained cannot come into contact with wood or any other combustible material, or that the entire surface of the floor and walls, if made of wood or another combustible material has been provided with an impermeable surfacing resistant to combustion or has been coated with sodium silicate or a similar substance.

VV9a	Carriage in bulk is permitted, as a full load, in sheeted vehicles, closed containers or in sheeted large containers with complete walls.

For substances of Class 8, the body of the vehicle or container shall be equipped with a suitable and sufficiently stout inner lining.

VV9b	Carriage in bulk of full loads (if Class 8, only for wastes) is permitted in closed containers or in sheeted large containers with complete walls. For wastes of Class 8, containers shall be equipped with a suitable and sufficiently stout inner lining.

Note: in ADR 2007 VV9b will be replaced by VV9a and VV9a becomes VV9

VV10	Carriage in bulk is permitted, as a full load, in sheeted vehicles, closed containers or sheeted large containers with complete walls.

The body of vehicles or containers shall be leakproof or rendered leakproof, for example by means of a suitable and sufficiently stout inner lining.

VV11	Carriage in bulk is permitted in specially equipped vehicles and containers in a manner which avoids risks to humans, animals and the environment, e.g. by loading the wastes in bags or by airtight connections.

VV12	Substances for which carriage in tank-vehicles, in portable tanks or in tank-containers is unsuitable because of the high temperature and density of the substance may be carried in special vehicles or containers in accordance with standards specified by the competent authority of the country of origin. If the country of origin is not a contracting party to ADR, the conditions laid down shall be recognized by the competent authority of the first country contracting party to ADR reached by the consignment.

VV13	Carriage in bulk is permitted in specially equipped vehicles or containers in accordance with standards specified by the competent authority of the country of origin. If the country of origin is not a contracting party to ADR, the conditions laid down shall be recognized by the competent authority of the first country contracting party to ADR reached by the consignment.

VV14	(1)	Used batteries may be carried in bulk in specially equipped vehicles or containers. Large plastics containers shall not be permitted. Small plastics containers shall be capable of withstanding, when fully loaded, a drop from a height of 0.8 m onto a hard surface at -18 °C, without breakage.

(2)	The load compartments of vehicles or containers shall be of steel resistant to the corrosive substances contained in the batteries. Less resistant steels may be used when there is a sufficiently great wall thickness or a plastics lining/layer resistant to the corrosive substances.

The design of the load compartments of vehicles or containers shall take account of any residual currents and impact from the batteries.

NOTE: Steel exhibiting a maximum rate of progressive reduction of 0.1 mm per year under the effects of the corrosive substances may be considered as resistant.

(3) 	It shall be ensured by means of constructional measures that there will be no leakage of corrosive substances from the load compartments of vehicles or containers during carriage. Open load compartments shall be covered. The cover shall be resistant to the corrosive substances.

(4)	Before loading, the load compartments of vehicles or containers, including their equipment, shall be inspected for damage. Vehicles or containers with damaged load compartments shall not be loaded.

The load compartments of vehicles or containers shall not be loaded above the top of their walls.

(5)	No batteries containing different substances and no other goods liable to react dangerously with each other shall be present in the load compartments of vehicles or containers (see "Dangerous reaction" in 1.2.1).

During carriage no dangerous residue of the corrosive substances contained in the batteries shall adhere to the outer surface of the load compartments of vehicles or containers.

VV15		Carriage in bulk is permitted in closed or sheeted vehicles, closed containers or sheeted large containers with complete walls for substances or mixtures (such as preparations or wastes) containing not more than 1000 mg/kg of substance to which this UN No is assigned.

The bodies of vehicles or containers shall be leakproof or rendered leakproof, for example by means of a suitable and sufficiently stout inner lining.

VV16	Carriage in bulk is permitted in accordance with the provisions of 4.1.9.2.3.

VV17	Carriage in bulk of SCO-I is permitted in accordance with the provisions of 4.1.9.2.3.

______________

# Text boxes

STSTE

Secretariat