| UNITED NATIONS |  | ST |
| --- | --- | --- |
|  | Secretariat | Distr. GENERAL ST/SG/AC.10/C.3/2006/80 9 September 2006 ENGLISH Original: FRENCH |

COMMITTEE OF EXPERTS ON THE TRANSPORT OF
DANGEROUS GOODS AND ON THE GLOBALLY
HARMONIZED SYSTEM OF CLASSIFICATION
AND LABELLING OF CHEMICALS

Sub-Committee of Experts on the
Transport of Dangerous Goods

Thirtieth session
Geneva, 4-12 (a.m.) December 2006
Item 2 (b) of the provisional agenda

# Proposals of amendments to the Recommendations 
on the Transport of Dangerous Goods

## Manual of Tests and Criteria

## Section 23

## Communication from the observer for Switzerland

### Context

1.	In section 23.2.1 of the fourth edition of the Manual of Tests and Criteria, which covers Test series C, there is a slight disparity between the English and French versions.  The French texts reads:

“Il est répondu à la question ‘La déflagration s’y propage-t-elle?’ (cases 3, 4 et 5 de la figure 20.1) selon les résultats de l’une des épreuves du tableau 23.1.”

while the English version reads:

“The question ‘Does it propagate a deflagration?’ (boxes 3, 4 and 5 of Figure 20.1) is answered on the basis of the results of the test methods in Table 23.1.”

GE.06-25323  (E)    161106    171106

Taken out of context, the French version could imply that it is sufficient to perform just one of the two C.1 and C.2 tests referred to in Table 23.1.  The matter is cleared up if the text is read in conjunction with the notes at the end of 23.4.1.4.2 and 23.4.2.4.2.  The French text in 23.2.1 is thus insufficiently explicit.  The fact that the explanation is contained in the notes at the end of the section is unfortunate, given that the main text can be interpreted in a contrary sense.  The English and French versions should therefore be amended to reflect the idea that it is sometimes, though not always, sufficient to perform only one of the two tests.

### Proposal

2.	It is proposed to amend paragraph 23.2.1 to read as follows:

“The question ‘Does it propagate a deflagration?’ (boxes 3, 4 and 5 of Figure 20.1) is answered on the basis of the results of one, or if necessary both, of the test methods in Table 23.1.”

-----