Distr.
GÉNÉRALE

ST/SG/AC.10/C.3/2006/93
10 septembre 2006

FRANÇAIS
Original: ANGLAIS

COMITÉ D’EXPERTS DU TRANSPORT DES
MARCHANDISES DANGEREUSES ET DU SYSTÈME
GÉNÉRAL HARMONISÉ DE CLASSIFICATION ET
D’ÉTIQUETAGE DES PRODUITS CHIMIQUES

Sous-Comité d’experts du transport
des marchandises dangereuses

Trentième session
Genève, 4-12 (matin) décembre 2006
Point 2 a) de l’ordre du jour provisoire

PROPOSITIONS D’AMENDEMENTS AUX RECOMMANDATIONS RELATIVES
AU TRANSPORT DES MARCHANDISES DANGEREUSES

Règlement type concernant le transport des marchandises dangereuses

Affectation des instructions de transport en citerne mobile
aux liquides toxiques par inhalation

Communication de l’expert des États-Unis d’Amérique

Introduction

1.	À sa session précédente, le Sous-Comité a examiné la question des instructions de transport en citerne mobile pour le numéro ONU 1569 Bromacétone (voir le document ST/SG/AC.10/C.3/2006/57). Le Sous-Comité a convenu que l’instruction de transport en citerne mobile T20 et les dispositions spéciales TP2 et TP13 étaient appropriées compte tenu de la toxicité et de la pression de vapeur du bromacétone. L’affectation retenue pour le bromacétone est conforme à la Partie II des Principes directeurs s’appliquant au Règlement type de l’ONU, qui traitent de l’affectation des instructions de transport en citerne mobile et des dispositions spéciales. En vertu de ces principes, l’instruction T20 devrait être affectée aux matières dont la toxicité par inhalation est inférieure ou égale à 1 000 ml/m3 et la concentration de vapeur saturée supérieure ou égale à 10 CL50, et  l’instruction T22 à celles dont la toxicité par inhalation est inférieure ou égale à 200 ml/m3 et la concentration de vapeur saturée supérieure ou égale à 500 CL50.

2.	L’expert des États-Unis a passé en revue les liquides considérés comme toxiques par inhalation et propose de leur affecter des instructions de transport en citerne mobile appropriées compte tenu de la pression de vapeur et de la toxicité de chaque matière.

Propositions

3.	Pour les matières énumérées à l’annexe, modifier les instructions de transport en citerne mobile et dispositions spéciales comme indiqué.

*     *     *

Annex (ENGLISH ONLY)

Proposed Portable Tank Instructions for Toxic by Inhalation Liquids

|  |  |  |  |  | Current | Proposed |
| --- | --- | --- | --- | --- | --- | --- |
| UN # | Name | Class | SubRisk | PG | Instruction | Special Provisions | Instruction | Special Provisions |
| Liquids with an inhalation toxicity lower than or equal to 200 ml/m3 and saturated vapour concentration greater than or equal to 500 LC50: |
| 1092 | ACROLEIN, STABILIZED | 6.1 | 3 | I | T14 | TP2 TP7 TP13 | T22 | TP2, TP7, TP13 |
| 1185 | ETHYLENEIMINE, STABILIZED | 6.1 | 3 | I |  |  | T22 | TP2, TP13 |
| 1238 | METHYL CHLOROFORMATE | 6.1 | 3 8 | I | T14 | TP2 TP13 | T22 | TP2, TP13 |
| 1239 | METHYL CHLOROMETHYL ETHER | 6.1 | 3 | I | T14 | TP2 | T22 | TP2 |
| 1244 | METHYLHYDRAZINE | 6.1 | 3 8 | I | T14 | TP2 TP13 | T22 | TP2, TP13 |
| 1251 | METHYL VINYL KETONE, STABILIZED | 6.1 | 3 8 | I | T14 | TP2 TP13 | T22 | TP2, TP13 |
| 1834 | SULPHURYL CHLORIDE | 8 |  | I | T20 | TP2 TP12 | T22 | TP2, TP12 |
| 1994 | IRON PENTACARBONYL | 6.1 | 3 | I |  |  | T22 | TP2, TP13 |
| 2480 | METHYL ISOCYANATE | 6.1 | 3 | I |  |  | T22 | TP2, TP13 |
| 2481 | ETHYL ISOCYANATE | 3 | 6.1 | I | T14 | TP2 TP13 | T22 | TP2, TP13 |
| 2482 | n-PROPYL ISOCYANATE | 6.1 | 3 | I | T14 | TP2 TP13 | T22 | TP2, TP13 |
| 2483 | ISOPROPYL ISOCYANATE | 3 | 6.1 | I | T14 | TP2 TP13 | T22 | TP2, TP13 |
| 2484 | tert-BUTYL ISOCYANATE | 6.1 | 3 | I | T14 | TP2 TP13 | T22 | TP2, TP13 |
| 2486 | ISOBUTYL ISOCYANATE | 3 | 6.1 | II | T8 | TP2 TP13 | T22 | TP2, TP13, TP27 |
| 2605 | METHOXYMETHYL ISOCYANATE | 3 | 6.1 | I | T14 | TP2 TP13 | T22 | TP2, TP13 |
| Liquids with an inhalation toxicity lower than or equal to 1000 ml/m3 and saturated vapour concentration greater than or equal to 10 LC50 |
| 1098 | ALLYL ALCOHOL | 6.1 | 3 | I | T14 | TP2 TP13 | T20 | TP2, TP13 |
| 1135 | ETHYLENE CHLOROHYDRIN | 6.1 | 3 | I | T14 | TP2 TP13 | T20 | TP2, TP13 |
| 1143 | CROTONALDEHYDE or CROTONALDEHYDE, STABILIZED | 6.1 | 3 | I | T14 | TP2 TP13 | T20 | TP2, TP13 |
| 1163 | DIMETHYLHYDRAZINE, UNSYMMETRICAL | 6.1 | 3 8 | I | T14 | TP2 TP13 | T20 | TP2, TP13 |
| 1182 | ETHYL CHLOROFORMATE | 6.1 | 3 8 | I | T14 | TP2 TP13 | T20 | TP2, TP13 |
| 1510 | TETRANITROMETHANE | 5.1 | 6.1 | I |  |  | T20 | TP2, TP13 |
| 1541 | ACETONE CYANOHYDRIN, STABILIZED | 6.1 |  | I | T14 | TP2 TP13 | T20 | TP2, TP13 |
| 1560 | ARSENIC TRICHLORIDE | 6.1 |  | I | T14 | TP2 TP13 | T20 | TP2, TP13 |
| 1569 | BROMOACETONE | 6.1 | 3 | II | T3 | TP33 | T20 | TP2, TP13 |
| 1580 | CHLOROPICRIN | 6.1 |  | I | T14 | TP2 TP13 | T20 | TP2, TP13 |
| 1595 | DIMETHYL SULPHATE | 6.1 | 8 | I | T14 | TP2 TP13 | T20 | TP2, TP13 |
| 1605 | ETHYLENE DIBROMIDE | 6.1 |  | I | T14 | TP2 TP13 | T20 | TP2, TP13 |
| 1613 | HYDROCYANIC ACID, AQUEOUS SOLUTION (HYDROGEN CYANIDE, AQUEOUS SOLUTION) with not more than 20% hydrogen cyanide | 6.1 |  | I | T14 | TP2 TP13 | T20 | TP2, TP13 |
| 1647 | METHYL BROMIDE AND ETHYLENE DIBROMIDE MIXTURE, LIQUID | 6.1 |  | I |  |  | T20 | TP2, TP13 |
| 1670 | PERCHLOROMETHYL MERCAPTAN | 6.1 |  | I | T14 | TP2 TP13 | T20 | TP2, TP13 |
| 1672 | PHENYLCARBYLAMINE CHLORIDE | 6.1 |  | I | T14 | TP2 TP13 | T20 | TP2, TP13 |
| 1695 | CHLOROACETONE, STABILIZED | 6.1 | 3 8 | I | T14 | TP2 TP13 | T20 | TP2, TP13 |
| 1722 | ALLYL CHLOROFORMATE | 6.1 | 3 8 | I | T14 | TP2 TP13 | T20 | TP2, TP13 |
| 1746 | BROMINE TRIFLUORIDE | 5.1 | 6.1 8 | I | T22 | TP2 TP12 TP13 | T20 | TP2, TP12, TP13 |
| 1752 | CHLOROACETYL CHLORIDE | 6.1 | 8 | I | T14 | TP2 TP13 | T20 | TP2, TP13 |
| 1809 | PHOSPHORUS TRICHLORIDE | 6.1 | 8 | I | T14 | TP2 TP13 | T20 | TP2, TP13 |
| 1810 | PHOSPHORUS OXYCHLORIDE | 8 |  | II | T7 | TP2 | T20 | TP2 |
| 1838 | TITANIUM TETRACHLORIDE | 8 |  | II | T10 | TP2 TP13 | T20 | TP2, TP13 |
| 1892 | ETHYLDICHLOROARSINE | 6.1 |  | I | T14 | TP2 TP13 | T20 | TP2, TP13 |
| 2232 | 2-CHLOROETHANAL | 6.1 |  | I | T14 | TP2 TP13 | T20 | TP2, TP13 |
| 2334 | ALLYLAMINE | 6.1 | 3 | I | T14 | TP2 TP13 | T20 | TP2, TP13 |
| 2337 | PHENYL MERCAPTAN | 6.1 | 3 | I | T14 | TP2 TP13 | T20 | TP2, TP13 |
| 2382 | DIMETHYLHYDRAZINE, SYMMETRICAL | 6.1 | 3 | I | T14 | TP2 TP13 | T20 | TP2, TP13 |
| 2407 | ISOPROPYL CHLOROFORMATE | 6.1 | 3 8 | I |  |  | T20 | TP2, TP13 |
| 2438 | TRIMETHYL-ACETYL CHLORIDE | 6.1 | 3 8 | I | T14 |  | T20 | TP2, TP13 |
| 2442 | TRICHLORO-ACETYL CHLORIDE | 8 |  | II | T7 | TP2 | T20 | TP2 |
| 2474 | THIOPHOSGENE | 6.1 |  | II | T7 |  | T20 | TP2 |
| 2477 | METHYL ISOTHIOCYANATE | 6.1 | 3 | I | T14 | TP2 TP13 | T20 | TP2, TP13 |
| 2485 | n-BUTYL ISOCYANATE | 6.1 | 3 | I | T14 | TP2 TP13 | T20 | TP2, TP13 |
| 2487 | PHENYL ISOCYANATE | 6.1 | 3 | I | T14 | TP2 TP13 | T20 | TP2, TP13 |
| 2488 | CYCLOHEXYL ISOCYANATE | 6.1 | 3 | I | T14 | TP2 TP13 | T20 | TP2, TP13 |
| 2521 | DIKETENE, STABILIZED | 6.1 | 3 | I | T14 | TP2 TP13 | T20 | TP2, TP13 |
| 2606 | METHYL ORTHOSILICATE | 6.1 | 3 | I | T14 | TP2 TP13 | T20 | TP2, TP13 |
| 2644 | METHYL IODIDE | 6.1 |  | I | T14 | TP2 TP13 | T20 | TP2, TP13 |
| 2646 | HEXACHLOROCYCLO-PENTADIENE | 6.1 |  | I | T14 | TP2 TP13 | T20 | TP2, TP13 |
| 2668 | CHLOROACETONITRILE | 6.1 | 3 | II | T7 | TP2 | T20 | TP2 |
| 2826 | ETHYL CHLOROTHIOFORMATE | 8 | 3 | II | T7 | TP2 | T20 | TP2 |
| 3023 | 2-METHYL-2-HEPTANETHIOL | 6.1 | 3 | I | T14 | TP2 TP13 | T20 | TP2, TP13 |
| 3079 | METHACRYLONITRILE, STABILIZED | 3 | 6.1 | I | T14 | TP2 TP13 | T20 | TP2, TP13 |
| 3246 | METHANESULPHONYL CHLORIDE | 6.1 | 8 | I | T14 | TP2 TP12 TP13 | T20 | TP2, TP12, TP13 |
| 3294 | HYDROGEN CYANIDE, SOLUTION IN ALCOHOL with not more than 45% hydrogen cyanide | 6.1 | 3 | I | T14 | TP2 TP13 | T20 | TP2, TP13 |

-----

# Text boxes

NATIONS UNIES

Secrétariat

ST

ST/SG/AC.10/C.3/2006/93

page 3

Annexe

ST/SG/AC.10/C.3/2006/93

page 4

Annexe

ST/SG/AC.10/C.3/2006/93

page 5

Annexe