# UN/SCETDG/29/INF.38

COMMITTEE OF EXPERTS ON THE TRANSPORT OF

DANGEROUS GOODS AND ON THE GLOBALLY

HARMONIZED SYSTEM OF CLASSIFICATION

AND LABELLING OF CHEMICALS

Sub-Committee of Experts on the

Transport of Dangerous Goods

Twenty-ninth session

Geneva, 3-12 (a.m.) July 2006

Item 7 of the provisional agenda

MISCELLANEOUS PROPOSALS OF AMENDMENTS TO THE MODEL REGULATIONS ON THE TREANSPORT OD DANGEROUS GOODS

Comments on ST/SG/AC.10/C.3/2006/35

Transport of various substances of Classes 3-9 in portable tanks

Transmitted by the expert from Germany

Introduction

- The Committee of Experts on the Transport of Dangerous Goods adopted during its twentieth session in September 1998 the guidelines for assigning portable tank requirements to substances in classes 3 to 9 (see ST/SG/AC.10/25/Add.2).

- After introduction of the requirements for liquid substances which are toxic by inhalation, which are not included in the 11 revised edition of the UN Recommendations, the USA proposed the guidelines for assigning portable tank requirements to substances listed in the dangerous goods list (see ST/SG/AC.10/C.3/2005/51).

- As described in the document ST/SG/AC.10/C.3/2006/35 of the United Kingdom there are a number of substances indicated in the Dangerous Goods List of the Model Regulations that do not attract a portable tank code. Thus the expert of the United Kingdom attaches in the Annex of document ST/SG/AC.10/C.3/2006/35 a list of those substances which do not appear to come into the category of those considered unsuitable for portable tanks and are referred to in the general guidelines for portable tanks, see part 1 of ST/SG/AC.10/C.3/2005/51.

- Germany appreciates this document but has still some remarks. There are still some substances where neither in the dangerous goods list of the Model Regulations nor in the document ST/SG/AC.10/C.3/2006/35 of the United Kingdom a portable tank code is assigned. Those substances are listed in Annex 1.

- Furthermore there is one substance mentioned in the document (UN 1259) which is in the opinion of Germany a toxic by inhalation one. Thus for this entry the portable tank code T22 or T20 shall by used.

- Because the special tank provision TP13 is proposed for UN 1647 and 1699 it maybe that this are also substances which are toxic by inhalation and thus the portable tank code T22 or T20 should by used.

- Substances of UN 3094 are only permitted in packages of P099. In the Dangerous Goods List of the Model Regulations are a lot of substances where no portable tank code but packing instruction P099 is assigned. UN 3094 is the only one of those which is mentioned in the United Kingdom’s document. It is the opinion of Germany that for UN 3094 no portable tank code shall be assigned.

- Additionally during the work on the United Kingdom’s document Germany found out that there are a lot of toxic by inhalation substances where the portable tank code T14 is listed. Those substances are listed in Annex 2.

- Germany would like to ask the United Kingdom to take into consideration the above mentioned comments and to revise their document accordingly.

______________

Annex 1 (according to item 4 of this document) (ENGLISH ONLY)

| UN NUMBER | PROPER SHIPPING NAME | CLASS | SUB HAZARD | PG |
| --- | --- | --- | --- | --- |
| 3274 | ALCOHOLATES SOLUTION, N.O.S., in alcohol | 3 | 8 | II |
| 1389 | ALKALI METAL AMALGAM, LIQUID | 4.3 |  | I |
| 1391 | ALKALI METAL DISPERSION or ALKALINE EARTH METAL DISPERSION | 4.3 |  | I |
| 1392 | ALKALINE EARTH METAL AMALGAM, LIQUID | 4.3 |  | I |
| 1411 | LITHIUM ALUMINIUM HYDRIDE, ETHEREAL | 4.3 | 3 | I |
| 1420 | POTASSIUM METAL ALLOYS, LIQUID | 4.3 |  | I |
| 1421 | ALKALI METAL ALLOY, LIQUID, N.O.S. | 4.3 |  | I |
| 3129 | WATER-REACTIVE LIQUID, CORROSIVE, N.O.S. | 4.3 | 8 | I |
| 3129 | WATER-REACTIVE LIQUID, CORROSIVE, N.O.S. | 4.3 | 8 | II |
| 3129 | WATER-REACTIVE LIQUID, CORROSIVE, N.O.S. | 4.3 | 8 | III |
| 3130 | WATER-REACTIVE LIQUID, TOXIC, N.O.S. | 4.3 | 6.1 | I |
| 3130 | WATER-REACTIVE LIQUID, TOXIC, N.O.S. | 4.3 | 6.1 | II |
| 3130 | WATER-REACTIVE LIQUID, TOXIC, N.O.S. | 4.3 | 6.1 | III |
| 3148 | WATER-REACTIVE LIQUID, N.O.S. | 4.3 |  | I |
| 3148 | WATER-REACTIVE LIQUID, N.O.S. | 4.3 |  | II |
| 3148 | WATER-REACTIVE LIQUID, N.O.S. | 4.3 |  | III |
| 3098 | OXIDIZING LIQUID, CORROSIVE, N.O.S. | 5.1 | 8 | I |
| 3098 | OXIDIZING LIQUID, CORROSIVE, N.O.S. | 5.1 | 8 | II |
| 3098 | OXIDIZING LIQUID, CORROSIVE, N.O.S. | 5.1 | 8 | III |
| 3099 | OXIDIZING LIQUID, TOXIC, N.O.S. | 5.1 | 6.1 | I |
| 3099 | OXIDIZING LIQUID, TOXIC, N.O.S. | 5.1 | 6.1 | II |
| 3099 | OXIDIZING LIQUID, TOXIC, N.O.S. | 5.1 | 6.1 | III |
| 3139 | OXIDIZING LIQUID, N.O.S. | 5.1 |  | I |
| 3139 | OXIDIZING LIQUID, N.O.S. | 5.1 |  | II |
| 3139 | OXIDIZING LIQUID, N.O.S. | 5.1 |  | III |
| 1185 | ETHYLENEIMINE, STABILIZED | 6.1 | 3 | I |
| 1654 | NICOTINE | 6.1 |  | II |
| 1693 | TEAR GAS SUBSTANCE, LIQUID, N.O.S. | 6.1 |  | I |
| 1693 | TEAR GAS SUBSTANCE, LIQUID, N.O.S. | 6.1 |  | II |
| 1994 | IRON PENTACARBONYL | 6.1 | 3 | I |
| 2236 | 3-CHLORO-4-METHYLPHENYL ISOCYANATE, LIQUID | 6.1 |  | II |
| 2407 | ISOPROPYL CHLOROFORMATE | 6.1 | 3 8 | I |
| 2480 | METHYL ISOCYANATE | 6.1 | 3 | I |
| 2648 | 1,2-DIBROMOBUTAN-3-ONE | 6.1 |  | II |
| 2742 | CHLOROFORMATES, TOXIC, CORROSIVE, FLAMMABLE, N.O.S. | 6.1 | 3 8 | II |
| 2942 | 2-TRIFLUOROMETHYL-ANILINE | 6.1 |  | III |
| 2029 | HYDRAZINE, ANHYDROUS | 8 | 3 6.1 | I |

Annex 2 (according to item 8 of this document) (ENGLISH ONLY)

| UN NUMBER | PROPER SHIPPING NAME | CLASS | SUB HAZARD | PG |
| --- | --- | --- | --- | --- |
| 1092 | ACROLEIN, STABILIZED | 6.1 | 3 | I |
| 1098 | ALLYL ALCOHOL | 6.1 | 3 | I |
| 1143 | CROTONALDEHYDE or CROTONALDEHYDE, STABILIZED | 6.1 | 3 | I |
| 1163 | DIMETHYLHYDRAZINE, UNSYMMETRICAL | 6.1 | 3 8 | I |
| 1182 | ETHYL CHLOROFORMATE | 6.1 | 3 8 | I |
| 1238 | METHYL CHLOROFORMATE | 6.1 | 3 8 | I |
| 1239 | METHYL CHLOROMETHYL ETHER | 6.1 | 3 | I |
| 1244 | METHYLHYDRAZINE | 6.1 | 3 8 | I |
| 1251 | METHYL VINYL KETONE, STABILIZED | 6.1 | 3 8 | I |
| 1613 | HYDROCYANIC ACID, AQUEOUS SOLUTION (HYDROGEN CYANIDE, AQUEOUS SOLUTION) with not more than 20% hydrogen cyanide | 6.1 |  | I |
| 1695 | CHLOROACETONE, STABILIZED | 6.1 | 3 8 | I |
| 2334 | ALLYLAMINE | 6.1 | 3 | I |
| 2382 | DIMETHYLHYDRAZINE, SYMMETRICAL | 6.1 | 3 | I |
| 2438 | TRIMETHYLACETYL CHLORIDE | 6.1 | 3 8 | I |
| 2482 | n-PROPYL ISOCYANATE | 6.1 | 3 | I |
| 2484 | tert-BUTYL ISOCYANATE | 6.1 | 3 | I |
| 2485 | n-BUTYL ISOCYANATE | 6.1 | 3 | I |
| 2606 | METHYL ORTHOSILICATE | 6.1 | 3 | I |
| 3294 | HYDROGEN CYANIDE, SOLUTION IN ALCOHOL with not more than 45% hydrogen cyanide | 6.1 | 3 | I |

________________