# UN/SCETDG/30/INF.36

COMMITTEE OF EXPERTS ON THE TRANSPORT OF

DANGEROUS GOODS AND ON THE GLOBALLY

HARMONIZED SYSTEM OF CLASSIFICATION

AND LABELLING OF CHEMICALS

Sub-Committee of Experts on the

Transport of Dangerous Goods

# Twenty-ninth session

Geneva, 4-12 (a.m.) December 2006

Item 2 (a) (ii) of the provisional agenda

LISTING, CLASSIFICATION AND PACKING

Subsidiary risk of hydrogen cyanide

### Note by the Secretariat

- Four UN numbers are assigned to hydrogen cyanide in the Model Regulations:

| UN No. | Name | Class | Subsi-diary risk | UN packing group | Special provi-sions | LQ | Packings and IBCs | Portable tanks and bulk containers |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1051 | HYDROGEN CYANIDE, STABILIZED containing less than 3% water | 6.1 | 3 | I |  | NONE | P200 |  |  |  |
| 1613 | HYDROCYANIC ACID, AQUEOUS SOLUTION (HYDROGEN CYANIDE, AQUEOUS SOLUTION) with not more than 20% hydrogen cyanide | 6.1 |  | I | 48 | NONE | P601 |  | T14 | TP2 TP13 |
| 1614 | HYDROGEN CYANIDE, STABILIZED, containing less than 3% water and absorbed in a porous inert material | 6.1 |  | I |  | NONE | P099 |  |  |  |
| 3294 | HYDROGEN CYANIDE, SOLUTION IN ALCOHOL with not more than 45% hydrogen cyanide | 6.1 | 3 | I |  | NONE | P601 |  | T14 | TP2 TP13 |

- It is noted that Subsidiary risk "3" has been assigned to UN Nos. 1613 and 1614 in RID/ADR.

- The Sub-committee may wish to consider whether it is appropriate to add subsidiary risk "3" for UN Nos. 1613 and 1614.

_______________