UNITED

# NATIONS

Distr.

# GENERAL

# ST/SG/AC.10/C.4/2006/8/Add.2

# 15 May 2006

ENGLISH

Original: ENGLISH AND FRENCH

COMMITTEE OF EXPERTS ON THE TRANSPORT OF

# DANGEROUS GOODS AND ON THE GLOBALLY

# HARMONIZED SYSTEM OF CLASSIFICATION

# AND LABELLING OF CHEMICALS

Sub-Committee of Experts on the Globally

Harmonized System of Classification

and Labelling of Chemicals

Eleventh session, 12-14 July 2006

Item 3(c) of the provisional agenda

HAZARD COMMUNICATION ISSUES

Codification of hazard and precautionary statements

Transmitted by the representative from the European Chemical Industry Council (CEFIC) 
on behalf of the precautionary statements correspondence working group

Addendum 2

Revision of precautionary statement texts

Amendments to the text of the precautionary statements

| Code | Revised text | Original text | Hazard class | Hazard category |
| --- | --- | --- | --- | --- |
| P101 | If medical advice is needed, have product container or label at hand. | If medical advice is needed: Have product container or label at hand. |  |  |
| P210 | Keep away from heat/sparks/open flame/hot surfaces. – No smoking. | Keep away from heat/sparks/open flame. - No smoking. | Explosives (chapter 2.1) | Divisions 1.1, 1.2, 1.3, 1.4, 1.5 |
|  |  |  | Flammable gases (chapter 2.2) | 1, 2 |
|  |  |  | Flammable aerosols (chapter 2.3) | 1, 2 |
|  |  |  | Flammable liquids (chapter 2.6) | 1, 2, 3 |
|  |  |  | Flammable solids (chapter 2.7) | 1, 2 |
|  |  |  | Self-reactive substances and mixtures (chapter 2.8) | Types A, B, C, D, E, F |
|  |  |  | Pyrophoric liquids (chapter 2.9) | 1 |
|  |  |  | Pyrophoric solids (chapter 2.10) | 1 |
|  |  |  | Organic peroxides (chapter 2.15) | Types A, B, C, D, E, F |
|  |  | Keep away from flames and hot surfaces. | Flammable liquids (chapter 2.6) | 4 |
|  |  | Keep away from heat. | Oxidizing liquids (chapter 2.13) | 1, 2, 3 |
|  |  |  | Oxidizing solids (chapter 2.14) | 1, 2, 3 |
| P211 | Do not spray on an open flame or other ignition source. | Do not spray on an open flame or any white-hot material. | Flammable aerosols (chapter 2.3) | 1, 2 |
| P220 | Keep/Store away from clothing/.../ combustible materials. | Keep away from combustible materials. | Oxidizing gases (chapter 2.4) | 1 |
|  |  | Keep away from ... | Self-reactive substances and mixtures (chapter 2.8) | Types A, B, C, D, E, F |
|  |  |  | Organic peroxides (chapter 2.15) | Types A, B, C, D, E, F |
|  |  | Keep away from clothing and other combustible materials. Store away from combustibles/... | Oxidizing liquids (chapter 2.13) | 1 |
|  |  |  | Oxidizing solids (chapter 2.14) | 1 |
|  |  | Store away from combustibles/... | Oxidizing liquids (chapter 2.13) | 2, 3 |
|  |  |  | Oxidizing solids (chapter 2.14) | 2, 3 |
| P223 | Keep away from any possible contact with water, because of violent reaction and possible flash fire. | Keep from any possible contact with water, because of violent reaction and possible flash fire. | Substances and mixtures which, in contact with water, emit flammable gases (chapter 2.12) | 1, 2 |
| P231 + P232 | Handle under inert gas. Protect from moisture. | Handle under inert gas, protect from moisture. | Substances and mixtures which, in contact with water, emit flammable gases (chapter 2.12) | 1, 2, 3 |
| P235 + P410 | Keep cool. Protect from sunlight. | Keep cool and protect from sunlight. | Self-heating substances and mixtures (chapter 2.11) | 1, 2 |
| P260 | Do not breathe dust/fume/gas/mist/vapours/spray. | Do not breathe dust/fume/gas/mist/vapours/spray. | Acute toxicity – inhalation (chapter 3.1) | 1, 2 |
|  |  |  | Specific target organ systemic toxicity – single exposure (chapter 3.8) | 1, 2 |
|  |  |  | Specific target organ systemic toxicity – prolonged or repeated exposure (chapter 3.9) | 1, 2 |
|  |  | Do not breathe dust or mist | Skin corrosion (chapter 3.2) | 1A, 1B, 1C |
|  |  |  | Reproductive toxicity – effects on or via lactation (chapter 3.7) | Additional category |
| P264 | Wash ... thoroughly after handling. | Wash hands thoroughly after handling. | Acute toxicity – oral (chapter 3.1) | 1, 2, 3, 4 |
|  |  |  | Acute toxicity – dermal (chapter 3.1) | 1, 2 |
|  |  |  | Reproductive toxicity – effects on or via lactation (chapter 3.7) | Additional category |
|  |  |  | Specific target organ systemic toxicity – single exposure (chapter 3.8) | 1, 2 |
|  |  |  | Specific target organ systemic toxicity – prolonged or repeated exposure (chapter 3.9) | 1 |
|  |  | Wash thoroughly after handling. | Skin corrosion (chapter 3.2) | 1A, 1B, 1C |
|  |  |  | Skin irritation (chapter 3.2) | 2 |
|  |  | Wash hands after handling. | Eye irritation (chapter 3.3) | 2A, 2B |
| P280 | Wear protective gloves/protective clothing/eye protection/face protection. | Wear protective gloves/clothing and eye/face protection | Skin corrosion (chapter 3.2) | 1A, 1B, 1C |
|  |  | Wear protective gloves and eye/face protection | Flammable liquids (chapter 2.6) | 1, 2, 3, 4 |
|  |  |  | Flammable solids (chapter 2.7) | 1, 2 |
|  |  |  | Self-reactive substances and mixtures (chapter 2.8) | Types A, B, C, D, E, F |
|  |  |  | Pyrophoric liquids (chapter 2.9) | 1 |
|  |  |  | Pyrophoric solids (chapter 2.10) | 1 |
|  |  |  | Self-heating substances and mixtures (chapter 2.11) | 1, 2 |
|  |  |  | Substances and mixtures which, in contact with water, emit flammable gases (chap. 2.12) | 1, 2, 3 |
|  |  |  | Oxidizing liquids (chapter 2.13) | 1, 2, 3 |
|  |  |  | Oxidizing solids (chapter 2.14) | 1, 2, 3 |
|  |  |  | Organic peroxides (chapter 2.15) | Types A, B, C, D, E, F |
| P280 (cont’d) |  | Wear protective gloves/clothing | Acute toxicity – dermal (chapter 3.1) | 1, 2, 3, 4 |
|  |  | Wear protective gloves | Skin irritation (chapter 3.2) | 2 |
|  |  |  | Skin sensitization (chapter 3.4) | 1 |
|  |  | Wear eye/face protection | Severe eye damage (chapter 3.3) | 1 |
|  |  |  | Eye irritation (chapter 3.3) | 2A |
|  |  | Wear face protection | Explosives (chapter 2.1) | Divisions 1.1, 1.2, 1.3, 1.4, 1.5 |
| P302 + P334 | IF ON SKIN: Immerse in cool water/wrap in wet bandages. | If on skin, immerse in cool water/wrap with wet bandages. | Pyrophoric liquids (chapter 2.9) | 1 |
| P304 + P340 | IF INHALED: Remove to fresh air and keep at rest in a position comfortable for breathing. | IF INHALED: Remove victim to fresh air and keep at rest in a position comfortable for breathing | Acute toxicity – inhalation (chapter 3.1) | 1, 2 |
| P308 + P313 | If exposed or concerned: Get medical advice/attention. | If exposed or concerned: Get medical attention/advice. | Germ cell mutagenicity (chapter 3.5) | 1A, 1B, 2 |
|  |  |  | Carcinogenicity (chapter 3.6) | 1A, 1B, 2 |
|  |  |  | Reproductive toxicity (chapter 3.7) | 1A, 1B, 2 |
|  |  |  | Reproductive toxicity – effects on or via lactation (chapter 3.7) | Additional category |
| P309 + P311 | IF exposed or if you feel unwell: Call a POISON CENTER or doctor/physician. | Call a POISON CENTER or doctor/ physician if exposed or you feel unwell: | Specific target organ systemic toxicity – single exposure (chapter 3.8) | 2 |
| P312 | Call a POISON CENTER or doctor/physician if you feel unwell. | Call a POISON CENTER/doctor/physician if you feel unwell. | Acute toxicity – oral (chapter 3.1) | 5 |
| P314 | Get medical advice/attention if you feel unwell. | Get medical attention/advice if you feel unwell. | Specific target organ systemic toxicity – prolonged or repeated exposure (chapter 3.9) | 1, 2 |
| P315 | Get immediate medical advice/attention. | Seek immediate medical attention/advice. | Gases under pressure (chapter 2.5) | Refrigerated liquefied gas |
| P332 + P313 | If skin irritation occurs: Get medical advice/ attention. | If skin irritation occurs, seek medical advice/ attention. | Skin irritation (chapter 3.2) | 2, 3 |
| P333 + P313 | If skin irritation or rash occurs: Get medical advice/attention. | If skin irritation or rash occurs, seek medical advice/attention. | Skin sensitization (chapter 3.4) | 1 |
| P335 + P334 | Brush off loose particles from skin. Immerse in cool water/wrap in wet bandages. | Brush off loose particles from skin and immerse in cool water/wrap in wet bandages. | Pyrophoric solids (chapter 2.10) | 1 |
|  |  |  | Substances and mixtures which, in contact with water, emit flammable gases (chapter 2.12) | 1, 2 |
| P337 + P313 | If eye irritation persists: Get medical advice/attention. | If eye irritation persists, get medical advice/ attention. | Eye irritation (chapter 3.3) | 2A, 2B |
| P342 + P311 | If experiencing respiratory symptoms: Call a POISON CENTER or doctor/ physician. | If experiencing respiratory symptoms call a POISON CENTER or doctor/physician. | Respiratory sensitization (chapter 3.4) | 1 |
| P362 | Take off contaminated clothing and wash before re-use. | Take of contaminated clothing and wash before re-use | Skin irritation (chapter 3.2) | 2 |
| P363 | Wash contaminated clothing before reuse. | Wash/Decontaminate removed clothing before reuse. | Acute toxicity – dermal (chapter 3.1) | 1, 2, 3 |
| P370 + P376 | In case of fire: Stop leak if safe to do so. | In case of fire, stop leak if safe to do so. | Oxidizing gases (chapter 2.4) | 1 |
| P370 + P378 | In case of fire: Use ... for extinction | In case of fire, use ... for extinction | Flammable liquids (chapter 2.6) | 1, 2, 3, 4 |
|  |  |  | Flammable solids (chapter 2.7) | 1, 2 |
|  |  |  | Self-reactive substances and mixtures (chapter 2.8) | Types A, B, C, D, E, F |
|  |  |  | Pyrophoric liquids (chapter 2.9) | 1 |
|  |  |  | Pyrophoric solids (chapter 2.10) | 1 |
|  |  |  | Substances and mixtures which, in contact with water, emit flammable gases (chapter 2.12) | 1, 2, 3 |
|  |  |  | Oxidizing liquids (chapter 2.13) | 1, 2, 3 |
|  |  |  | Oxidizing solids (chapter 2.14) | 1, 2, 3 |
| P370 + P380 | In case of fire: Evacuate area. | In case of fire, evacuate area. | Explosives (chapter 2.1) | Divisions 1.1, 1.2, 1.3, 1.4, 1.5 |
| P380 + P375 | Evacuate area. Fight fire remotely due to the risk of explosion. | Evacuate area and fight fire remotely due to the risk of explosion. | Self-reactive substances and mixtures (chapter 2.8) | Types A, B |
|  |  |  | Oxidizing liquids (chapter 2.13) | 1 |
|  |  |  | Oxidizing solids (chapter 2.14) | 1 |
| P402 + P404 | Store in a dry place. Store in a closed container. | Store in a dry place and/or in a closed container. | Substances and mixtures which, in contact with water, emit flammable gases (chapter 2.12) | 1, 2, 3 |
| P403 + P233 | Store in a well-ventilated place. Keep container tightly closed. | Store container tightly closed in well-ventilated place. | Acute toxicity – inhalation (chapter 3.1) | 1, 2, 3 |
|  |  |  | Specific target organ systemic toxicity – single exposure; respiratory tract irritation (chapter 3.8) | 3 |
|  |  |  | Specific target organ systemic toxicity – single exposure; narcosis (chapter 3.8) | 3 |
| P403 + P235 | Store in a well-ventilated place. Keep cool. | Store in a cool/well-ventilated place. | Flammable liquids (chapter 2.6) | 1, 2, 3, 4 |
|  |  |  | Self-reactive substances and mixtures (chapter 2.8) | Types A, B, C, D, E, F |
| P406 | Store in corrosive resistant/... container with a resistant inner liner. | Store in corrosive resistant/... container with a resistant inliner. | Substances and mixtures corrosive to metals (chapter 2.16) | 1 |
| P410 + P403 | Protect from sunlight. Store in a well-ventilated place. | Protect from sunlight and store in well-ventilated place. | Gases under pressure (chapter 2.5) | Compressed gas |
|  |  |  |  | Liquefied gas |
|  |  |  |  | Dissolved gas |
| P410 + P412 | Protect from sunlight. Do not expose to temperatures exceeding 50 °C/ 122 °F. | Protect from sunlight and do not expose to temperatures exceeding 50 °C/122 °F. | Flammable aerosols (chapter 2.3) | 1, 2 |
| P411 + P235 | Store at temperatures not exceeding …°C/…°F. Keep cool. | Store in cool place at temperatures not exceeding …°C/…°F. | Organic peroxides (chapter 2.15) | Types A, B, C, D, E, F |

Amendments to the text of the precautionary statements concerning the conditions for use

| Code | Revised text | Original text | Hazard class | Hazard category |
| --- | --- | --- | --- | --- |
| P240 | - if product is volatile so as to generate hazardous atmosphere | - if product is as volatile as to generate hazardous atmosphere | Flammable liquids (chapter 2.6) | 1, 2, 3 |
| P403+ P233 | - if product is volatile so as to generate hazardous atmosphere | - if product is as volatile as to generate hazardous atmosphere | Acute toxicity – inhalation (chapter 3.1) | 1, 2, 3 |
|  |  |  | Specific target organ systemic toxicity – single exposure (chapter 3.8): - respiratory tract irritation; - narcotic effects; | 3 |
| P260 | Manufacturer/supplier or the competent authority to specify applicable conditions |  | Acute toxicity – inhalation (chapter 3.1) | 1, 2, 3 |
|  |  |  | Specific target organ systemic toxicity – single exposure (chapter 3.8) | 1, 2 |
|  |  |  | Specific target organ systemic toxicity – prolonged or repeated exposure (chapter 3.9) | 1, 2 |
|  | - if inhalable particles of dusts or mists may occur during use. | - if inhalable particles may occur during use. | Skin corrosion (chapter 3.2) | 1A, 1B, 1C |
|  |  |  | Reproductive toxicity – effects on or via lactation (chapter 3.7) | Additional category |
| P261 | Avoid breathing dust/fume/gas/mist/vapours/spray. Manufacturer/supplier or the competent authority to specify applicable conditions |  | Acute toxicity – inhalation (chapter 3.1) | 3, 4 |
|  |  |  | Respiratory sensitization (chapter 3.4) | 1 |
|  |  |  | Skin sensitization (chapter 3.4) | 1 |
|  |  |  | Specific target organ systemic toxicity – single exposure; (chapter 3.8): - respiratory tract irritation - narcotic effects | 3 |

# Text boxes

STSTE

Secretariat