| UNITED NATIONS |  | ST |
| --- | --- | --- |
|  | Secretariat | Distr. GENERAL ST/SG/AC.10/C.4/2006/23 27 October 2006 ENGLISH Original: ENGLISH AND FRENCH |

COMMITTEE OF EXPERTS ON THE TRANSPORT OF

# DANGEROUS GOODS AND ON THE GLOBALLY

# HARMONIZED SYSTEM OF CLASSIFICATION

# AND LABELLING OF CHEMICALS

Sub-Committee of Experts on the Globally

Harmonized System of Classification

and Labelling of Chemicals

Twelfth session

Geneva, 12(p.m.)-14 December 2006

Item 2 (b) of the provisional agenda

UPDATING OF THE GLOBALLY HARMONIZED SYSTEM OF CLASSIFICATION
AND LABELLING OF CHEMICALS

# Amendments to decision logics 3.4.1 and 3.4.2 in Chapter 3.4 of the GHS

Transmitted by the expert from Germany

In the decision logics 3.4.1 and 3.4.2, the cut-off values/concentration limits of ingredients of a mixture classified as either skin sensitizers or respiratory sensitizers that would trigger the classification of the mixture are not consistent with those given in table 3.4.1.

## Proposal

(a)	In decision logic 3.4.1, amend the text in the last but one box on the left as follows:

And insert a footnote “5” after current footnote 4 as follows:

“5	See 3.4.4.2.”

(b)	In decision logic 3.4.2, amend the text in the last but one box on the left as follows:

And insert a footnote “5” after current footnote 4 as follows:

“5	See 3.4.4.2.”

____________

# Text boxes

Does the mixture contain one or more ingredients classified as a respiratory sensitizer at 4, 5:

- (  0.1% w/w (solid/liquid), or

- (  1.0% w/w (solid/liquid)

or

- (  0.1% v/v (gas), (see 3.4.3.3)

- (  0.2% v/v (gas)?, (see 3.4.3.3)

Does the mixture contain one or more ingredients classified as a skin sensitizer at 4, 5:

- (  0.1%, , or

- (  1.0%? (see 3.4.3.3)