| UNITED NATIONS | E |
| --- | --- |
|  | Economic and Social Council | Distr. GENERAL ECE/TRANS/WP.29/2006/31/Add.1/Rev.1 3 July 2006 Original: ENGLISH |

###### ECONOMIC COMMISSION FOR EUROPE

# INLAND TRANSPORT COMMITTEE

# World Forum for Harmonization of Vehicle Regulations (WP.29)

One-hundred-and-fortieth session

Geneva, 14-17 November 2006

Item 4.2.34. of the provisional agenda

REVISED PROPOSAL FOR SUPPLEMENT 4 TO THE 02 SERIES OF AMENDMENTS  TO REGULATION No. 51

(Noise emissions)

Submitted by the representative of the European Community (EC)

Addendum

Note:	The text reproduced below was prepared by the representative of the EC in order to complement its proposal.  The modifications of document ECE/TRANS/WP.29/2006/31/Add.1 are marked in bold characters.

This document is a working document circulated for discussion and comments. The use of this document for other purposes is the entire responsibility of the user. Documents are also available via the INTERNET: http://www.unece.org/trans/main/welcwp29.htm

GE.06-

Paragraph 5.1., amend to read:

"5.1.	Type approval shall only be granted if,

(a)	the vehicle type meets the requirements of paragraphs 6. and 7. below when tested according to measurement method A of Annex 3, and

(b)	starting at 1 July 2007 and for a maximum period of two years, the results of the test run of that vehicle type in accordance with the measurement method B of Annex 10 have been added to the test report in Annex 9 and communicated to the European Commission and those Contracting Parties that express an interest in receiving the data.  This does not include any tests done in connection with the extension of existing approvals according to Regulation No. 51.  Furthermore, for the purpose of this monitoring procedure a vehicle is not considered to be a new type if the vehicle differs only in respect to paragraphs 2.2.1. and 2.2.2."

Annex 10, paragraph 2.2.2., footnote 2/, add the following text at the end of the existing text.

"     tyre/road sound emission regulations.  Snow tyres and special tyres according to UNECE Regulation No. 117 should be excluded during type-approval- and COP-measurements on request of the manufacturer."

- - - - -