#### UNITED

# NATIONS

Distr.

# GENERAL

# ST/SG/AC.10/C.3/2007/6

23 March 2007

Original:  ENGLISH

## COMMITTEE OF EXPERTS ON THE TRANSPORT OF

# DANGEROUS GOODS AND ON THE GLOBALLY

# HARMONIZED SYSTEM OF CLASSIFICATION

# AND LABELLING OF CHEMICALS

# Sub-Committee of Experts on the

# Transport of Dangerous Goods

# Thirty-first session

# Geneva, 2-6 July 2007

# Item 3 of the provisional agenda

LISTING, CLASSIFICATION AND PACKING

###### Allocation of substances and articles to Packing Instruction P099

Transmitted by the International Air Transport Association (IATA)

#### Background

###### 1.	At the thirtieth session of the Sub-Committee IATA submitted informal document INF.38 that identified substances and articles assigned to P099 in the fourteenth revised edition of the UN Model Regulations with the packing instructions assigned to those UN numbers in ADR, the ICAO Technical Instructions and IMDG Code.

###### 2.	The paper identified inconsistency in the assignment of packing instructions for some substances. For example a number of substances and articles are permitted for transport by road and/or air in packagings other than those specifically approved by a competent authority as would be required by P099, e.g. UN 1222 – Isopropyl nitrate, UN 3095 – Corrosive solid, self-heating, n.o.s., etc.

###### 3.	A relaxation for the packaging requirement for some modes of transport creates a potential for multi-modal disharmony.  In general terms, the provisions contained within the UN Model Regulations should be taken as a minimum standard. So while some modes, or States, may impose additional restrictions or requirements, the modal or State regulations should not provide for a lesser standard than that contained in the Model Regulations.

###### Proposal

###### 4.	Based on a review of the provisions of ADR, the United States Code of Federal Regulations Title 49 (49 CFR) and the ICAO Technical Instructions, it is proposed that a number of substances currently assigned Packing Instruction P099 be amended as follows:

Group A

5.	These are substances to which ADR has assigned a generic packing instruction, P001 or P002 without any additional special provisions.  It is proposed that the Model Regulations be similarly revised

| UN No. | Name and description | Class or division | Subsi-diary risk | UN packing group | Special provi-sions |  | Packagings and IBCs | Portable tanks and bulk containers |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  |  |  | Packing Instruction | Special packing provisions | Instruc-tions | Special provis -ions |
| (1) | (2) | (3) | (4) | (5) | (6) | (7a) | (7b) | (8) | (9) | (10) | (11) |
| 1194 | ETHYL NITRITE SOLUTION | 3 | 6.1 | I |  | 0 | E0 | P099 P001 |  |  |  |
| 1222 | ISOPROPYL NITRATE | 3 |  | II | 26 | 1 L | E2 | P099 P001 IBC02 | B7 |  |  |
| 1261 | NITROMETHANE | 3 |  | II | 26 | 1 L | E0 | P099 P001 |  |  |  |
| 1865 | n-PROPYL NITRATE | 3 |  | II | 26 | 1 L | E2 | P099 P001 IBC02 | B7 |  |  |
| 3094 | CORROSIVE LIQUID, WATER-REACTIVE, N.O.S. | 8 | 4.3 | I | 274 | 0 | E0 | P099 P001 |  |  |  |
| 3095 | CORROSIVE SOLID, SELF-HEATING, N.O.S. | 8 | 4.2 | I | 274 | 0 | E0 | P099 P002 |  | T6 | TP9 TP33 |
| 3096 | CORROSIVE SOLID, WATER-REACTIVE, N.O.S. | 8 | 4.3 | I | 274 | 0 | E0 | P099 P002 |  | T6 | TP9 TP33 |
| 3124 | TOXIC SOLID, SELF-HEATING, N.O.S. | 6.1 | 4.2 | I | 274 | 0 | E0 | P099 P002 |  | T6 | TP9 TP33 |
| 3301 | CORROSIVE LIQUID, SELF-HEATING, N.O.S. | 8 | 4.2 | I | 274 | 0 | E0 | P099 P001 |  |  |  |

Group B

6.	These are substances to which ADR, ICAO and/or US DOT in 49 CFR has assigned a specific packing instruction.  It is proposed that the applicable packing instruction be assigned to the substance as shown:

| UN No. | Name and description | Class or division | Subsi-diary risk | UN packing group | Special provis-ions |  | Packagings and IBCs | Portable tanks and bulk containers |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  |  |  | Packing Instruction | Special packing provisions | Instruc-tions | Special provis-ions |
| (1) | (2) | (3) | (4) | (5) | (6) | (7a) | (7b) | (8) | (9) | (10) | (11) |
| 3123 | TOXIC LIQUID, WATER-REACTIVE, N.O.S. | 6.1 | 4.3 | I | 274 | 0 | E0 | P099 P601 |  |  |  |
| 3125 | TOXIC SOLID, WATER-REACTIVE, N.O.S. | 6.1 | 4.3 | I | 274 | 0 | E0 | P099 P002 | T6 | TP9 TP33 | T6 |

Group C

7.	This group is a little more problematic. These are substances where ADR and in some cases the IMDG Code has gone beyond P099 and identified that the substance is forbidden for transport (see below).  The question raised here is, should the UN Sub-Committee consider adopting a provision that goes beyond P099 to perhaps include, for some substances, recommendation that their transport requires a multilateral approval for international transport.

8.	This was an issue that was raised by the expert from Italy in INF.11 at the twenty-eighth session of the Sub-Committee.  The report of the twenty-eighth session identifies that the Sub-Committee “…agreed that a rationalized approach should be adopted in future in the Model Regulations for this purpose.”

9.	The Sub-Committee is invited to consider the development of such a rationalised approach.

| UN Number | Proper Shipping Name | Class /Div | Sub Risk | PG | ADR | ICAO TI | IMDG Code |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 2186 | HYDROGEN CHLORIDE REFRIGERATED LIQUID | 2.3 | 8 |  | Forbidden | Forbidden Forbidden | Forbidden |
| 2249 | DICHLORODIMETHYL ETHER STABILIZED | 6.1 | 3 | I | Forbidden | Forbidden Forbidden | P099 |
| 3097 | FLAMMABLE SOLID, OXIDIZING, N.O.S. | 4.1 | 5.1 | II/III | Forbidden | Forbidden Forbidden | P099 |
| 3100 | OXIDIZING SOLID, SELF-HEATING, N.O.S. | 5.1 | 4.2 | I/II | Forbidden | Forbidden Forbidden | P099 |
| 3121 | OXIDIZING SOLID, WATER-REACTIVE, N.O.S. | 5.1 | 4.3 | I/II | Forbidden | Forbidden Forbidden | P099 |
| 3127 | SELF-HEATING SOLID, OXIDIZING, N.O.S. | 4.2 | 5.1 | II/III | Forbidden | Forbidden (A2) Forbidden (A2) | P099 |
| 3133 | WATER-REACTIVE SOLID, OXIDIZING, N.O.S. | 4.3 | 5.1 | II/III | Forbidden | Forbidden (A2) Forbidden (A2) | P099 |
| 3137 | OXIDIZING SOLID, FLAMMABLE, N.O.S. | 5.1 | 4.1 | I | Forbidden | Forbidden Forbidden | P099 |
| 3255 | tert-BUTYL HYPOCHLORITE | 4.2 | 8 | I | Forbidden | Forbidden Forbidden | P099 |

___________

# Text boxes

STSTE

Secretariat