# UN/SCETDG/31/INF.35

COMMITTEE OF EXPERTS ON THE TRANSPORT OF

DANGEROUS GOODS AND ON THE GLOBALLY

HARMONIZED SYSTEM OF CLASSIFICATION

AND LABELLING OF CHEMICALS

# Sub-Committee of Experts on the

# Transport of Dangerous Goods

# Thirty-first session

Geneva, 2-6 July 2007

Item 3 (a) of the provisional agenda

# LISTING, CLASSIFICATION AND PACKING

# Problems encountered for testing “Explosive Properties”

# of pharmaceutical chemicals

# Transmitted by the expert from the United States of America

1.	This paper is intended only to facilitate discussion. No decision by the Sub-Committee is requested.  The expert from the United States of America is seeking comments from members of the Sub-Committee on the issues presented in this paper.

Background

2.	Pharmaceutical companies routinely screen a large number of materials for their potential applications.  Many of these materials are candidates for “explosives” based on the screening procedures, i.e. structure-activity relationship, decomposition energy and temperature by scanning calorimetry, etc.

Problems

(a)	Only small quantities of materials are available at the time of evaluation;

(b)	Materials are very expensive;

(c)	Classification testing is very expensive for the number of materials to be evaluated.

Solutions desired

(a)	Small scale testing methods and criteria;

(b)	Simplified testing requirements or reduced number of tests;

(c)	Consider non-regulated substance status for transport of very small quantities of these materials.

____________