| UNITED NATIONS |  | E |
| --- | --- | --- |
|  | Economic and Social Council | Distr. GENERAL ECE/TRANS/WP.15/AC.1/2007/15 28 December 2006 Original: ENGLISH |

ECONOMIC COMMISSION FOR EUROPE

INLAND TRANSPORT COMMITTEE

Working Party on the Transport of Dangerous Goods

Joint Meeting of the RID Committee of Experts and the

Working Party on the Transport of Dangerous Goods

Bern, 26-30 March 2007

Item 5 of the provisional agenda

PROPOSALS OF AMENDMENTS TO RID/ADR/ADN */

Special Provision 274

Transmitted by the European Chemical Industry Council (CEFIC)

| SUMMARY |
| --- |
| Executive Summary: | Remove disharmony between RID/ADR/ADN and the UN Model Regulations, IMDG Code and ICAO TI regarding the assignment of SP 274 |
| Action to be taken: | Remove SP 274 from column 6 of Table A for UN numbers listed in annex |
| Related documents: | None |

_________

*/ 	Circulated by the Intergovernmental Organization for International Carriage by Rail (OTIF) under the symbol OTIF/RID/RC/2007/15.

Introduction

1.	In RID/ADR/ADN some 135 entries have been assigned SP 274 (requiring to supplement the proper shipping name with the technical name) whereas this is neither the case in the UN Model Regulations, the IMDG Code nor the ICAO Technical Instructions. This is also not the case in the United States CFR 49. The list of affected entries is shown in the annex. These diverging requirements may lead to problems in intermodal transport, where one part of the journey may not require the inclusion of a technical name, whereas the following part does.

Proposal

2.	Remove SP 274 from column 6 of Table A for the UN numbers in Annex.

3.	If this proposal is not adopted, the delegations of the Joint Meeting are invited to give their opinion on whether, on the contrary, they would support a proposal to the United Nations Sub-Committee of Experts on the Transport of Dangerous Goods to assign SP 274 to those entries without SP 274 but with SP 274 in RID/ADR/ADN i.e. achieving harmonisation of other modal regulations with European land transport regulations.

Justification

4.	The absence of the requirement for a technical name has not resulted in problems for transport by sea or air nor for land transport in the United States of America. The removal of SP 274 for these substances will lead to further harmonisation between modes and will align all modal regulations with the UN Model Regulations.

Safety implications/Feasibility/Enforceability

5.	No problem.

Annex

List of entries in RID/ADR/ADN 2007 with SP 274 in column 6 but without SP 274

in UN Model Regulations, IMDG Code, ICAO TI

(English only)

| UN No. | Name and description | Class | Classification code | Packing group | Labels | Special provisions |
| --- | --- | --- | --- | --- | --- | --- |
|  | 3.1.2 | 2.2 | 2.2 | 2.1.1.3 | 5.2.2 | 3,3 |
| (1) | (2) | (3a) | (3b) | (4) | (5) | (6) |
| 1075 | PETROLEUM GASES, LIQUEFIED | 2 | 2F |  | 2.1 | 274 583 639 |
| 1353 | FIBRES or FABRICS IMPREGNATED WITH WEAKLY NITRATED NITROCELLULOSE, N.O.S. | 4.1 | F1 | III | 4.1 | 274 502 |
| 1373 | FIBRES or FABRICS, ANIMAL or VEGETABLE or SYNTHETIC, N.O.S. with oil | 4.2 | S2 | III | 4.2 | 274 |
| 1378 | METAL CATALYST, WETTED with a visible excess of liquid | 4.2 | S4 | II | 4.2 | 274 |
| 1389 | ALKALI METAL AMALGAM, LIQUID | 4.3 | W1 | I | 4.3 | 182 274 |
| 1390 | ALKALI METAL AMIDES | 4.3 | W2 | II | 4.3 | 182 274 505 |
| 1391 | ALKALI METAL DISPERSION or ALKALINE EARTH METAL DISPERSION having a flash-point of not more than 60°C | 4.3 | WF1 | I | 4.3 +3 | 182 183 274 506 |
| 1391 | ALKALI METAL DISPERSION or ALKALINE EARTH METAL DISPERSION having a flash-point above 60°C | 4.3 | W1 | I | 4.3 | 182 183 274 282 506 |
| 1392 | ALKALINE EARTH METAL AMALGAM, LIQUID | 4.3 | W1 | I | 4.3 | 183 274 506 |
| 1393 | ALKALINE EARTH METAL ALLOY, N.O.S. | 4.3 | W2 | II | 4.3 | 183 274 506 |
| 1421 | ALKALI METAL ALLOY, LIQUID, N.O.S. | 4.3 | W1 | I | 4.3 | 182 274 |
| 1450 | BROMATES, INORGANIC, N.O.S. | 5.1 | O2 | II | 5.1 | 274 604 |
| 1461 | CHLORATES, INORGANIC, N.O.S. | 5.1 | O2 | II | 5.1 | 274 605 |
| 1462 | CHLORITES, INORGANIC, N.O.S. | 5.1 | O2 | II | 5.1 | 274 509 606 |
| 1477 | NITRATES, INORGANIC, N.O.S. | 5.1 | O2 | II | 5.1 | 274 511 |
| 1477 | NITRATES, INORGANIC, N.O.S. | 5.1 | O2 | III | 5.1 | 274 511 |
| 1481 | PERCHLORATES, INORGANIC, N.O.S. | 5.1 | O2 | II | 5.1 | 274 |
| 1481 | PERCHLORATES, INORGANIC, N.O.S. | 5.1 | O2 | III | 5.1 | 274 |
| 1482 | PERMANGANATES, INORGANIC, N.O.S. | 5.1 | O2 | II | 5.1 | 274 608 |
| 1482 | PERMANGANATES, INORGANIC, N.O.S. | 5.1 | O2 | III | 5.1 | 274 608 |
| 1483 | PEROXIDES, INORGANIC, N.O.S. | 5.1 | O2 | II | 5.1 | 274 |
| 1483 | PEROXIDES, INORGANIC, N.O.S. | 5.1 | O2 | III | 5.1 | 274 |
| 1549 | ANTIMONY COMPOUND, INORGANIC, SOLID, N.O.S. | 6.1 | T5 | III | 6.1 | 45 274 512 |
| 1556 | ARSENIC COMPOUND, LIQUID, N.O.S., inorganic, including: Arsenates, n.o.s., Arsenites, n.o.s.; and Arsenic sulphides, n.o.s. | 6.1 | T4 | I | 6.1 | 43 274 |
| 1556 | ARSENIC COMPOUND, LIQUID, N.O.S., inorganic, including: Arsenates, n.o.s., Arsenites, n.o.s.; and Arsenic sulphides, n.o.s. | 6.1 | T4 | II | 6.1 | 43 274 |
| 1556 | ARSENIC COMPOUND, LIQUID, N.O.S., inorganic, including: Arsenates, n.o.s., Arsenites, n.o.s.; and Arsenic sulphides, n.o.s. | 6.1 | T4 | III | 6.1 | 43 274 |
| 1557 | ARSENIC COMPOUND, SOLID, N.O.S., inorganic, including: Arsenates, n.o.s.; Arsenites, n.o.s.; and Arsenic sulphides, n.o.s. | 6.1 | T5 | I | 6.1 | 43 274 |
| 1557 | ARSENIC COMPOUND, SOLID, N.O.S., inorganic, including: Arsenates, n.o.s.; Arsenites, n.o.s.; and Arsenic sulphides, n.o.s. | 6.1 | T5 | II | 6.1 | 43 274 |
| 1557 | ARSENIC COMPOUND, SOLID, N.O.S., inorganic, including: Arsenates, n.o.s.; Arsenites, n.o.s.; and Arsenic sulphides, n.o.s. | 6.1 | T5 | III | 6.1 | 43 274 |
| 1564 | BARIUM COMPOUND, N.O.S. | 6.1 | T5 | II | 6.1 | 177 274 513 587 |
| 1564 | BARIUM COMPOUND, N.O.S. | 6.1 | T5 | III | 6.1 | 177 274 513 587 |
| 1566 | BERYLLIUM COMPOUND, N.O.S. | 6.1 | T5 | II | 6.1 | 274 514 |
| 1566 | BERYLLIUM COMPOUND, N.O.S. | 6.1 | T5 | III | 6.1 | 274 514 |
| 1583 | CHLOROPICRIN MIXTURE, N.O.S. | 6.1 | T1 | I | 6.1 | 274 315 515 |
| 1583 | CHLOROPICRIN MIXTURE, N.O.S. | 6.1 | T1 | II | 6.1 | 274 515 |
| 1583 | CHLOROPICRIN MIXTURE, N.O.S. | 6.1 | T1 | III | 6.1 | 274 515 |
| 1655 | NICOTINE COMPOUND, SOLID, N.O.S. or NICOTINE PREPARATION, SOLID, N.O.S. | 6.1 | T2 | I | 6.1 | 43 274 |
| 1655 | NICOTINE COMPOUND, SOLID, N.O.S. or NICOTINE PREPARATION, SOLID, N.O.S. | 6.1 | T2 | II | 6.1 | 43 274 |
| 1655 | NICOTINE COMPOUND, SOLID, N.O.S. or NICOTINE PREPARATION, SOLID, N.O.S. | 6.1 | T2 | III | 6.1 | 43 274 |
| 1740 | HYDROGENDIFLUORIDES, N.O.S. | 8 | C2 | II | 8 | 274 517 |
| 1740 | HYDROGENDIFLUORIDES, N.O.S. | 8 | C2 | III | 8 | 274 517 |
| 1851 | MEDICINE, LIQUID, TOXIC, N.O.S. | 6.1 | T1 | II | 6.1 | 221 274 601 |
| 1851 | MEDICINE, LIQUID, TOXIC, N.O.S. | 6.1 | T1 | III | 6.1 | 221 274 601 |
| 1935 | CYANIDE SOLUTION, N.O.S. | 6.1 | T4 | I | 6.1 | 274 525 |
| 1935 | CYANIDE SOLUTION, N.O.S. | 6.1 | T4 | II | 6.1 | 274 525 |
| 1935 | CYANIDE SOLUTION, N.O.S. | 6.1 | T4 | III | 6.1 | 274 525 |
| 2024 | MERCURY COMPOUND, LIQUID, N.O.S. | 6.1 | T4 | I | 6.1 | 43 274 |
| 2024 | MERCURY COMPOUND, LIQUID, N.O.S. | 6.1 | T4 | II | 6.1 | 43 274 |
| 2024 | MERCURY COMPOUND, LIQUID, N.O.S. | 6.1 | T4 | III | 6.1 | 43 274 |
| 2025 | MERCURY COMPOUND, SOLID, N.O.S. | 6.1 | T5 | I | 6.1 | 43 274 529 585 |
| 2025 | MERCURY COMPOUND, SOLID, N.O.S. | 6.1 | T5 | II | 6.1 | 43 274 529 585 |
| 2025 | MERCURY COMPOUND, SOLID, N.O.S. | 6.1 | T5 | III | 6.1 | 43 274 529 585 |
| 2026 | PHENYLMERCURIC COMPOUND, N.O.S. | 6.1 | T3 | I | 6.1 | 43 274 |
| 2026 | PHENYLMERCURIC COMPOUND, N.O.S. | 6.1 | T3 | II | 6.1 | 43 274 |
| 2026 | PHENYLMERCURIC COMPOUND, N.O.S. | 6.1 | T3 | III | 6.1 | 43 274 |
| 2291 | LEAD COMPOUND, SOLUBLE, N.O.S. | 6.1 | T5 | III | 6.1 | 199 274 535 |
| 2430 | ALKYLPHENOLS, SOLID, N.O.S. (including C2-C12 homologues) | 8 | C4 | I | 8 | 274 |
| 2430 | ALKYLPHENOLS, SOLID, N.O.S. (including C2-C12 homologues) | 8 | C4 | II | 8 | 274 |
| 2430 | ALKYLPHENOLS, SOLID, N.O.S. (including C2-C12 homologues) | 8 | C4 | III | 8 | 274 |
| 2445 | LITHIUM ALKYLS, LIQUID | 4.2 | SW | I | 4.2 +4.3 | 274 320 |
| 2570 | CADMIUM COMPOUND | 6.1 | T5 | I | 6.1 | 274 596 |
| 2570 | CADMIUM COMPOUND | 6.1 | T5 | II | 6.1 | 274 596 |
| 2570 | CADMIUM COMPOUND | 6.1 | T5 | III | 6.1 | 274 596 |
| 2583 | ALKYLSULPHONIC ACIDS, SOLID or ARYLSULPHONIC ACIDS, SOLID with more than 5% free sulphuric acid | 8 | C2 | II | 8 | 274 |
| 2584 | ALKYLSULPHONIC ACIDS, LIQUID or ARYLSULPHONIC ACIDS, LIQUID with more than 5% free sulphuric acid | 8 | C1 | II | 8 | 274 |
| 2585 | ALKYLSULPHONIC ACIDS, SOLID or ARYLSULPHONIC ACIDS, SOLID with not more than 5% free sulphuric acid | 8 | C4 | III | 8 | 274 |
| 2586 | ALKYLSULPHONIC ACIDS, LIQUID or ARYLSULPHONIC ACIDS, LIQUID with not more than 5% free sulphuric acid | 8 | C3 | III | 8 | 274 |
| 2627 | NITRITES, INORGANIC, N.O.S. | 5.1 | O2 | II | 5.1 | 103 274 |
| 2630 | SELENATES or SELENITES | 6.1 | T5 | I | 6.1 | 274 |
| 2742 | CHLOROFORMATES, TOXIC, CORROSIVE, FLAMMABLE, N.O.S. | 6.1 | TFC | II | 6.1 +3 +8 | 274 561 |
| 2837 | BISULPHATES, AQUEOUS SOLUTION | 8 | C1 | II | 8 | 274 |
| 2837 | BISULPHATES, AQUEOUS SOLUTION | 8 | C1 | III | 8 | 274 |
| 2856 | FLUOROSILICATES, N.O.S. | 6.1 | T5 | III | 6.1 | 274 |
| 2881 | METAL CATALYST, DRY | 4.2 | S4 | I | 4.2 | 274 |
| 2881 | METAL CATALYST, DRY | 4.2 | S4 | II | 4.2 | 274 |
| 2881 | METAL CATALYST, DRY | 4.2 | S4 | III | 4.2 | 274 |
| 2985 | CHLOROSILANES, FLAMMABLE, CORROSIVE, N.O.S. | 3 | FC | II | 3 +8 | 274 548 |
| 2986 | CHLOROSILANES, CORROSIVE, FLAMMABLE, N.O.S. | 8 | CF1 | II | 8 +3 | 274 548 |
| 2987 | CHLOROSILANES, CORROSIVE, N.O.S. | 8 | C3 | II | 8 | 274 548 |
| 2988 | CHLOROSILANES, WATER-REACTIVE, FLAMMABLE, CORROSIVE, N.O.S. | 4.3 | WFC | I | 4.3 +3 +8 | 274 549 |
| 3051 | ALUMINIUM ALKYLS | 4.2 | SW | I | 4.2 +4.3 | 274 320 |
| 3052 | ALUMINIUM ALKYL HALIDES, LIQUID | 4.2 | SW | I | 4.2 +4.3 | 274 320 |
| 3053 | MAGNESIUM ALKYLS | 4.2 | SW | I | 4.2 +4.3 | 274 320 |
| 3076 | ALUMINIUM ALKYL HYDRIDES | 4.2 | SW | I | 4.2 +4.3 | 274 320 |
| 3089 | METAL POWDER, FLAMMABLE, N.O.S. | 4.1 | F3 | II | 4.1 | 274 552 |
| 3089 | METAL POWDER, FLAMMABLE, N.O.S. | 4.1 | F3 | III | 4.1 | 274 552 |
| 3141 | ANTIMONY COMPOUND, INORGANIC, LIQUID, N.O.S. | 6.1 | T4 | III | 6.1 | 45 274 512 |
| 3144 | NICOTINE COMPOUND, LIQUID, N.O.S. or NICOTINE PREPARATION, LIQUID, N.O.S. | 6.1 | T1 | I | 6.1 | 43 274 |
| 3144 | NICOTINE COMPOUND, LIQUID, N.O.S. or NICOTINE PREPARATION, LIQUID, N.O.S. | 6.1 | T1 | II | 6.1 | 43 274 |
| 3144 | NICOTINE COMPOUND, LIQUID, N.O.S. or NICOTINE PREPARATION, LIQUID, N.O.S. | 6.1 | T1 | III | 6.1 | 43 274 |
| 3145 | ALKYLPHENOLS, LIQUID, N.O.S. (including C2-C12 homologues) | 8 | C3 | I | 8 | 274 |
| 3145 | ALKYLPHENOLS, LIQUID, N.O.S. (including C2-C12 homologues) | 8 | C3 | II | 8 | 274 |
| 3145 | ALKYLPHENOLS, LIQUID, N.O.S. (including C2-C12 homologues) | 8 | C3 | III | 8 | 274 |
| 3167 | GAS SAMPLE, NON-PRESSURIZED, FLAMMABLE, N.O.S., not refrigerated liquid | 2 | 7F |  | 2.1 | 274 |
| 3168 | GAS SAMPLE, NON-PRESSURIZED, TOXIC, FLAMMABLE, N.O.S., not refrigerated liquid | 2 | 7TF |  | 2.3 +2.1 | 274 |
| 3169 | GAS SAMPLE, NON-PRESSURIZED, TOXIC, N.O.S., not refrigerated liquid | 2 | 7T |  | 2.3 | 274 |
| 3210 | CHLORATES, INORGANIC, AQUEOUS SOLUTION, N.O.S. | 5.1 | O1 | II | 5.1 | 274 605 |
| 3210 | CHLORATES, INORGANIC, AQUEOUS SOLUTION, N.O.S. | 5.1 | O1 | III | 5.1 | 274 605 |
| 3211 | PERCHLORATES, INORGANIC, AQUEOUS SOLUTION, N.O.S. | 5.1 | O1 | II | 5.1 | 274 |
| 3211 | PERCHLORATES, INORGANIC, AQUEOUS SOLUTION, N.O.S. | 5.1 | O1 | III | 5.1 | 274 |
| 3212 | HYPOCHLORITES, INORGANIC, N.O.S. | 5.1 | O2 | II | 5.1 | 274 559 |
| 3213 | BROMATES, INORGANIC, AQUEOUS SOLUTION, N.O.S. | 5.1 | O1 | II | 5.1 | 274 604 |
| 3213 | BROMATES, INORGANIC, AQUEOUS SOLUTION, N.O.S. | 5.1 | O1 | III | 5.1 | 274 604 |
| 3214 | PERMANGANATES, INORGANIC, AQUEOUS SOLUTION, N.O.S. | 5.1 | O1 | II | 5.1 | 274 608 |
| 3215 | PERSULPHATES, INORGANIC, N.O.S. | 5.1 | O2 | III | 5.1 | 274 |
| 3216 | PERSULPHATES, INORGANIC, AQUEOUS SOLUTION, N.O.S. | 5.1 | O1 | III | 5.1 | 274 |
| 3218 | NITRATES, INORGANIC, AQUEOUS SOLUTION, N.O.S. | 5.1 | O1 | II | 5.1 | 270 274 511 |
| 3218 | NITRATES, INORGANIC, AQUEOUS SOLUTION, N.O.S. | 5.1 | O1 | III | 5.1 | 270 274 511 |
| 3219 | NITRITES, INORGANIC, AQUEOUS SOLUTION, N.O.S. | 5.1 | O1 | II | 5.1 | 103 274 |
| 3219 | NITRITES, INORGANIC, AQUEOUS SOLUTION, N.O.S. | 5.1 | O1 | III | 5.1 | 103 274 |
| 3248 | MEDICINE, LIQUID, FLAMMABLE, TOXIC, N.O.S. | 3 | FT1 | II | 3 +6.1 | 220 221 274 601 |
| 3248 | MEDICINE, LIQUID, FLAMMABLE, TOXIC, N.O.S. | 3 | FT1 | III | 3 +6.1 | 220 221 274 601 |
| 3249 | MEDICINE, SOLID, TOXIC, N.O.S. | 6.1 | T2 | II | 6.1 | 221 274 601 |
| 3249 | MEDICINE, SOLID, TOXIC, N.O.S. | 6.1 | T2 | III | 6.1 | 221 274 601 |
| 3256 | ELEVATED TEMPERATURE LIQUID, FLAMMABLE, N.O.S. with flash-point above 60 °C, at or above its flash-point | 3 | F2 | III | 3 | 274 560 |
| 3257 | ELEVATED TEMPERATURE LIQUID, N.O.S., at or above 100 °C and below its flash-point (including molten metals, molten salts, etc.) | 9 | M9 | III | 9 | 274 580 643 |
| 3258 | ELEVATED TEMPERATURE SOLID, N.O.S., at or above 240 °C | 9 | M10 | III | 9 | 274 580 643 |
| 3283 | SELENIUM COMPOUND, SOLID, N.O.S. | 6.1 | T5 | I | 6.1 | 274 563 |
| 3283 | SELENIUM COMPOUND, SOLID, N.O.S. | 6.1 | T5 | II | 6.1 | 274 563 |
| 3283 | SELENIUM COMPOUND, SOLID, N.O.S. | 6.1 | T5 | III | 6.1 | 274 563 |
| 3284 | TELLURIUM COMPOUND, N.O.S. | 6.1 | T5 | I | 6.1 | 274 |
| 3284 | TELLURIUM COMPOUND, N.O.S. | 6.1 | T5 | II | 6.1 | 274 |
| 3284 | TELLURIUM COMPOUND, N.O.S. | 6.1 | T5 | III | 6.1 | 274 |
| 3285 | VANADIUM COMPOUND, N.O.S. | 6.1 | T5 | I | 6.1 | 274 564 |
| 3285 | VANADIUM COMPOUND, N.O.S. | 6.1 | T5 | II | 6.1 | 274 564 |
| 3285 | VANADIUM COMPOUND, N.O.S. | 6.1 | T5 | III | 6.1 | 274 564 |
| 3361 | CHLOROSILANES, TOXIC, CORROSIVE, N.O.S. | 6.1 | TC1 | II | 6.1 +8 | 274 |
| 3362 | CHLOROSILANES, TOXIC, CORROSIVE, FLAMMABLE, N.O.S. | 6.1 | TFC | II | 6.1 +3 +8 | 274 |
| 3401 | ALKALI METAL AMALGAM, SOLID | 4.3 | W2 | I | 4.3 | 182 274 |
| 3402 | ALKALINE EARTH METAL AMALGAM, SOLID | 4.3 | W2 | I | 4.3 | 183 274 506 |
| 3433 | LITHIUM ALKYLS, SOLID | 4.2 | SW | I | 4.2+4.3 | 274 320 |
| 3440 | SELENIUM COMPOUND, LIQUID, N.O.S. | 6.1 | T4 | I | 6.1 | 274 563 |
| 3440 | SELENIUM COMPOUND, LIQUID, N.O.S. | 6.1 | T4 | II | 6.1 | 274 563 |
| 3440 | SELENIUM COMPOUND, LIQUID, N.O.S. | 6.1 | T4 | III | 6.1 | 274 563 |
| 3461 | ALUMINIUM ALKYL HALIDES, SOLID | 4.2 | SW | I | 4.2 +4.3 | 274 320 |

__________