Clarification for draft amendment to the proposal for the 11 series of amendments to

Regulation No. 13       (ECE/TRANS/WP.29/2007/106)

The table reproduced below was prepared by the expert from the UK.  It is aimed at clarifying the numerous permutations of ESC fitment to vehicles with different braking systems contained in the implementation table outlined in paragraph 12.4.1.

| Vehicle category | Application date (period after entry into force of the 11 series of amendments) |
| --- | --- |
|  | Contracting Parties [may/shall] refuse type approval to vehicles not meeting the applicable requirements. | Contracting Parties [may/shall] refuse first entry into service of vehicles not meeting the applicable requirements. |
| M2 | 60 months | 84 months |
| M3 (Class III) M3 <16 tonnes (air brakes) M3 (Class III)1 (hydraulic brakes) M3 (Class III) 1 (air/hydraulic brakes) | 12 months 24 months 60 months 72 months | 36 months 48 months 84 months 96 months |
| M3 (other than above) M3 (Class II and B) (hydraulic brakes) M3 (Class II2) (air/hydraulic brakes) | 24 months 60 months 72 months | 48 months 84 months 96 months |
| N2 N2 (hydraulic brakes) N2 (air/hydraulic brakes) | 48 months 60 months 72 months | 72 months 84 months 96 months |
| N3 (2 axle tractors for semi-trailers) N3 (2 axle tractors for semi-trailers with air brakes/abs) | 12 months 36 months | 36 months 60 months |
| N3 (other than above) N3 (3 axles with EBS) N3 (3 axles with air brakes/abs) | 24 months 36 months 48 months | 48 months 60 months 72 months |
| O3 O3 (combined axle load between 3.5 - 7.5 tonnes) | 36 months 48 months | 60 months 72 months |
| O4 | 24 months | 36 months |

- - - - -

# Footnotes

Class III - vehicles constructed exclusively for the carriage of seated passengers.

Class II - vehicles constructed principally for the carriage of seated passengers, and designed to allow the carriage of standing passengers in the gangway and/or in an area which does not exceed the space provided for two double seats.

Class B - vehicles not designed to carry standing passengers; a vehicle of this class has no provision for standing passengers