| UNITED NATIONS |  | ST |
| --- | --- | --- |
|  | Secretariat | Distr. GENERAL ST/SG/AC.10/C.3/2008/80 16 September 2008 Original: ENGLISH |

## COMMITTEE OF EXPERTS ON THE TRANSPORT OF

# DANGEROUS GOODS AND ON THE GLOBALLY

# HARMONIZED SYSTEM OF CLASSIFICATION

# AND LABELLING OF CHEMICALS

# Sub-Committee of Experts on the

# Transport of Dangerous Goods

# Thirty-fourth session

# Geneva, 1-9 December 2008

# Item 4 of the provisional agenda

# LISTING, CLASSIFICATION AND PACKING

Thiourea dioxide (UN 3341): Subsidiary risk 6.1

Submitted by the expert from Germany

Introduction

1.	Following a series of accidents, the Sub-Committee, at its twelfth session in 1996, included Thiourea dioxide in the Dangerous Goods List under entry UN 3341, Division 4.2, Packing Group (PG) II or III.

2.	According to available experimental data, Thiourea dioxide also fulfils the criteria for classification under Division 6.1: an acute inhalation toxicity study was performed according to OECD test guideline 403 with a nebulised aqueous solution. From the results an LC50 value of 0.656 mg/l/1 h (equivalent to 0,164 mg/l/4 h) can be determined, which falls into the range for classification under Division 6.1, PG II.

3.	According to the UN Model Regulations, paragraph 2.0.3, (Precedence of hazard characteristics), Thiourea dioxide would thus need to be classified either

(a)	Under Division 4.2, subsidiary risk 6.1 in cases where its Division 4.2 characteristics fall into PG II; or

(b)	Under Division 6.1, subsidiary risk 4.2 in cases where its Division 4.2 characteristics fall into PG III.

In both cases, the substance would need to be transported according to the provisions assigned to the PG II performance level since the Division 6.1 characteristics fall into PG II in any case. For pragmatic reasons, the expert from Germany proposes to retain the present listing under Division 4.2, PG II only, and amend entry UN 3341 to add the subsidiary risk of 6.1 as outlined below.

4.	The relevant data for assignment to Division 6.1 (not to Division 4.2 as it is not affected by this proposal) are contained in the Annex to this document.

### Proposal

5.	In Chapter 3.2, dangerous goods list,

a)	Amend entry for UN 3341, PG II, to read:

| UN No. | Name and description | Class or division | Subsidiary risk | UN packing group | Special provisions | Limited and excepted quantities | Packagings and IBC’s | Portable tanks and bulk containers |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  |  |  | Packing instruction | Special provisions | Instruction | Special provisions |
| (1) | (2) | (3) | (4) | (5) | (6) | (7a) | (7b) | (8) | (9) | (10) | (11) |
| 3341 | Thiourea dioxide | 4.2 | 6.1 | II | - | 0 | E2 | P002 IBC06 | B2 | T3 | TP 33 |

b)	Delete the entry for UN 3341, PG III:

Annex

(English only)

Section 5. HARMFUL BIOLOGICAL EFFECTS

5.1	LD50, oral (2.6.2.1.11)	1120 mg/kg	Animal species rat

LD50, oral (2.6.2.1.11)	1486 mg/kg	Animal species mouse

5.2	LD50, dermal (2.6.2.1.21)	>2000 mg/kg Animal species rat

5.3	LC50, inhalation (2.6.2.1.31)	0.164 mg/l	Exposure time	4 hours

or		ml/m3	Animal species rat

5.4	Saturated vapour concentration at 20 °C (2.6.2.2.4.31)	not applicable

5.5	Skin exposure (2.81) results irritating	Exposure time 	24 hours

Animal species	rabbit

5.6	Other data

Fish (Poecilia reticulate), LC50 (96 h): 416 mg/l

Aquatic invertebrates (Daphnia magna), EC50 (24 h): 390 mg/l

Aquatic plants (Scenedesmus subspicatus), EC50 (72 h): 32 mg/l

5.7	Human experience

Airborne dust may irritate eyes, skin, or respiratory tract. Direct or continuous contact may irritate skin.

_______________

# Footnotes

In accordance with the programme of work of the Sub-Committee for 2007-2008 approved by the Committee at its third session (refer to ST/SG/AC.10/C.3/60 para. 100 and ST/SG/AC.10/34, para. 14)

1	This references are to chapters and paragraphs in the Model Regulations on the Transport of Dangerous Goods.