| UNITED NATIONS |  | E |
| --- | --- | --- |
|  | Economic and Social Council | Distr. GENERAL ECE/TRANS/WP.15/AC.2/2008/3/Add.1 13 November 2007 ENGLISH Original: FRENCH |

ECONOMIC COMMISSION FOR EUROPE

INLAND TRANSPORT COMMITTEE

Working Party on the Transport of Dangerous Goods

Joint Meeting of Experts on the Regulations annexed to the
European Agreement concerning the International Carriage
of Dangerous Goods by Inland Waterways (ADN)*

Twelfth session
Geneva, 21-25 January 2008
Item 4 (b) of the provisional agenda

# PROPOSALS FOR AMENDMENTS TO THE REGULATIONS
ANNEXED TO ADN**

## Protection of the aquatic environment

## Note by the secretariat

## Addendum

1.	The secretariat’s attention has been drawn to the fact that the 2009 draft amendments to RID/ADR provide for a classification flowchart (taken from the UN Model Regulations, para. 2.9.3.3) in 2.2.9.1.10 of RID/ADR (see ECE/TRANS/WP.15/AC.1/2007/51, annex 2).

2.	This flowchart was not reproduced in the secretariat’s proposal because it applies only to carriage in packages and could create confusion where transport in tank vessels is concerned. However, should the Joint Meeting of Experts consider such a flowchart useful, the secretariat has prepared a more complete one, reproduced below, which may be applied to both carriage in packages and transport in tank vessels, for example as 2.2.9.1.10.4 or 2.4.3.2.

Classification flowchart for environmentally hazardous substances

EHS = Environmentally hazardous substance

# Footnotes

*  This meeting is organized jointly by the Economic Commission for Europe and the Central Commission for the Navigation of the Rhine.

**  Distributed in German by the Central Commission for the Navigation of the Rhine under the symbol CCNR/ZKR/ADN/WP.15/AC.2/2008/3/Add.1.

# Text boxes

Rapidly 
degradable

Bioaccumulation

EHS 
Acute 1

EHS 
Chronic 1

No

Yes

Yes

No

Yes

No

L(E)C50*≤ 1 mg/l

NOEC > 1 mg/l

L(E)C50* ≤ 10 mg/l

Rapidly 
degradable

Bioaccumulation

EHS

(in tank vessels only) 
Acute 2

EHS 
Chronic 2

No

Yes

Yes

No or unknown

No

No

(Not subject to ADN
 in packages)

Not EHS

under ADN

Not EHS

EHS

(in tank vessels only) 
Chronic 3

10 < L(E)C50* ≤ 100 mg/l

Rapidly 
degradable

Bioaccumulation

EHS

(in tank vessels only) 
Acute 3

Yes

No

Yes

Yes

Yes

Yes

No

-----