| UNITED NATIONS |  | E |
| --- | --- | --- |
|  | Economic and Social Council | Distr. GENERAL ECE/TRANS/WP.29/2008/85 25 July 2008 Original: ENGLISH |

ECONOMIC COMMISSION FOR EUROPE

INLAND TRANSPORT COMMITTEE

World Forum for Harmonization of Vehicle Regulations

# One-hundred-and-forty-sixth session

Geneva, 11-14 November 2008

Item 4.2.17 of the provisional agenda

1958 AGREEMENT

Consideration of draft amendments to existing Regulations

Proposal for Corrigendum 1 to Revision 4 to Regulation No. 48

(Installation of lighting and light-signalling devices)

Submitted by the Working Party on Lighting and Light-Signalling (GRE) (/

The text reproduced below was adopted by GRE at its fifty-ninth session.  It is based on ECE/TRANS/WP.29/GRE/2008/21, as amended by Annex II to the report (see ECE/TRANS/WP.29/GRE/59, para.19).  It is submitted to WP.29 and AC.1 for consideration.

Paragraph 5.23., amend to read:

"5.23.	Lamps shall be fitted in a vehicle in such a way that the light source can be correctly replaced by the driver without the need for special tools, other than those provided with the vehicle by the manufacturer.  The vehicle manufacturer shall provide with the vehicle a detailed description of the procedure for replacement.  This paragraph is not applicable to:

(a)	Devices approved with a non-replaceable light source;

(b)	Devices approved with light sources according to Regulation No. 99."

- - - - -

# Footnotes

(/ In accordance with the programme of work of the Inland Transport Committee for 2006-2010 (ECE/TRANS/166/Add.1, programme activity 02.4), the World Forum will develop, harmonize and update Regulations in order to enhance performance of vehicles.  The present document is submitted in conformity with that mandate.