| Transmitted by the informal group on WMTC | Informal document No. GRPE-56-11 (56th GRPE, 3-6 June 2008, agenda item 4) |
| --- | --- |

Report on data collection as a basis for the discussion about the introduction of performance requirements in GTR No. 2 (World-wide harmonized motorcycle emission test cycle (WMTC))

1.	Introduction

After the establishment into the Global Registry of GTR No. 2 in June 2005, the work on Stage 2 of the World-wide harmonized motorcycle emission test cycle (WMTC) started.  One of issues for consideration in Stage 2 of WMTC was the introduction of performance requirements.  The informal group was mandated by AC.3 (ECE/TRANS/WP.29/AC.3/19) to collect data and prepare information as a basis for the discussion.

With the status report to GRPE in June 2006 (inf doc No. GRPE-52-6) the WMTC informal group recommends focusing on only limit values in Stage 2.  The discussion about the worldwide harmonization of other performance requirements like durability, off cycle emissions or evaporative emissions should be postponed to a subsequent Stage 3.

In line with the 1998 Agreement, Contracting Parties are preparing proposals for the introduction of GTR No. 2 as an alternative to the existing national/regional legislation.  This set of limit values is the basic information about the current legal situation regarding WMTC application.  In parallel, IMMA has collected comparative data and test results for a correlation study, based on technology and regulations that will be in use/force in 2006-08.  This can be the basis for further discussion by Contracting Parties of a possible harmonization of limit values, aiming on a timeframe of 2010 – 2012.

2.	Existing national / regional legislation (pollutant emissions) for motorcycles

The following tables gives only a rough summary of the limit values. More detailed information about some of the the national legislation can be found in the ANNEX. The tables below don't include mopeds (< 50 ccm), so "all" means > 50 ccm.

2.1.	China

| cycle | classification | stage | CO g/km | HC g/km | NOx g/km | HC+NOx g/km |
| --- | --- | --- | --- | --- | --- | --- |
| ECE R 40 | all | 2004 | 5,5 | 1,2 | 0,3 | - |
| ECE R 40 (cold) | < 150 ccm | 2007/8 | 2,0 | 0,8 | 0,15 | - |
| ECE R 40 + EUDC (max. 90 km/h) | > 150 | 2007/8 | 2,0 | 0,3 | 0,15 | - |

2.2.	EU

| cycle | classification | stage | CO g/km | HC g/km | NOx g/km | HC+NOx g/km |
| --- | --- | --- | --- | --- | --- | --- |
| ECE R 40 | < 150 ccm | 2003/4 | 5,5 | 1,2 | 0,3 | - |
| ECE R 40 | > 150 ccm | 2003/4 | 5,5 | 1,0 | 0,3 | - |
| ECE R 40 (cold) | < 150 ccm | 2006/7 | 2,0 | 0,8 | 0,15 | - |
| ECE R 40 + EUDC | > 150 ccm | 2006/7 | 2,0 | 0,3 | 0,15 | - |

2.3.	India

| cycle | classification | stage | CO g/km | HC g/km | NOx g/km | HC+NOx g/km |
| --- | --- | --- | --- | --- | --- | --- |
| IDC | all | 2005 | 1,5 | - | - | 1,5 |
| IDC | all | 2008/10 | 1,0 | - | - | 1,0 |

Note: Durability factor of 1.2 is applicable on above norms for CO & HC+NOx

2.4.	Japan

| cycle | classification | stage | CO g/km | HC g/km | NOx g/km | HC+NOx g/km |
| --- | --- | --- | --- | --- | --- | --- |
| TRIAS/LA4 | all / 2stroke | 1999 | 8,0 | 3,0 | 0,1 | - |
| TRIAS/LA4 | all / 4stroke | 1999 | 13,0 | 2,0 | 0,33 | - |
| TRIAS/LA4 | < 125 ccm | 2008 | 2,0 | 0,3 | 0,15 | - |
| TRIAS/LA4 | > 125 ccm | 2008 | 2,0 | 0,5 | 0,15 |  |

2.5.	Korea

| cycle | classification | stage | CO g/km | HC g/km | NOx g/km | HC+NOx g/km |
| --- | --- | --- | --- | --- | --- | --- |
| ECE R 40 | all | - | 8,0 | 4,0 | 0,1 | - |

2.6.	US

| cycle | classification | stage | CO g/km | HC g/km | NOx g/km | HC+NOx g/km |
| --- | --- | --- | --- | --- | --- | --- |
| FTP | < 170 ccm | 2006 | 12,0 | 1,0 | - |  |
| FTP | 170 - 279 | 2006 | 12,0 | 1,0 | - |  |
| FTP | > 280 | 2006 | 12,0 | - | - | 1,4 |
| FTP | > 280 | 2010 | 12,0 | - | - | 0,8 |

3.	Status of transposition of GTR No. 2 into national / regional legislation

3.1.	EU

With directive 2006/72/EC the EU transposed GTR No 2 into directive 97/24/EC.  Equivalent to Euro 3 (see above 2.2.) manufacturers optional can choose for type approval the following limits:

Table: WMTC limits correlated to EURO 3 stage

| cycle | classification | CO g/km | HC g/km | NOx g/km |
| --- | --- | --- | --- | --- |
| WMTC-old (stage 1) | vmax < 130 km/h | 2,62 | 0,75 | 0,17 |
| WMTC-old (stage 1) | vmax > 130 km/h | 2,62 | 0,33 | 0,22 |

3.2.	Japan

Based on emissions tests with motorcycles meeting the latest emission legislation, Japan will establish equivalent limits on WMTC within 2008.  Then the procedures for transposition of GTR No. 2 as an option will be started.  It can be expected, that the WMTC based limit values are on a similar level as in 3.1..

3.3.	China

China is estimated to follow the EU approach.

3.4.	US

The USA expects to introduce the WMTC as an alternative to the FTP with equivalent limits to the present USA emission regulations.  After some period of time (which would be determined through the US rulemaking process), the US intends to phase out the FTP option and ultimately rely exclusively on the WMTC for motorcycle certification purposes.  The timing of US regulatory action is currently not determined.

3.5.	India

In India, consideration for introducing WMTC as alternative to existing Indian regulation is under discussion. Various issues such as class wise stand still values & combined HC+NOx are being debated in conjunction with fuel consumption & CO2 emissions. Date for the implementation is presently not decided.

4.	Data and test results

4.1.	Test data

The test data is tabled in Annex D. It should be taken into account that already two versions of WMTC test cycles and classification exists. The version "WMTC-stage 1" is the basis, adopted as GTR No. 2 in 2005. With amendment 1 of GTR no. 2 slight modifications of the classification (classes 1, 2-1) and the test cycles (part 1, 2 alternative) had been introduced in 2007 (version "WMTC-stage 2").

Most of the data concern Class 3 vehicles and come from the JRC data. So for this class, the results are relatively homogenous.

Class 1 and 2 data are more spread around the world. Furthermore due to market differences, legislation and technology used, one might assume that the test results may vary a lot according to the region. This is why rough data of Class 1 and class 2 vehicles were analysed by region. Annex B shows figures with the results separated for vehicles and regions for class 1 and Annex C shows the results for class 2 vehicles.

4.2.	Emission results separated for different cycles, vehicles and regions

4.2.1.	Class 1 vehicles (Figures in ANNEX E)

The updated database contains 47 class 1 motorcycles. For 26 of these motorcycles measurement values are available for the Euro 3 cycle as well as for the WMTC cycle. The figures in ANNEX E show the emission results for the Euro 3 cycle and the WMTC cycle for CO, THC, NOx and CO2. The vehicle numbers are chosen in that way that the regions China, Japan, India and Europe can clearly separated by different colours.

Figure E-1 shows the CO emissions for the Euro 3 cycle. The Chinese results range between 2,1 and 5,4 g/km, the 2 European vehicles form a similar bandwidth. The Japanese data range between 0,3 and 1,7 g/km, the Indian data is in the same range but slightly higher.

Figure E-2 shows the corresponding results for the WMTC cycle. Ranking and ranges are almost the same as for the Euro 3 cycle. Only the results for the 2 European vehicles are closer together.

Figure E-4 and Figure E-5 show the results for the THC emissions. The overall range is 0,096 to 1,07 g/km for the Euro 3 cycle and 0,068 to 0,68 g/km for the WMTC cycle. The highest variation is shown for the Chinese data and the Euro 3 cycle. In each region vehicles with 0,2 g/km or even lower emissions can be found.

The NOx emissions are shown in Figure E-7 and Figure E-8.  For the Euro 3 cycle the NOx emissions are on average higher for the Chinese data and the Indian data than for the Japanese and European data, but 2 of the Chinese vehicles and 1 of the Indian vehicles have results within the Japanese/European range. The results for the WMTC cycle have a wider spread for the Chinese and the European data than for the Euro 3 cycle. In all regions except Japan some vehicles can be found for which the WMTC results are significantly higher than for the Euro 3 cycle. For both cycles the average emissions of the Chinese and Indian vehicles are more than 2 times higher than the average emissions of the Japanese vehicles. Nevertheless and even for the WMTC cycle some Chinese vehicles have NOx emissions within the variation range of the Japanese vehicles.

The CO2 emissions are shown in Figure E-10 and Figure E-11. At first can be noticed that the emission values for the different regions are closer together than for the pollutant emissions, except for the 2 European vehicles that have significantly higher CO2 emissions than the rest. The average CO2 emissions have the following rank order in rising order: India, China, Japan, Europe. The WMTC cycle results are always lower than the Euro 3 cycle results.

Figures E-3, E-6, E-9 and E-12 show comparisons of the results for the Euro 3 and WMTC cycle for CO, THC, NOx and CO2. The 2 European vehicles are coloured in light blue, 5 Chinese vehicles with extremely lower CO2 emissions for the WMTC cycle than for the Euro 3 cycle are highlighted in yellow. The CO emissions follow a one by one trend, the THC emissions are close to that for the major part of the vehicle sample. Also the NOx emissions are close to a one by one trend for most of the vehicles but with an additional tendency to higher values for the WMTC. The average CO2 emissions of the WMTC cycle is 86% of the Euro 3 cycle, if the European and the 5 highlighted Chinese vehicles are disregarded.

4.2.2.	Class 2 vehicles (Figures in ANNEX F)

The class 2 vehicle database is still smaller than for the other classes, even if some new vehicles have been added. The whole sample consists of 29 vehicles, 16 of them belonging to class 2-1 and 13 belonging to class 2-2. For all of them results for the WMTC cycle exist, results for the Euro 3 cycle are available for 20 vehicles. Concerning the regions must be mentioned that European data is completely missing and that class 2-2 consists of 4 Japanese and 3 Indian vehicle only and 3 vehicles from Europe. Corresponding figures as shown for the class 1 sample were drawn and are shown in ANNEX F.

The CO emissions for the 2 cycles are shown in Figure F-13and Figure F-14. The highest scatter is found for the Chinese vehicles. For some vehicles the WMTC cycle shows significantly higher results than the Euro 3 cycle. One extreme example is one Indian class 2-1 vehicle where the CO emission for the WMTC is 5,3 times higher than for the Euro 3 cycle. On the other hand there is one Chinese vehicle for which the CO emissions for the WMTC cycle is only 50% of the emission for the Euro 3 cycle.

The THC emissions are shown in Figure F-16and Figure F-17. The WMTC cycle results have a lower variation range than the Euro 3 cycle. For both cycles the lowest values are found for the Japanese vehicles.

The NOx emissions are shown in Figure F-19and Figure F-20. The results show a high variation range, especially for the WMTC cycle. The Japanese vehicles determine the lower end of the bandwidth for both cycles. But 1 Chinese and 1 Indian vehicle have comparably low NOx emissions than the Japanese vehicles for the WMTC cycle.

The CO2 emissions are shown in Figure F-22and Figure F-23. The emissions for the WMTC cycle are always lower than for the Euro 3 cycle but with high individual differences. The WMTC cycle emissions are between 49% and 94% of the Euro 3 cycle emissions. For the pollutant emissions no significant difference between class 2-1 and class 2-2 was found. The CO2 emissions of the Japanese class 2-2 vehicles are significantly higher than the rest and the lower envelope of the range is performed by Chinese and Indian class 2-1 vehicles. But there is also 1 Japanese class 2-1 vehicle with the same low emission.

Figures F-15, F-18, F-21 and F-24 show comparisons of the results for the two cycles. No clear trend can be seen for the CO emissions. The THC emissions follow a one by one trend for low values but increasingly lower values for the WMTC cycle compared to the Euro 3 cycle for increasing THC values. For NOx emissions the trend is nearly the same for low emission values and almost the opposite for high values. As already stated the CO2 emissions of the WMTC cycle are always lower than for the Euro 3 cycle, but CO2 emission values of 49% to 61% of the Euro 3 cycle for the WMTC cycle can hardly be imagined.

4.3.	Evaluation of the test results - standstill limit values

4.3.1.	Explanation of the standstill limit values

When changing from one test cycle to another, the first question to be resolved in thinking about new limit values is, “What would the existing limits look like if adjusted to fit the new test cycle?” The answer to this question is, the “standstill value”.

Assuming tests done with the same vehicle under the same general test conditions, the standstill value is calculated with the following formula:

Lwmtc = Le x Rwmtc

Re

where:

Lwmtc = the limit value for the WMTC test cycle

Le = the Limit value with the existing cycle

Rwmtc = the test result with the WMTC cycle

Re = the test result with the existing test cycle

How the resulting data cloud is analysed depends on the objectives.  There are many statistical methods for finding out the stand still ratio. E.g. JRC used the method of taking the average of the ratios for each vehicle tested.  In what follows, the IMMA analysis, for example, used a regression line to establish the trend.  Such an approach means that some vehicles that would pass the existing test and limit values would not do so with the new limit values.  The linear regression method assumes that there is a linear relation ship between the emission results of the two cycles.  Where such a relation does not exist, the results arrived will be illogical tending to be irrational.  Whether the linear relationship exists or not can easily be made out by comparing the coefficient of regression (R2), which should be more than about 0.85.

The most important determinant of the comparison is the sample that is used to carry out the study. For example, IMMA’s analysis imposed a filter on the data in order to eliminate vehicles with a technology that would not be useable for a future reduction in limit values.  The data of vehicles on Euro-3 cycle exceeding the Euro 2 limits were discarded.  A different basis for the comparison has been used by past and ongoing regional/national studies, such as that carried out by the European Union.

Factors that will influence the results include:

- the proportion of the different classes of vehicle in the sample: eg a sample with a high concentration of Class 3 vehicles will not necessarily adequately reflect the situation for Class 1 vehicles

- the design concept prevalent in the different markets will make it difficult to combine the results, eg a design based on fuel economy will not combine well with a design based on sports performance

- the reference fuel used

All these factors should be taken into account when considering the results and standstill values presented below.

4.3.2.	IMMA Study on standstill limit values

| Country /Region | CHINA | EU | INDIA | JPN | US |
| --- | --- | --- | --- | --- | --- |
| Stage (current) | CHN-2 | EU-3 | BS-Ⅱ | JPN-2 | EPA-Tier1 |
| Limit values (g/km) | CO | HC | NOx | CO | HC | NOx | CO | HC+ NOx | CO | HC | NOx | CO | HC+ NOx |
|  |  | <150 cc | >150 cc |  |  | <150 cc | >150 cc |  |  |  |  | <125 cc | >125 cc |  |  | <170 cc | >170 cc |
|  | 5.5 | 1.2 | 1.0 | 0.30 | 2.0 | 0.8 | 0.3 | 0.15 | 1.5 | 1.5 | 2.0 | 0.5 | 0.3 | 0.15 | 12 | 1.0 | 1.4 |
| Step-1. 2004 data | - | - | - | - | 2.42 | 0.79 | 0.34 | 0.20 | - | - | 3.29 | 0.47 | 0.35 | 0.31 | 17.0 | 1.27 | 1.77 |
| Step-2. All data | 4.48 | 0.60 | 0.54 | 0.29 | 2.82 | 0.63 | 0.37 | 0.18 | 2.65 | 1.80 | 2.54 | 0.39 | 0.27 | 0.31 | 19.3 | 1.29 | 1.77 |
| Step-2. EU-2 filter | 5.55 | 0.76 | 0.65 | 0.34 | 2.43 | 0.68 | 0.29 | 0.18 | - 3.17 | 2.02 | 1.88 | 0.42 | 0.25 | 0.21 | 22.9 | 1.43 | 2.00 |

4.3.3.	India study - class wise - standstill limit values

More background information regarding the class wise evaluation is tabled in ANNEX G

Indian Analysis has been carried out separately for each class and for each region. In the case of EURO3-WMTC correlation, analysis has been carried out with all data, and also applying EURO 2 filter.

Comments from India:

- EURO-WMTC data points of 111 available include India’s 18 and Chinese 31 vehicles, which do not reflect proper correlation, as these vehicles are not tuned for compliance to EURO 3. Indian data is based on Indian drive Cycle (IDC). Relating this data from IDC to Euro 3 norms and then equating to WMTC equivalent values does not reflect a correct correlation.

- The analysis of data on Indian motorcycles of Class 2-1, show abnormally high SS values for CO, which are not justifiable. India had expressed these reservations in the FEG meeting held in Ann Arbor on 20/21st Nov ’07, while accepting the compromise formula. We are now convinced that Part 2 (reduced speed) cycle is not suitable for India and similar countries, as the operating conditions in such regions focus on commuting and fuel efficiency, rather than high acceleration and power.

- Comparative Emission traces, highlights the abnormal increase of CO Emissions, when the same motorcycle is tested on Part 2 (reduced speed) cycle compared to Part 1(reduced speed) cycle . This explains the reason for the abnormal CO values.

- India suggests that, the provision may be made in the GTR in such a way that, Class 2.1 vehicles may also be allowed to be tested on Part 1 Reduced speed cycle.

5.	Comments and conclusions

- In some of the WMTC classes (e.g. 2-1) the data base is poor because of the low no. of tests conducted. The results should not be taken as exact figures, but can show trends.

- A difference in national / regional legislation exists concerning NOx and HC. In some cases the limits are seperated, sometimes combined (see 2.).  The reason for seperated limits maybe a focus on NOx controlling. Countries like India, focussing more on fuel consumption and CO2 emissions, prefer a combined limit value.  USA also follows a combined HC+NOx.

- Harmonisation of reference fuel is an important condition for the introduction of harmonised limit values, because on the influence on the results of emission tests.

- A comparison of the level of limit values from national / regional legislation is limited because of the following reasons:
-- different classification,
-- motorcycles maybe designed for different purposes, like high performance or low fuel consumption,
-- engines are designed to meet the existing limit values under the special test conditions like cycle, cold/warm-start, reference fuel.

- Concerning the suggestion made by India above, the WMTC informal group recommends to avoid any additional amendment of the test cycles and classification in GTR No. 2 for the time being. Special situations in Contracting Parties can be taken into account by exemptions in the transposition of GTR No. 2 into national legislation.

ANNEX A - Chinese legislation

The Chinese national exhaust emission legislation for motorcycles, tricycles and mopeds is modelled on the corresponding EU Directives and is summarised in the table below.

Table: Summary of Motorcycle Emission Standards of China

ANNEX B - Indian legislation

Indian emission test and norms were made applicable from 1991. Test cycle was based on the data collections in major cities in 1988, which was representative of the driving pattern in the cities. The Indian driving cycle is consisting of the series of phases idling, cruising, acceleration & deceleration. The distance of one cycle is 0.658km and period of time 108sec. The overall cycle consists of combination of 6 such cycles. The total distance covered during the emission test is 3.948 km, average speed is 29.93 km/hr & maximum speed is 42 km/hr. Maximum acceleration is 0.65 m/sec seq & deceleration is 0.56 m/sec seq. India’s current & proposed regulations are based on combining HC & Nox for better fuel consumption & less CO2 emission. Controlling of NOx independent of HC has an adverse effect on the fuel consumption and CO2 emission. Motorcycles in India are specifically earmarked for introduction of CO2/ Fuel consumption regulation due to the large number of vehicles operating on Indian roads (74% of total fleet of vehicles).

In view of the above, India recommends that an option of a combined HC + NOx limit value should be included.

Existing / Proposed Indian legislation for motorcycles:

| Regulation | Vehicle Type | Effective Date | CO (gm/km) | HC+NOx (g/km) |
| --- | --- | --- | --- | --- |
| India BSII | All 2 W | 2005 | 1.5 | 1.5 |
| India BSIII | All 2 W | 2010 | 1.0 | 1.0 |

Note : Durability factor of 1.2 is applicable on above norms for CO & HC+NOx

ANNEX C - US legislation

The emissions test procedure used by the United States for motorcycle emission testing is known as the Federal Test Procedure (FTP).  The FTP was designed to measure a vehicle's tailpipe emissions under urban driving conditions.  The driving cycle used for the FTP was developed in the mid-1960's to represent home-to-work commuting in Los Angeles, California.  The FTP includes a series of accelerations, decelerations, and idling (such as at stop lights).  It also includes starting the vehicle after it has been parked for an extended period of time (called a “cold start”), as well as a start on a warmed-up engine (called a “hot start”).  The total distance covered by the FTP is about 11 miles and the average speed is about 21 mph, with a maximum speed of about 56 mph.  The maximum acceleration rate is a relatively mild 3.3 mph/sec, which is due to the limitations of the dynamometer technology at the time the test was developed.

Federal regulations currently define a motorcycle as “any motor vehicle with a headlight, taillight, and stoplight and having: two wheels, or three wheels and a curb mass less than or equal to 793 kilograms (1749 pounds)” (see 40 CFR 86.402-98). Note that any motorcycle or motorcycle-like vehicle that falls outside that definition would be considered a nonroad vehicle and be subject to different requirements.

Table: Current U.S. Motorcycle Exhaust Emission Standards

| Class | Engine Size (cc) | Model Year Effective Date | HC (g/km) | HC+NOx (g/km) | CO (g/km) |
| --- | --- | --- | --- | --- | --- |
| I | Less than 170 | 2006 | 1.0 | -- | 12.0 |
| II | 170-279 | 2006 | 1.0 | -- | 12.0 |
| III | 280 and greater | 2006 | -- | 1.4 | 12.0 |
|  |  | 2010 | -- | 0.8 | 12.0 |

In addition to the exhaust emission standards described above, EPA also regulates evaporative emissions from motorcycles with requirements that limit the permeation of gasoline through the walls of fuel hoses and fuel tanks.

ANNEX D		Test Data - total 134 units: 82 (stage 1 (2004)) + 52 (stage 2 (2007/8))

ANNEX E - Figures F-1 - F-12 / Class 1

Figure E-1: CO emissions of class 1 motorcycles in different regions for Euro 3 cycle

Figure E-2: CO emissions of class 1 motorcycles in different regions for WMTC cycle

Figure E-3: Class 1 vehicles, WMTC cycle versus Euro 3 cycle results, CO emissions

Figure E-4: THC emissions of class 1 motorcycles in different regions for Euro 3 cycle

Figure E-5: THC emissions of class 1 motorcycles in different regions for WMTC cycle

Figure E-6: Class 1 vehicles, WMTC cycle versus Euro 3 cycle results, THC emissions

Figure E-7: NOx emissions of class 1 motorcycles in different regions for Euro 3 cycle

Figure E-8: NOx emissions of class 1 motorcycles in different regions for WMTC cycle

Figure E-9: Class 1 vehicles, WMTC cycle versus Euro 3 cycle results, NOx emissions

Figure E-10: CO2 emissions of class 1 motorcycles in different regions for Euro 3 cycle

Figure E-11: CO2 emissions of class 1 motorcycles in different regions for WMTC cycle

Figure E-12: Class 1 vehicles, WMTC cycle versus Euro 3 cycle results, CO2 emissions

ANNEX F - Figures F-13 - F-24 / Class 2 vehicles

Figure F-13: CO emissions of class 2 motorcycles in different regions for Euro 3 cycle

Figure F-14: CO emissions of class 2 motorcycles in different regions for WMTC cycle

Figure F-15: Class 2 vehicles, WMTC cycle versus Euro 3 cycle results, CO emissions

Figure F-16: THC emissions of class 2 motorcycles in different regions for Euro 3 cycle

Figure F-17: THC emissions of class 2 motorcycles in different regions for WMTC cycle

Figure F-18: Class 2 vehicles, WMTC cycle versus Euro 3 cycle results, THC emissions

Figure F-19: NOx emissions of class 2 motorcycles in different regions for Euro 3 cycle

Figure F-20: NOx emissions of class 2 motorcycles in different regions for WMTC cycle

Figure F-21: Class 2 vehicles, WMTC cycle versus Euro 3 cycle results, NOx emissions

Figure F-22: CO2 emissions of class 2 motorcycles in different regions for Euro 3 cycle

Figure F-23: CO2 emissions of class 2 motorcycles in different regions for WMTC cycle

Figure F-24: Class 2 vehicles, WMTC cycle versus Euro 3 cycle results, CO2 emissions

ANNEX G - class wise evaluation

Tables Detailing Class Wise, Region Wise Number of Vehicles

Subjected for Tests

| Step 2 Data ( 2004+ 2007) + (2008) | No. Of vehicles | Total |
| --- | --- | --- |
|  | 2004 | 2007 | 2008 | Number | % |
| All Data | 52 | 62 | 20 | 134 | 100 |
| Class 1 : | 0 | 42 | 5 | 47 | 35.1 |
| Class 2.1 : | 0 | 10 | 6 | 16 | 11.9 |
| Class 2.2 : | 6 | 4 | 3 | 13 | 9.7 |
| Class 3 : | 46 | 6 | 6 | 58 | 43.3 |
| Class 2-1 and class2-2 have only 20% share of the data. |

Table-2:                                                                                         Distribution of vehicles subjected to EURO 3 & WMTC tests

Table 2.1 Class wise

|  | All data | After applying Euro 2 filter |
| --- | --- | --- |
|  | No. of vehicles | % | No. of vehicles | % |
| All Data | 111 | 100 | 59 | 100 |
| Class 1 : | 43 | 38.7 | 26 | 44.1 |
| Class 2.1 : | 10 | 9.0 | 5 | 8.5 |
| Class 2.2 : | 10 | 9.0 | 4 | 6.8 |
| Class 3 : | 48 | 43.2 | 24 | 40.7 |

Table  2. 2:  Region wise (in numbers)

|  | ACEM/JRC | China | India | Japan | US | Total |
| --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  | Number | % |
| All data |
| class 1 | 1 | 26 | 11 | 5 | 0 | 43 | 38.7 |
| class2-1 | 0 | 5 | 3 | 2 | 0 | 10 | 9.0 |
| class2-2 | 3 |  | 3 | 4 | 0 | 10 | 9.0 |
| class 3 | 34 |  | 1 | 7 | 6 | 48 | 43.2 |
| Total | 38 | 31 | 18 | 18 | 6 | 111 | 100 |
| After applying Euro 2 filter |
| class 1 | 1 | 14 | 6 | 5 | 0 | 26 | 43.3 |
| class2-1 | 1 | 1 | 1 | 2 | 0 | 5 | 8.3 |
| class2-2 | 0 | 0 | 1 | 3 | 0 | 4 | 6.7 |
| class 3 | 14 | 0 | 1 | 6 | 4 | 25 | 41.7 |
| Total | 16 | 15 | 9 | 16 | 4 | 60 | 100 |

Analysis combining all the classes will not be influenced by Class 2-1 and class2-2 data, as they have only 18% share of the total data15% of Euro2 filtered data

Table 2.3 Region wise (in % age)

|  | class 1 | class2-1 | class2-2 | class 3 |
| --- | --- | --- | --- | --- |
| All data |
| ACEM/JRC | 2.3 | 0.0 | 30.0 | 70.8 |
| China | 60.5 | 50.0 | 0 | 0 |
| India | 25.6 | 30.0 | 30.0 | 2.1 |
| Japan | 11.6 | 20.0 | 40.0 | 14.6 |
| US | 0 | 0 | 0 | 12.5 |
| Total | 100 | 100 | 100 | 100 |
| After applying Euro 2 filter |
| ACEM/JRC | 3.8 | 20 | 0 | 56 |
| China | 53.8 | 20 | 0 | 0 |
| India | 23.1 | 20 | 25 | 4 |
| Japan | 19.2 | 40 | 75 | 24 |
| US | 0 | 0 | 0 | 16 |
| Total | 100 | 100 | 100 | 100 |
| Class 1 analysis will be heavily influenced by data from China, on which there is still clarity required. Class 2-1- & 2-2 analysis will not be influenced by data from EU Class 3 analysis will be influenced by data from EU |

| Table 3 : Distribution of vehicles Class wise subjected to Japan & WMTC tests |
| --- |
| Step 2 Data ( 2004+ 2007) + (2008) | Total |
|  | Number | % |
| All Data | 48 | (100) |
| Class 1 : | 9 | 18.8 |
| Class 2.1 : | 2 | 4.2 |
| Class 2.2 : | 7 | 14.6 |
| Class 3 : | 30 | 62.5 |

| Table 4 : Distribution of vehicles Class wise subjected to Indian IDC & WMTC tests |
| --- |
| Step 2 Data ( 2004+ 2007) + (2008) | Total |
|  | Number | % |
| All Data | 23 | 100 |
| Class 1 : | 11 | 47.8 |
| Class 2.1 : | 8 | 34.8 |
| Class 2.2 : | 3 | 13.0 |
| Class 3 : | 1 | 4.3 |

Table 5: Distribution of Vehicles Class wise subjected to USA & WMTC Tests

|  | Number | % |
| --- | --- | --- |
| All Data | 19 | 100 |
| Class 1 | 0 | 0 |
| Class 2.1 | 1 | 5.3 |
| Class 2.2 | 4 | 21.1 |
| Class 3 | 14 | 73.7 |

- - - - -

# Comments

Explain what are the data concerned

# Text boxes

0

0