| UNITED NATIONS | E |
| --- | --- |
|  | Economic and Social Council | Distr. GENERAL ECE/TRANS/WP.29/GRRF/2008/3 26 November 2007 Original: ENGLISH ENGLISH AND FRENCH ONLY |

ECONOMIC COMMISSION FOR EUROPE

INLAND TRANSPORT COMMITTEE

World Forum for Harmonization of Vehicle Regulations

Working Party on Brakes and Running Gear

Sixty-third session

Geneva, 4-8 February 2008

Item 3(f) of the provisional agenda

REGULATIONS Nos. 13 and 13-H (Braking)

Alignment of Regulation No. 13 with Regulation No. 13-H

#### Proposal for Corrigendum 1 to Revision 6 to Regulation No. 13

#### Submitted by the expert from Germany (

The text reproduced below was prepared by the expert from the Germany to correct some errors in Regulation No. 13.  It is based on a proposal (informal document No. GRRF-62-27), distributed without an official symbol during the sixty-second session of the Working Party on Brakes and Running Gear (GRRF) (see report ECE/TRANS/WP.29/GRRF/62, para. 22).  The modifications to the current text (Revision 6) of the Regulation are marked in bold characters or as strikethrough.

A.	PROPOSAL

Paragraph 5.2.1.23., correct to read:

"5.2.1.23.	With the exception of vehicles of Category N1, Power-driven vehicles authorized to tow a trailer equipped with an anti-lock system shall …….. "

Paragraph 5.2.1.25.7., correct to read:

"5.2.1.25.7.	For vehicles equipped with an anti-lock device, the anti-lock device shall control the electric regenerative braking system of either category."

B.	JUSTIFICATION

Ad paragraph 5.2.1.23.:

By inserting an derogation for N1 vehicles, there is no requirement to fit an ABS electrical connector to N1 vehicles ,although it is possible to tow, for example, a O3 trailer with a gross vehicle mass (GVM) of 5t, which is required to be fitted with ABS.  This proposal aims at reverting paragraph 5.2.1.23. to the level of Supplement 4 to the 09 series of amendments.

Ad paragraph 5.2.1.25.7.:

The specification "of either category" is not necessary as it is already specified in paragraph 5.2.1.24.3., and is not consistent with paragraph 5.2.1.25.6.

- - - - -

# Footnotes

( In accordance with the programme of work of the Inland Transport Committee for 2006-2010 (ECE/TRANS/166/Add.1, programme activity 02.4), the World Forum will develop, harmonize and update Regulations in order to enhance performance of vehicles.  The present document is submitted in conformity with that mandate.