Proposal for draft amendments to global technical regulation No. 1 (Door locks)

The existing Global Technical Regulation No.1 is document ECE/TRANS/180/Add.1 dated 01 April 2005.

The following documents have made amendment proposals since then:

Document ECE/TRANS/WP.29/2007/40 of 05 April 2007 from the United States

Document ECE/TRANS/WP.29/GRSP/2008/3 of 07 March 2008 from Japan

Document ECE/TRANS/WP.29/GRSP/2008/4 of 03 March 2008 from OICA

Document ECE/TRANS/WP.29/GRSP/2008/20 of 25 September 2008 from EC

On the basis of these proposals together (which contain some repeat amendments) the following are two further amendments which should be considered.

A.	PROPOSAL

Paragraph 5.1.5.1., amend to read:

"5.1.5.1.	Each door hinge system shall:

........

(d) 	On doors which open in a vertical direction, not separate when a vertical load of 9,000 N is applied in the direction of the axis of the hinge pin."

Annex 3, paragraph 2.1.3., amend to read:

"2.1.3.	Vertical load test (applicable only to back doors that open in a vertical direction)."

- - - -