# UN/SCETDG/35/INF.14

COMMITTEE OF EXPERTS ON THE TRANSPORT OF

DANGEROUS GOODS AND ON THE GLOBALLY

HARMONIZED SYSTEM OF CLASSIFICATION

AND LABELLING OF CHEMICALS

# Sub-Committee of Experts on the

# Transport of Dangerous Goods

# Thirty-fifth session

Geneva, 22-26 June 2009

Item 11  of the provisional agenda

OTHER BUSINESS

Criteria to assign packing groups to corrosive substances

# Transmitted by the expert from Spain

Introduction

1.	In order to prepare a document for the next session, the expert from Spain would like to see if there would be support for the proposal contained in this informal document.

2.	Paragraph 2.8.2.5 contains the criteria to assign packing groups to corrosive substances. In order to clarify this text, a table is proposed. This table would be similar to the already existing one in 2.3.2.6, for the hazard grouping based on flammability.

Proposal

3.	Add, after 2.8.2.5, a table explaining what is contained in paragraphs (a), (b) and (c) like follows:

| Packing Group | Exposure time | Observation time | Corrosion rate on steel/aluminium |
| --- | --- | --- | --- |
| I | ≤ 3 min | ≤ 60 min | - |
| II | > 3 min ≤ 60 min | ≤ 14 d | - |
| III | > 60 min ≤ 4 h | ≤ 14 d | > 6.25 mm a year at a test temperature of 55ºC |

______________