# UN/SCETDG/36/INF.58/Add.1

COMMITTEE OF EXPERTS ON THE TRANSPORT OF

DANGEROUS GOODS AND ON THE GLOBALLY

HARMONIZED SYSTEM OF CLASSIFICATION

AND LABELLING OF CHEMICALS

# Sub-Committee of Experts on the

# Transport of Dangerous Goods

# Thirty-sixth session

Geneva, 30 November – 9 December 2009

Item 8 of the provisional agenda

# GLOBAL HARMONIZATION OF TRANSPORT OF DANGEROUS GOODS REGULATIONS WITH THE UN MODEL REGULATIONS

Outcome of DSC 14

Note by the secretariat

Following discussion of INF.30, the secretariat proposes the following additional amendments to the Model Regulations.

1.	Amend TP 37 to read as follows:

“TP 37 Portable tank provision T 14 may continue to be applied until 31 December 2016 except that until that date:

(a)	For UN Nos. 1810, 2474 and 2668, T7 may be applied;

(b)	For UN Nos. 2486, T8 may be applied; and

(c)	For UN Nos. 1838, T10 may be applied.”.

2.	Assign new special provision L3 for UN Nos.2208 and 3486.

Add the following special packing provision L3 in packing instruction LO02

“L3 for UN Nos. 2208 and 3486, transport by sea in large packagings is prohibited”.

3.	In packing instruction P002, add the following at the end of PP85:

“For transport by sea, bags are not allowed as single packagings”.

______________