# UN/SCETDG/36/INF.60

COMMITTEE OF EXPERTS ON THE TRANSPORT OF

DANGEROUS GOODS AND ON THE GLOBALLY

HARMONIZED SYSTEM OF CLASSIFICATION

AND LABELLING OF CHEMICALS

# Sub-Committee of Experts on the

# Transport of Dangerous Goods

# Thirty-sixth session
Geneva, 30 November – 9 December 2009

Item 10 of the provisional agenda

ISSUES RELATING TO THE GLOBALLY HARMONIZED SYSTEM

OF CLASSIFICATION AND LABELLING OF CHEMICALS (GHS)

Criteria to assign packing groups to corrosive substances

Transmitted by the expert from Spain

Introduction

1.	The table on document 2009/28 has been modified so that it includes comments made during the meeting. The word “time” has been changed by “Period” in column 3, “[Alternative Criteria]” has been added to column 4 to clarify its intention and “/” has been substituted by “or”. A new file has been added to the end of the table so that it is clear that in order to be PGIII only one criteria has to be complied with but not both. A name has been given to the table to clarify what it is intended for.

2.	Compiling also the comments made by the ICCA, a proposal 2 is presented as well as an alternative option to the Proposal 1.

Proposal 1

3.	Add, after 2.8.2.5, a table explaining what’s contained in paragraphs (a), (b) and (c) like follows

“Table clarifying the criteria in 2.8.2.5: Hazard grouping based on full thickness destruction of skin tissue

| Packing Group | Exposure Time | Observation Period | Corrosion rate on steel or aluminium [Alternative Criteria] |
| --- | --- | --- | --- |
| I | ≤ 3 min | ≤ 60 min | - |
| II | > 3 min ≤ 1 hour | ≤ 14 day | - |
| III | > 1 hour ≤ 4 h | ≤ 14 day | - |
| III | - | - | > 6.25 mm a year at a test temperature of 55ºC |

Proposal 2

“Table clarifying the criteria in 2.8.2.5

| Packing Group | Exposure Time | Observation Period | Effect |
| --- | --- | --- | --- |
| I | ≤ 3 min | ≤ 60 min | Full thickness destruction of intact skin |
| II | > 3 min ≤ 1 hour | ≤ 14 day | Full thickness destruction of intact skin |
| III | > 1 hour ≤ 4 h | ≤ 14 day | Full thickness destruction of intact skin |
| III [Alternative Criteria] | - | - | > 6.25 mm a year at a test temperature of 55ºC |

__________________