| Transmitted by the expert from OICA | Informal Document No GRRF-65-39 (65th GRRF, 2-6 February 2009 agenda item 3(b)) |
| --- | --- |

Proposal

Electric Regenerative Braking

Agenda 3 b) Documents 2009/2, 2009/14 and 65-10

Actual ECE 13H

5.2.22.4. Electric regenerative braking systems, which produce a retarding force upon release of the throttle pedal, shall not generate a signal mentioned above.

Proposal for ECE 13H

5.2.22.4. Electric regenerative braking systems as defined in paragraph 2.17., which produce a retarding force upon release of the accelerator control, may only generate the signal mentioned above at decelerations above 1.3 m/s². However, if the signal has been generated, the signal shall be de-activated at the latest when the deceleration has fallen below 0.7 m/s².