WP.15/AC.2/16/INF.9

ECONOMIC COMMISSION FOR EUROPE

INLAND TRANSPORT COMMITTEE

Working Party on the Transport of Dangerous Goods

Joint Meeting of Experts on the Regulations annexed to the

European Agreement concerning the International Carriage

of Dangerous Goods by Inland Waterways (ADN)

(ADN Safety Committee)

Sixteenth session

Geneva, 25-29 January 2010

Agenda item 4 (b)

PROPOSALS FOR AMENDMENTS TO THE REGULATIONS ANNEXED TO ADN

Other amendment proposals

Pump rooms below deck

Transmitted by the Government of Germany

Background

1.	At its last session, the ADN Safety Committee adopted an amendment to the provisions concerning pump rooms below deck and to allow for a transitional period until 31 Dec 2044 (see report ECE/TRANS/WP.15/AC.2/32, para. 43).

2.	However, the text for the transitional provision was not included in the annex to the report.

3.	The Government of Germany proposes the addition of a section 1.6.7.5 as follows:

"1.6.7.5	Transitional provisions concerning the transport of gases in tank vessels

Tank vessels in service on 1 January 2011 with a pump room below deck may continue to transport the substances listed in the following table until the renewal of the certificate of approval after 01-01-2045.

| UN-No. or substance identify-cation No. | Class and Classification code | Name and description |
| --- | --- | --- |
| 1005 | 2, 2TC | AMMONIA, ANHYDROUS |
| 1010 1010 1010 | 2, 2F 2, 2F 2, 2F | 1,2-BUTADIENE, STABILIZED 1,3-BUTADIENE, STABILIZED BUTADIENE STABILIZED or BUTADIENES AND HYDROCARBON MIXTURE, STABILIZED, having a vapour pressure at 70 °C not exceeding 1.1 MPa (11 bar) and a density at 50 °C not lower than 0.525 kg/l |
| 1011 | 2, 2F | BUTANE |
| 1012 | 2,2F | 1-BUTYLENE |
| 1020 | 2,2A | CHLOROPENTAFLUOROETHANE (REFRIGERANT GAS R 115) |
| 1030 | 2, 2F | 1,1-DIFLUOROETHANE (REFRIGERANT GAS R 152a) |
| 1033 1040 | 2, 2F 2, 2TF | DIMETHYL ETHER ETHYLENE OXIDE WITH NITROGEN up to a total pressure of 1 MPa (10 bar) at 50 °C |
| 1055 | 2, 2F | ISOBUTYLENE |
| 1063 | 2, 2F | METHYL CHLORIDE (REFRIGERANT GAS R 40) |
| 1077 | 2, 2F | PROPYLENE |
| 1083 | 2, 2F | TRIMETHYLAMINE, ANHYDROUS |
| 1086 | 2, 2F | VINYL CHLORIDE, STABILIZED |
| 1912 | 2, 2F | METHYL CHLORIDE AND METHYLENE CHLORIDE MIXTURE |
| 1965 | 2, 2F | HYDROCARBON GAS MIXTURE, LIQUEFIED, N.O.S., (MIXTURE A) |
| 1965 | 2, 2F | HYDROCARBON GAS MIXTURE, LIQUEFIED, N.O.S., (MIXTURE A0) |
| 1965 | 2, 2F | HYDROCARBON GAS MIXTURE, LIQUEFIED, N.O.S., (MIXTURE A01) |
| 1965 | 2, 2F | HYDROCARBON GAS MIXTURE, LIQUEFIED, N.O.S., (MIXTURE A02) |
| 1965 | 2, 2F | HYDROCARBON GAS MIXTURE, LIQUEFIED, N.O.S., (MIXTURE A1) |
| 1965 | 2, 2F | HYDROCARBON GAS MIXTURE, LIQUEFIED, N.O.S., (MIXTURE B) |
| 1965 | 2, 2F | HYDROCARBON GAS MIXTURE, LIQUEFIED, N.O.S., (MIXTURE B1) |
| 1965 | 2, 2F | HYDROCARBON GAS MIXTURE, LIQUEFIED, N.O.S., (MIXTURE B2) |
| 1965 | 2, 2F | HYDROCARBON GAS MIXTURE, LIQUEFIED, N.O.S., (MIXTURE C) |
| 1969 | 2, 2F | ISOBUTANE |
| 1978 | 2, 2F | PROPANE |
| 9000 | 2, 3TC | AMMONIA, ANHYDROUS, DEEPLY REFRIGERATED |