| UNITED NATIONS |  | E |
| --- | --- | --- |
|  | Economic and Social Council | Distr. GENERAL ECE/TRANS/WP.29/2010/12 18 December 2009 ENGLISH Original: ENGLISH AND FRENCH |

ECONOMIC COMMISSION FOR EUROPE

INLAND TRANSPORT COMMITTEE

World Forum for Harmonization of Vehicle Regulations

# One-hundred-and-fiftieth session

Geneva, 9-12 March 2010

Item 4.2.11 of the provisional agenda

1958 AGREEMENT

Consideration of draft amendments to existing Regulations

Proposal for Corrigendum 5 to the 03 series of amendments to Regulation No. 19

(Front fog lamps)

Submitted by the Working Party on Lighting and Light-Signalling (/

The text reproduced below was adopted by the Working Party on Lighting and Light-Signalling (GRE) at its sixty-second session.  It is based on ECE/TRANS/WP.29/GRE/2009/50, not amended.  It is submitted to the World Forum for Harmonization of Vehicle Regulations (WP.29) and to the Administrative Committee (AC.1) for consideration (ECE/TRANS/WP.29/GRE/62, para. 27).

Paragraph 6.4.3.2., amend to read:

"6.4.3.2. 	At the request of the applicant, two front fog lamps constituting a matched pair corresponding to paragraph 4.2.2.5. may be tested separately. In this case the specified requirements for lines 6, 7, 8, 9 and the Zone D in the table in paragraph 6.4.3. apply to half the sum of readings of the right-hand and left-hand side front fog lamp.  However, in the case of line 6, the two front fog lamps shall each meet at least 50 per cent of the value specified in the table."

- - - - -

# Footnotes

(/ In accordance with the programme of work of the Inland Transport Committee for 2006-2010 (ECE/TRANS/166/Add.1, programme activity 02.4), the World Forum will develop, harmonize and update Regulations in order to enhance performance of vehicles.  The present document is submitted in conformity with that mandate.