|  | United Nations | ECE/TRANS/WP.29/2010/67 |
| --- | --- | --- |
|  | Economic and Social Council | Distr.: General 8 April 2010 English Original: English and French |

Economic Commission for Europe

Inland Transport Committee

World Forum for Harmonization of Vehicle Regulations

One-hundred-and-fifty-first session

Geneva, 22 – 25 June 2010

Item 5.2.1 of the provisional agenda

1998 Agreement (Global) - Consideration and vote of

draft global technical regulations and/or draft

amendments to established global technical regulations

Proposal for Corrigendum 2 to global technical regulation No. 3 (Motorcycle braking)

Submitted by the Working Party on Brakes and Running Gear*

The text reproduced below was adopted by the Working Party on Brakes and Running Gear (GRRF) at its sixty-seventh session in order to correct global technical regulation No. 3 on motorcycle brake systems. It is based on ECE/TRANS/WP.29/GRRF/2010/14, not amended (ECE/TRANS/WP.29/GRRF/67, para. 20). It is submitted to the World Forum for Harmonization of Vehicle Regulations (WP.29) and to the Executive Committee (AC.3) for consideration.

Paragraph 3.3.1., amend to read:

“3.3.1.		MFDD (Mean fully developed deceleration):

Calculation of MFDD:

|  | m/s2 |
| --- | --- |

Where:

dm	= mean fully developed deceleration

Vb	= vehicle speed at 0.8 V1 in km/h

Ve	= vehicle speed at 0.1 V1 in km/h

Sb	= distance travelled between V1 and Vb in metres

Se	= distance travelled between V1 and Ve in metres

V1	= vehicle speed when rider actuates the control”

Paragraph 4.1.1.3., amend to read:

“4.1.1.3.	Measurement of PBC:

The PBC is measured as specified in national or regional legislation using either:

(a)	The American Society for Testing and Materials (ASTM) E1136 – 93 (Reapproved 2003) standard reference test tyre, in accordance with ASTM Method E1337-90 (Reapproved 2002), at a speed of 40 mph; or

(b)	…”

# Footnotes

*	In accordance with the programme of work of the Inland Transport Committee for 2006–2010 (ECE/TRANS/166/Add.1, programme activity 02.4), the World Forum will develop, harmonize and update Regulations in order to enhance the performance of vehicles. The present document is submitted in conformity with that mandate.