Proposal of Corrigendum 1 to Supplement 9 to Regulation No. 113 (Motor vehicle headlamps emitting a symmetrical passing beam or a driving beam or both and equipped with filament lamps)

The modifications to the existing text of the Regulation are marked in bold characters.

I.	Proposal

Paragraph 6.3.3.1.2., amend to read:

“6.3.3.1.2.	........, shall be obtained by the ratio:

IM

I'M = ─── = 0.280 0.208 EM

3

This value shall be .....................”

II.	Justification

Factor 0.208 is correct number as refer to above paragraph and/or other UNECE Lighting Regulations Nos. 98, 112 and 123.

Editorial error “0.208” had been indicated from Supplement 8 of this Regulation.