| Transmitted by the expert from GTB | Informal Document No. GRE-64-16 (64th GRE, 4-7 October 2010, agenda item 18(a)) |
| --- | --- |

Proposal of Supplement 1 to Regulation No.123

(Adaptive front-lighting systems)

This proposal replaces the content of ECE/TRANS/WP.29/GRE/2010/50 where a requirement for a corresponding amendment to the table 1 of annex 4 was omitted.

The modifications to the existing text of the Regulation are marked in bold characters.

I.	Proposal

Annex 3, table 1, amend to read:

"Table 1: Passing beam photometric requirements

|  | Position /deg | passing beam |
| --- | --- | --- |
| tabled requirements expressed in cd | horizontal | vertical | class C | class V | class E | class W |
|  | No | Element | at/ | from | to |  | at |  | min | max | min | max | min | max | min | max |
| Part A | 1 | B50L 4/ | L | 3.43 |  |  | U | 0.57 | 50 4/ | 350 |  | 50 | 350 |  | 50 | 625 | 8/ | 50 | 625 |  |
|  | 2 | HV 4/ | V |  |  |  | H |  | 50 4/ | 625 |  | 50 | 625 |  | 50 |  |  | 50 |  |  |
|  | 3 | BR 4/ | R | 2.5 |  |  | U | 1 | 50 4/ | 1750 |  | 50 | 880 |  | 50 | 1750 |  | 50 | 2650 |  |
|  | 4 | Segment BRR 4/ | R | 8 | R | 20 | U | 0.57 | 50 4/ | 3550 |  |  | 880 |  |  | 3550 |  |  | 5300 |  |
|  | 5 | Segment BLL 4/ | L | 8 | L | 20 | U | 0.57 | 50 4/ | 625 |  |  | 880 |  |  | 880 |  |  | 880 |  |
|  | 6 | P | L | 7 |  |  | H |  | 63 |  |  |  |  |  |  |  |  | 63 |  |  |
|  | 7 | Zone III (as specified by Table 3 of this annex) |  |  |  |  |  |  |  | 625 |  |  | 625 |  |  | 880 |  |  | 880 |  |
|  | 8a | S50, S50LL, S50RR 5/ |  |  |  |  | U | 4 | 63 7/ |  |  |  |  |  | 63 7/ |  |  | 63 7/ |  |  |
|  | 9a | S100, S100LL,S100RR 5/ |  |  |  |  | U | 2 | 125 7/ |  |  |  |  |  | 125 7/ |  |  | 1257/ |  |  |
|  | 10 | 50 R | R | 1.72 |  |  | D | 0.86 |  |  |  | 5100 |  |  |  |  |  |  |  |  |
|  | 11 | 75 R | R | 1.15 |  |  | D | 0.57 | 10100 |  |  |  |  |  | 15200 |  |  | 20300 |  |  |
|  | 12 | 50 V | V |  |  |  | D | 0.86 | 5100 |  |  | 5100 |  |  | 10100 |  |  | 10100 |  |  |
|  | 13 | 50 L | L | 3.43 |  |  | D | 0.86 | 3550 | 13200 | 9/ | 3550 | 13200 | 9/ | 6800 |  |  | 6800 | 26400 | 9/ |
|  | 14 | 25 LL | L | 16 |  |  | D | 1.72 | 1180 |  |  | 845 |  |  | 1180 |  |  | 3400 |  |  |
|  | 15 | 25 RR | R | 11 |  |  | D | 1.72 | 1180 |  |  | 845 |  |  | 1180 |  |  | 3400 |  |  |
|  | 16 | Segment 20 and below it | L | 3.5 | V |  | D | 2 |  |  |  |  |  |  |  |  |  |  | 17600 | 2/ |
|  | 17 | Segment 10 and below it | L | 4.5 | R | 2.0 | D | 4 |  | 12300 | 1/ |  | 12300 | 1/ |  | 12300 | 1/ |  | 7100 | 2/ |
|  | 18 | Emax 3/ |  |  |  |  |  |  | 16900 | 44100 |  | 8400 | 44100 |  | 16900 | 79300 | 8/ | 29530 | 70500 | 2/ |
| Part B (bending modes): Table 1 Part A applies, however with the lines Nos. 1, 2, 7, 13 and 18 being replaced by those listed hereunder |
| Part B | 1 | B50L 4/ | L | 3.43 |  |  | U | 0.57 | 50 4/ | 530 |  |  | 530 |  |  |  |  |  | 790 |  |
|  | 2 | HV 4/ |  |  |  |  |  |  | 50 4/ | 880 |  |  | 880 |  |  |  |  |  |  |  |
|  | 7 | Zone III (as specified by Table 3 of this annex) |  |  |  |  |  |  |  | 880 |  |  | 880 |  |  | 880 |  |  | 880 |  |
|  | 13 | 50L | L | 3.43 |  |  | D | 0.86 | 1700 |  |  | 1700 |  |  | 3400 |  |  | 3400 |  |  |
|  | 18 | Emax 6/ |  |  |  |  |  |  | 10100 | 44100 |  | 5100 | 44100 |  | 10100 | 79300 | 8/ | 20300 | 70500 | 2/ |

Annex 3, table 1, footnote 4, amend to read:

“4	The contribution of each side of the system (for segment BLL and BRR: of at least one point), when measured according to the provisions of Annex 9 to this Regulation shall not be less than 50 cd.”

II.	Justification

1.	During the development of the adaptive front-lighting systems (AFS) regulation, consideration was given to the appearance of vehicles fitted with AFS systems where there was a major difference in the photometric performance from each side of the system. As a result, it was decided to require a minimum value of 75 cd from each side of the system at test points in the glare zone.

2.	Experience with AFS systems, now installed on vehicles, has shown that with practically achievable systems this difference in appearance is not an issue and, in order to avoid imposing stringent testing requirements in the glare zone, it has been concluded that the existing requirements in Regulation No. 123 can be relaxed. Consequently, the existing minimum value of 85 cd has been reduced to 50 cd to provide an acceptable signal to other road users and footnote 4 is only applied to the Class C passing beam. This then also makes it possible for units that are type approved to Regulation No. 98, and performing perfectly satisfactorily in service, to also be installed as part of the AFS system producing the Class C passing beam and the bending light modes.