| Transmitted by the expert from CLEPA | Informal document No. GRE-64-40/Rev.1 (64th GRE, 4–7 October 2010, agenda item 21(k)) |
| --- | --- |

Proposal for Corrigendum 1 to Revision 1 of Regulation No. 104

Addendum 103: Regulation No. 104

Revision 1 – Corrigendum 1

Uniform Provisions Concerning the Approval of Retro-Reflective Markings for Vehicles of Category M,N and O

Note: The text reproduced below was prepared by the expert from CLEPA. The modifications to the current text of Regulation No. 104 - Rev. 1 are marked in bold.

Annex 7, Paragraph1, amend to read:
When illuminated with a CIE Standard illuminant A and measured as recommended
by CIE Publication No. 54, 1982, the coefficient of retro-reflection R` in candelas
per m2 per lux (cd.m-2.lux-1) of the retro-reflective areas in new condition shall be at
least as indicated in table 1 for yellow, white and red materials. and white materials and at least as indicated in table 2 for red materials

Annex 7, Table 1, amend to read:

| Table 1 Minimum values for the Coefficient of Retro-reflection R’ [cd/m²/lx] |
| --- |
| Observation angle  [°] | Entrance Angle  [°] |
|  = 0.33° (20’) | 1 0 0 0 0 0 2 5 20 30 40 60 |
| Colour Yellow White Red | 300 -- 130 75 10 450 -- 200 95 16 120 60 30 10 -- |

Justification:

The photometric specifications for retro-reflective markings of red color have been introduced with supplement 1 to Regulation No. 104. The retro-reflective requirements had been copied from existing requirements in Regulation No. 69 for red material. Photometric specifications were given for the entrance angle  5°, 20°, 30° and 40°. This is not consistent with entrance angles for white and yellow material in Regulation No. 104. During the consolidation of various supplements in Rev. 1 of Regulation No. 104, the photometric specifications have not been correctly transferred.