| Transmitted by the expert from Italy | Informal Document No. GRE-64-43 (64th GRE, 4-7 October 2010, agenda item 8) |
| --- | --- |

# Proposal for Supplement 19 to Regulation No. 7

# in relation to the introduction of requirements for interdependent lamp system.

A	Proposal

# Paragraph 6.1.6, amend to read;

"6.1.6.	When an assembly of two independent lamps to be type approved as “D” lamps having the same function is deemed to be a single lamp, it shall comply with the requirements for:

(a)	Maximum intensity if all lamps together are lit

(b)	Minimum intensity if one lamp has failed."

# Paragraph 6.1.8, amend to read;

6.1.8.	When all light sources are illuminated the maximum intensity specified for a single lamp shall not be exceeded, while, in the case of a lamp marked "D", the maximum intensity specified for the lamp marked "D" shall not be exceeded. may be exceeded provided that the single lamp is not marked "D" and the maximum intensity specified for an assembly of two or more lamps is not exceeded."

B	Justification

-	Paragraph 6.1.6.

We think this paragraph was originally introduced only for the "D" lamp.  To clarify that this paragraph has not to be applied to the interdependent lamp system, we propose to amend it as shown above.

-	Paragraph. 6.1.8.

This amendment does not relate to the proposal of the interdependent lamp system.

The maximum intensity requirement will be amended by R7-02 supplement 16 (WP29/2009/83), which was adopted at 149th WP29 meeting.  In this amendment, the column of “Maximum intensity specified for an assembly of two or more lamps” in the photometric table of Paragraph 6.1 has already disappeared.

The text of this paragraph should be modified accordingly or it could be decided that the whole paragraph is no more necessary and to delete it.