Supplement to the proposal for 04 series of amendments to Regulation No. 10

The text reproduced below was prepared by the experts from France and Germany in order to propose transitional provisions date for application of the proposal of amendment of R 10, 03 revision to extend the scope of the present Regulation to all kinds of power train systems above a certain working voltage level, when they are in charging mode connected to the main, document TRANS-WP29-GRE-2010-54e.

The modifications are strikethrough and the new proposals are marked in bold and underlined.

I.	Content

Modify paragraph 13.1 to 13.4, to read:

“13.1.	As from the official date of entry into force of the 03 series of amendments, no Contracting Party applying this Regulation shall refuse to grant ECE approval under this Regulation as amended by the 03 series of amendments.

13.2.	As from 12 months after the date of entry into force of this Regulation, as amended by the 03 series of amendments, Contracting Parties applying this Regulation shall grant approvals only if the vehicle type, component or separate technical unit to be approved meets the requirements of this Regulation as amended by the 03 series of amendments.

13.3 Contracting Parties applying this Regulation shall not refuse to grant extensions of approval to the preceding series of amendments to this Regulation

13.4.	Starting 48 months after the entry into force of the 03 series of amendments to this Regulation, Contracting Parties applying this Regulation may refuse first national registration (first entry into service) of a vehicle, component or separate technical unit which does not meet the requirements of the 03 series of amendments to this Regulation.

13.5.	As from  [ ….] months after the official date of entry into force of this Regulation, as amended by the  04 series of amendments, Contracting Parties applying this Regulation shall grant approvals only if the vehicle type, to be approved meets the requirements of this Regulation as amended by the  04 series of amendments.

13.6.	Until 48 months after the date of entry into force of the 04 series of amendments, no Contracting Parties shall refuse national or regional approval of a vehicle approved to the preceding series of amendments to this Regulation.

13.7.	as from […date ..], Contracting Parties may refuse first registration of a new vehicle which does not meet the requirements of the 04 series of amendments to this Regulation.

13. 8.	Notwithstanding paragraphs 13.6 and 13.7 approvals of vehicle granted to the preceding series of amendments to the Regulation, which are not affected by the 04 series of amendments, shall remain valid and Contracting Parties applying the Regulation shall continue to accept them.